## Slide 1: AQWATCH preparation: First insights of NO2 pollution over Mexico City with TROPOMI
PETETIN Hervé
AC group meeting
25/02/2020

## Slide 2: AQ-WATCH

## Slide 3: AQ-WATCH
Started in January 2020
Coordinated by MPI (Hamburg), involving 12 partners
General objective of AQ-WATCH : Develop a supply chain leading to the generation of several innovative downstream AQ products and services
[WP2, task 2.5]
  Objective : estimate surface pollutant concentrations and derive AQ indices using machine learning algorithms, satellite observations (e.g. TROPOMI) among other dataset (e.g. Copernicus, ECMWF)
  Application to NO2 and aerosols.
https://earth.bsc.es/wiki/doku.php?id=projects:aqwatch

## Slide 4: General information on TROPOMI

## Slide 5: TROPOMI
Sentinel-5 Precursor (LEO) : fill the gap between the current records from OMI (NASA EOS Aura) and SCIAMACHY (ESA Envisat) and the operational Sentinel-4/5 missions
Notes: (which cannot be donne by GOME-2 and IASI instruments on MetOp because of limited spatial resolution and lack of CH4 and CO measurements with good sensitivity down to the Earth’s surface)

## Slide 6: TROPOMI versus OMI
Optical chanel | Spectral range (um) | Nadir pixel size (km2) | Max S/N ratio
UV | 270-314 | 36x48 | 750
UVIS | 306-500 | 13x24 | 1000
Optical chanel | Spectral range (um) | Nadir pixel size (km2) | Max S/N ratio
UV | 267-332 | 7x28 | 1000
UVIS | 303-499 | 7x3.5 | 1500
NIR | 675-775 | 7x3.5 | 500
SWIR | 2305-2385 | 7x7 | 100
TROPOMI combines the strengths of SCIMACHY, OMI and state of the art technologies
Major improvement of spatial/temporal resolution, spectral resolution, sensitivity
OMI
TROPOMI
Global daily coverage at 13h30 LST
Statistics on (lon-lat) spatial resolution calculated over one orbit :
  Mean : 6.1±2.7 x 5.6±0.1 km2 (area = 34 km2)
  Min : 3.6 x 5.2 km2 (20 km2)
  Max : 15.1 x 5.6 km2 (84 km2)
  p50 : 5.0 x 5.6 km2 (28 km2)

## Slide 7: TROPOMI NO2 at Mexico City

## Slide 8: Day-to-day variability
TROPOMI L2 products merged and regridded at 3 km resolution, here for several days in january :

## Slide 9: Annual average in 2019
Many cells within Mexico City and generally only one surface station per cell  Strong potential for investigation intra-urban variability in large megacities like Mexico City

## Slide 10: Orography and land cover
Complex orography with mountains at west/south and volcano at east (Popocatépetl)
Crops represents 50% of the land cover in many areas around the cities (and moutains)
(from Copernicus Land Monitoring Service )

## Slide 11: Cloud fraction
Relatively mean low cloud radiance fraction (CRF) in Mexico City area. Highest value of CRF close to Popocatépetl (not only cloud but also eruption plumes?)
(p95)
(mean)

## Slide 12: Meteorology
ERA5 meteorology quite coarse (about 30 km) at the megacity scale
Maybe poor quality in an area of such complex orography

## Slide 13: Mean versus extreme values
(p05)
(p95)
(mean)
Around the city center of Mexico City :
Mean NO2 tropospheric column of about : 18e15 molec/cm2
5th percentile : 5e15 molec/cm2
95th percentile : 40e15 molec/cm2

## Slide 14: Weekdays and weekends
NO2 tropospheric columns about 1.3 higher during weekdays than during weekends
Surprisingly, highest ratio (about 1.9) is in north-west of Mexico City
(ratio)
(weekdays)
(weekends)

## Slide 15: Weekdays and weekends
Weekdays-over-weekend ratio quite consistent with surface observations (colocated in time with TROPOMI)

## Slide 16: Weekdays and weekends
Focusing on shorter periods, the spatial pattern of the ratio can be strongly accentuated
Here for January : much higher ratio in north-west part (but less days taken into account, so representativeness maybe deteriorated...)
(ratio)
(weekdays)
(weekends)

## Slide 17: Monthly variability
Very strong seasonal variability
(NB : data gaps maybe partly to TROPOMI netcdf still missing on esarchive)

## Slide 18: Mexico versus Santiago de Chile
Mean annual NO2 tropospheric columns in 2019 are comparable in the city center of both cities

## Slide 19: Surface versus columns at Mexico City
Surface NO2 concentrations are quite well correlated with NO2 columns observed from space, especially when considering larger temporal scales

## Slide 20: Inference of surface NO2 concentrations
Features
Predictions with surface concentrations
Target :
Machine learning