## Slide 1
Barcelona, 4th November 2015
CIUDADES COMO CENTROS DE MODELIZACIÓN CIENTÍFICA
Jornada sobre Biosfera y Ciudades
Albert Soret Miravet
Earth Sciences Department at BSC

## Slide 2: Objective and outline
Objective: to introduce air quality and climate modelling systems to explore their potential applications at urban scales.
Outline:
Introduction to:
  BSC activities
Air quality
  Urban areas
    Air quality in Europe
    Case studies
Climate change
  Exposure and vulnerability of urban areas
  Case studies
Future work
Conclusions
Notes: També podem treballar a totes les escales temporals. L’anàlisi diagnòstic d’esdeveniments passats, els pronòstics per als propers dies, les projeccions a molts anys vista i el terme mitg, les prediccions que van des de setmanes i mesos fins a dècades.
On som forts i el que ens fa destacar son dos casos concrets que molt pocs altres centres treballen i que estan fortament lligats tant a l’energia solar com a l’energia eòlica.
D’una banda som líders en temes de modelització de la pols a l’atmòsfera que és un tema crític per a zones àrides, semiàrides i zones adjacents (Àfrica, Sud d’Espanya i Orient Mitjà) i cabdal per a la gestió de l’energia solar.
D’altra banda les prediccions climàtiques (seasonal to decadal) són un tema molt nou que tot just es comença a treballar a nivell mundial i en el que només el nostre centre i la Met Office de Regne Unit estem fent coses i en molts casos col·laborant i en contacte constant amb el sector de l’energia eòlica.
A continuació us explicaré aquest dos punts amb una mica més de detall.

## Slide 3: Introduction

## Slide 4: Barcelona Supercomputing Center
Created in 2005; 350 employees
Research, develop and manage information technology
Facilitate scientific progress and its application in society
Earth Science Department
Atmospheric composition modelling
Climate prediction modelling
Computational Earth Sciences
Earth Sciences Services

## Slide 5: Earth sciences modelling: climate and air quality modelling
Towards modelling the Earth system
Notes: Aquests models els podem aplicar a múltiples escales espaials, des de la més global fins a centrar-nos només en una ciutat.

## Slide 6: Spatial scales
Multi-scale models from
global to local scales
Multiscale Models from Global to Local Scales
Notes: Aquests models els podem aplicar a múltiples escales espaials, des de la més global fins a centrar-nos només en una ciutat.

## Slide 7: Temporal scales
Today
Hours
Days
Weeks
Months
Seasons
Years
Decades
Past
Century
FORECAST
PREDICTION
PROJECTION
DIAGNOSTIC
Mineral Dust
Air quality
Meteorology
Climate predictions
Climate projections
Climate projections
Climate predictions
Notes: També podem treballar a totes les escales temporals. L’anàlisi diagnòstic d’esdeveniments passats, els pronòstics per als propers dies, les projeccions a molts anys vista i el terme mitg, les prediccions que van des de setmanes i mesos fins a dècades.
On som forts i el que ens fa destacar son dos casos concrets que molt pocs altres centres treballen i que estan fortament lligats tant a l’energia solar com a l’energia eòlica.
D’una banda som líders en temes de modelització de la pols a l’atmòsfera que és un tema crític per a zones àrides, semiàrides i zones adjacents (Àfrica, Sud d’Espanya i Orient Mitjà) i cabdal per a la gestió de l’energia solar.
D’altra banda les prediccions climàtiques (seasonal to decadal) són un tema molt nou que tot just es comença a treballar a nivell mundial i en el que només el nostre centre i la Met Office de Regne Unit estem fent coses i en molts casos col·laborant i en contacte constant amb el sector de l’energia eòlica.
A continuació us explicaré aquest dos punts amb una mica més de detall.

## Slide 8: Air quality and climate modelling systems in urban areas. Framework at BSC
Road transport:
e.g. the use of cleaner fuels and technologies. Fleet electrification.
Industrial emissions
Port emissions, etc.
Air quality diagnostic studies:
the case of Santa Cruz de Tenerife
Air quality forecast system: CALIOPE
Air quality management measures
Air quality modelling systems
Climate modelling systems
Climate prediction systems
Climate projection systems
Downscaling techniques

## Slide 9: Air quality

## Slide 10: Air pollution in urban areas
Beijing
Barcelona
Madrid
Istanbul
Mexico DF
Santiago de Chile
OMI tropospheric NO2 vertical column densities, 2005 average (1015 molecules/cm2) (Wenig et al., 2008).

## Slide 11: Air pollution and urban areas: causes
Plaça Espanya, Barcelona (1908)
Plaça Espanya, Barcelona (2014)
C/ Gran de Gràcia, Barcelona (1908)
C/ Gran de Gràcia, Barcelona (2014)

## Slide 12: Air pollution in Europe
Mean annual PM10 concentration
Mean annual NO2 concentration
Mean annual SO2 concentration
Highest daily running 8h running maximums O3
Year 2011
Source: EEA, 2013

## Slide 13: Methodology: air quality modelling system
Air quality modelling system:
Meteorological model (e.g. WRF-ARW)
Emission model (e.g. HERMES)
Air quality model (e.g CMAQ)
Others: mineral dust model (e.g NMMB/BSC-Dust), ocen and wave models, etc.
Configuration:
High spatial (1x1 km2) and temporal resolution (1h)
HERMES: Bottom-up emission model for Spain 1x1 km2 and a temporal resolution of 1 h
Baldasano et al., 2008; Guevara et al, 2013

## Slide 14: Air quality and climate modelling systems in urban areas. Framework at BSC
Road transport:
e.g. the use of cleaner fuels and technologies. Fleet electrification.
Industrial emissions
Port emissions, etc.
Air quality diagnostic studies:
the case of Santa Cruz de Tenerife
Air quality forecast system: CALIOPE
Air quality management measures
Air quality modelling systems
Climate modelling systems
Climate prediction systems
Climate projection systems
Downscaling techniques

## Slide 15: Santa Cruz de Tenerife, atmospheric dynamics
Annual mean concentration of SO2 in 2011
Dust storm over Canary Islands
Source: Terra-MODIS
Singular characteristics of Santa Cruz de Tenerife:
The interaction between the complex topography of the island of Tenerife (3718m) and trade winds.
Breezes cycles due to the coastal location.
Thermal inversion at relatively low altitudes that hinders convective motions.

## Slide 16: Measured air quality concentration. SO2.
Chart: Hourly SO2 concentration (ug/m3) April 6, 2011
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Casa Cuna | 3 | 5 | 3 | 3 | 8 | 12 | 20 | 21 | 14 | 26 | 13 | 16 | 18 | 15 | 7 | 7 | 8 | 7 | 6 | 8 | 6 | 7 | 5 | 6
Merca Tenerife | 11 | 6 | 10 | 12 | 7 | 8 | 13 | 5 | 14 | 9 | 15 | 14 | 3 | 7 | 7 | 8 | 6 | 10 | 7 | 9 | 5 | 9 | 11 | 7
Refineria | 2 | 2 | 2 | 2 | 7 | 8 | 8 | 78 | 159 | 161 | 333 | 85 | 114 | 68 | 12 | 5 | 3 | 2 | 2 | 2 | 2 | 3 | 2 | 3
Vuelta Los Pájaros-Sta Cruz TF | 7 | 8 | 5 | 5 | 13 | 5 | 13 | 16 | 14 | 7 | 60 | 25 | 16 | 54 | 15 | 8 | 5 | 7 | 4 | 6 | 11 | 5 | 8 | 5
Depósito de Tristán-Sta Cruz TF | 4 | 4 | 4 | 4 | 6 | 6 | 7 | 6 | 6 | 7 | 11 | 46 | 39 | 28 | 7 | 4 | 5 | 5 | 4 | 6 | 5 | 4 | 5 | 4
Los Gladiolos | 11 | 10 | 12 | 12 | 17 | 62 | 85 | 0 | 0 | 22 | 25 | 32 | 21 | 29 | 92 | 21 | 16 | 14 | 12 | 12 | 12 | 11 | 11 | 11
Tome Cano | 34 | 34 | 34 | 35 | 33 | 36 | 35 | 35 | 37 | 40 | 41 | 40 | 40 | 40 | 239 | 1241 | 671 | 152 | 231 | 142 | 210 | 175 | 121 | 67
Tena Artigas-Sta Cruz de TF | 6 | 6 | 6 | 7 | 8 | 10 | 11 | 10 | 15 | 25 | 21 | 60 | 44 | 14 | 10 | 9 | 6 | 7 | 8 | 7 | 6 | 6 | 7 | 7
Piscina Municipal-Sta Cruz TF | 5 | 4 | 6 | 6 | 7 | 5 | 8 | 7 | 8 | 10 | 11 | 7 | 7 | 7 | 423 | 543 | 198 | 148 | 74 | 60 | 56 | 28 | 21 | 17
VL hora 350 (24) | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350 | 350
VL día 125 (3) | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125
1325 µg m-3
Refinery

## Slide 17: Results. Air quality levels. The impact of the refinery
0 UTC
01 UTC
02 UTC
03 UTC
04 UTC
05 UTC
06 UTC
07 UTC
08 UTC
09 UTC
10 UTC
11 UTC
12 UTC
13 UTC
14 UTC
15 UTC
16 UTC
17 UTC
18 UTC
19 UTC
20 UTC
21 UTC
22 UTC
23 UTC
Obs. Data
Wind rose at 10m
West (24th January 2011)
WRF-ARW (1 x 1 km2)

## Slide 18: Air quality results. Primary area of influence of the refinery
Maximum hourly SO2 concentration for the Jannuary, 24th 2014
Chart: Maximum hourly increases of SO2 due to the emission from the Tenerife refinery against distance to the refinery
(Baldasano et al., 2014)

## Slide 19: Air quality and climate modelling systems in urban areas. Framework at BSC
Road transport:
e.g. the use of cleaner fuels and technologies. Fleet electrification.
Industrial emissions
Port emissions, etc.
Air quality diagnostic studies:
the case of Santa Cruz de Tenerife
Air quality forecast system: CALIOPE
Air quality management measures
Air quality modelling systems
Climate modelling systems
Climate prediction systems
Climate projection systems
Downscaling techniques

## Slide 20: CALIOPE air quality operational forecasts
Information is delivered using both online or custom applications:
www.bsc.es/caliope
Provides air quality related information for the coming days and for the application of short term action plans for air quality managers.

## Slide 21: Air quality and climate modelling systems in urban areas. Framework at BSC
Road transport:
e.g. the use of cleaner fuels and technologies. Fleet electrification.
Industrial emissions
Port emissions, etc.
Air quality diagnostic studies:
the case of Santa Cruz de Tenerife
Air quality forecast system: CALIOPE
Air quality management measures
Air quality modelling systems
Climate modelling systems
Climate prediction systems
Climate projection systems
Downscaling techniques

## Slide 22: Fleet electrification
Hybrid electric vehicles (HEV)
Plug-in electric vehicle (PHEV)
Battery electric vehicle (BEV)
e.g. BMW i3
e.g. Piaggio MP3 Hybrid 300
e.g. Van Hool Exquicity
Fleet electrification: Replacement of internal combustion vehicles by electric vehicles

## Slide 23: Fleet electrification. Air quality impacts
NO2 maxh reductions:
25 - 30 µg m-3
8-16%
PM10 maxh reductions:
< 8 µg m-3
2-5%
NO2 maxh reductions:
30 - 35 µg m-3
8-16%
PM10 maxh reductions:
< 6 µg m-3
2-4%
(Soret et al., 2014)

## Slide 24: Climate

## Slide 25: Climate change. Exposure and vulnerability of urban areas
Exposure and vulnerability are dynamic, varying across temporal and spatial scales, and depend on economic, social, geographic, demographic, cultural, institutional, governance, and environmental factors.
Rapid urbanization and the growth of megacities, especially in developing countries,
have led to the emergence of highly vulnerable urban communities.
For example, coastal cities, including cities in small islands and megadeltas, are exposed and vulnerable to climate extremes in both developed and developing countries.
The ten largest urban megacities. Urban population trends
(UN, 2014)

## Slide 26: Coastal megacities: The case of Mumbai
At present, Mumbai is the city with the largest population exposed to coastal flooding.
In July 2005, Mumbai, India, was struck by an exceptional storm. In one 24-hour span alone, the city received 94 cm of rain, and the storm left more than 1,000 dead, mostly in slum settlements.
Attributing causes of changes in monsoons is difficult due to substantial differences between models, and the observed maximum rainfall on India’s west coast, where Mumbai is located, is poorly simulated by many models. (IPCC, 2012)

## Slide 27: Heat waves
Global climate change is likely to be accompanied by an increase in the frequency and intensity of heat waves, as well as warmer summers.
Heat waves have a much bigger health impact in cities than in surrounding suburban and rural areas. Urban areas typically experience higher—and nocturnally sustained—temperatures because of the "heat island" effect.
Difference in average temperature (2000, 2001, 2002 and 2004) from 2003, covering the date range of 20 July – 20 August
Source: (MODIS) on NASA’s Terra satellite

## Slide 28: Air quality and climate modelling systems in urban areas. Framework at BSC
Road transport:
e.g. the use of cleaner fuels and technologies. Fleet electrification.
Industrial emissions
Port emissions, etc.
Air quality diagnostic studies:
the case of Santa Cruz de Tenerife
Air quality forecast system: CALIOPE
Air quality management measures
Air quality modelling systems
Climate modelling systems
Climate prediction systems
Climate projection systems
Downscaling techniques

## Slide 29: Climate prediction and projection systems
The interactions between the various components of the system play a crucial role in the dynamics of climate. E.g. EC-EARTH modelling system:
  IFS: representing the atmosphere
  NEMO: representing the ocean
  LIM: representing the sea-ice
  HTESSEL: representing the continental surfaces and vegetation
  TM5: representing the atmospheric chemistry
Today
Hours
Days
Weeks
Months
Seasons
Years
Decades
Past
Century
FORECAST
PREDICTION
PROJECTION
DIAGNOSTIC
Climate predictions
Climate projections
Climate projections
Climate predictions

## Slide 30: Climate prediction and projection systems. Spatial resolution
Climate modelling: resolution of the climate models used in the IPCC
1990
1996
2001
2007

## Slide 31: Climate prediction and projection systems. Spatial resolution
(IPCC, 2013)

## Slide 32: Downscaling techniques
Dynamical downscaling of climatic temperature and precipitation trends. This work aims to provide an assessment of temperature and precipitation projections for mid-21st century in the North Western Mediterranean Basin (NWMB) at high resolution.
Global models Regional models
Climatological mean from the WRF-EH5OMs1 and s3 simulations for 1971–2000 and projected changes for 2021–2050 as derived from WRF-EH5OMs1 and s3 according to B1, A1B and A2 scenarios for the tropical nights number.
(Barrera-Escoda et al., 2013)

## Slide 33: Downscaling techniques
Dynamical downscaling of climatic temperature and precipitation trends. This work aims to provide an assessment of temperature and precipitation projections for mid-21st century in the North Western Mediterranean Basin (NWMB) at high resolution.
Global models Regional models
Climatological mean from the WRF-EH5OMs1 and s3 simulations for 1971–2000 and projected changes for 2021–2050 as derived from WRF-EH5OMs1 and s3 according to B1, A1B and A2 scenarios for the contribution of very wet days to total precipitation amount.
(Barrera-Escoda et al., 2013)

## Slide 34: Future work

## Slide 35: Further understanding of urban processes.
Further understanding of local scales processes to allow the assessment of sustainable management of urban areas within the SmartCities context by using two key-elements:
microscale atmospheric models
observations from smart infrastructures
From global to regional scales
Next step: microscale
Notes: Nowadays the majority of urban areas around the world have air quality related problems in both developed and developing countries.

## Slide 36: Air quality assessment at urban scales. Strategy: interdisciplinar approach
Meteorological core
Emission module
Air quality module
Smart infrastructures
CDF air quality at microscale
CASE dep. + Earth Sciences dep. + Computer dep.

## Slide 37: Conclusions

## Slide 38: Conclusions
Air quality and climate model systems are an important tool to understand and analyze earth system processes.
Air quality modelling allow relating emission sources and meteorological processes with changes in air quality levels.
Air quality modelling can be applied in diagnostic studios, air quality forecast systems and air quality management plans.
Air quality modelling systems: their spatial resolution (up to 1x1 km2) and configuration (e.g. urban land use categories within the meteorological models) allow for assessing air quality related impacts in urban areas.
Climate modelling systems have difficulties to resolve urban related processes.

## Slide 39
Thank you!
For further information please contact
albert.soret@bsc.es
Satellite view of Earth at night. 1-4% of land surface is urban.
More than 50% of world’s population lives in urban areas.
Source: NASA

## Slide 40: Mobility management
Chart: Traffic growth in Europe
| 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
 | 1135402.8999 | 1195569.5345 | 1259333.0478 | 1328374.7304 | 1394245.162 | 1457237.325 | 1518908.3382 | 1580287.8598 | 1641563.1014 | 1702324.96 | 1763269.5699 | 1823474.0919 | 1879735.5679 | 1933848.5144 | 1986556.7842 | 2040566.2153 | 2094286.6958 | 2149498.2917 | 2204082.1353 | 2265144.2883 | 2324623.3709 | 2390064.544 | 2452885.3624 | 2516635.571 | 2584317.3846 | 2642989.2606 | 2699702.5501 | 2754713.4887 | 2811279.7765 | 2867146.2884 | 2922398.7075 | 2975944.3681 | 3029374.4616 | 3082328.3503 | 3134946.7146 | 3187279.5628 | 3236759.2804 | 3286177.2864 | 3335654.6083 | 3385313.9446 | 3435114.8922 | 3481223.7171 | 3526926.1727 | 3572027.4851 | 3616567.1408 | 3660452.856 | 3701138.6591 | 3741124.4565 | 3780512.4106 | 3819445.9622 | 3857991.688
Source: EIONET, 2003
Implementation of Superblocks in Barcelona
Source: BCNEcologia

## Slide 41: Emission trends
Chart: Emission trends in Spain
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
NOx | 1340.9586 | 1390.0892 | 1430.7654 | 1399.0313 | 1423.7035 | 1412.3448 | 1370.1829 | 1361.0746 | 1347.5246 | 1384.9692 | 1397.6625 | 1359.831 | 1401.4402 | 1401.8862 | 1436.6861 | 1421.0692 | 1366.7757 | 1355.4516 | 1167.3345 | 1032.9443 | 954.9723 | 949.472 | 920.5346
SOx | 2169.8141 | 2192.6013 | 2157.624 | 2027.9082 | 1987.0972 | 1854.7006 | 1628.9461 | 1766.0917 | 1607.4536 | 1606.7772 | 1495.8371 | 1444.949 | 1571.5433 | 1306.5296 | 1333.1845 | 1278.1495 | 1166.7426 | 1135.0408 | 511.9959 | 459.2722 | 424.2821 | 458.9353 | 407.5169
CO | 3660.2699 | 3729.0282 | 3738.3419 | 3574.6684 | 3460.198 | 3163.6301 | 3202.6403 | 3087.6386 | 2989.8189 | 2822.8289 | 2703.565 | 2636.7415 | 2385.1232 | 2448.8136 | 2315.4261 | 2140.4371 | 2119.0167 | 2110.2875 | 1994.3241 | 1927.0021 | 2000.4834 | 1987.0404 | 1924.4942
NMVOC | 1054.6503 | 1068.8068 | 1071.1613 | 992.2268 | 1008.9477 | 976.8735 | 1010.6636 | 1014.6068 | 1043.5008 | 1025.479 | 994.151 | 964.3918 | 897.024 | 898.6232 | 873.8567 | 829.8836 | 798.4148 | 779.9188 | 713.4945 | 653.9674 | 648.6528 | 618.9922 | 598.2186
NH3 | 335.3758 | 328.3748 | 325.4397 | 302.3502 | 328.0903 | 317.4699 | 351.0159 | 352.8461 | 367.5714 | 382.2741 | 400.3863 | 401.5523 | 394.9752 | 412.6347 | 400.712 | 379.3193 | 396.9104 | 400.8276 | 369.5991 | 378.413 | 390.8976 | 380.6225 | 379.9158
PM10 | 145.896 | 145.253 | 144.4944 | 143.9304 | 143.6009 | 143.0343 | 142.4171 | 142.2243 | 141.6553 | 140.9167 | 140.8916 | 138.0103 | 140.6228 | 139.9245 | 136.9131 | 134.4048 | 130.4667 | 129.9362 | 115.3832 | 111.8688 | 107.6165 | 106.4595 | 102.2083
PM2.5 | 106.5142 | 105.6104 | 104.6 | 103.7576 | 103.1199 | 102.2789 | 101.3595 | 100.8465 | 99.9219 | 98.8863 | 98.3193 | 96.0726 | 96.653 | 97.4534 | 94.9118 | 93.6218 | 91.5296 | 91.0665 | 82.3064 | 81.0351 | 76.7538 | 75.0954 | 71.983
Source: EEA, 2013
% of urban population exposed to air pollution
exceeding EU air quality standards
Emission have dropped considerably but air quality still needs to improve
A significant proportion of urban population is exposed to air quality concentrations exceeding EU air quality standards
Chart: Emission trends in Europe (EU-28)
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
NOx | 17358.1479 | 16901.8651 | 16436.3956 | 15764.4017 | 15090.2267 | 14707.0058 | 14493.176 | 13947.158 | 13555.7851 | 13097.109 | 12702.4463 | 12463.9774 | 12208.6714 | 12111.8823 | 11949.4887 | 11610.9861 | 11296.2204 | 10940.1575 | 10133.0144 | 9274.5427 | 9116.495 | 8774.6312 | 8478.627
SOx | 25835.0336 | 23587.0165 | 21605.9886 | 20338.3569 | 18782.533 | 16765.7897 | 15530.1144 | 14453.0367 | 12838.198 | 11193.6964 | 10102.6707 | 9669.1167 | 9129.0918 | 8708.2902 | 8170.8768 | 7732.9917 | 7529.2871 | 7187.8457 | 5573.2825 | 4768.8251 | 4484.3036 | 4433.5798 | 4005.4319
CO | 66406.6428 | 64144.631 | 60720.8756 | 60274.1572 | 53474.0349 | 49799.2242 | 48803.6858 | 46463.6897 | 44032.6961 | 41435.2144 | 38095.7739 | 36530.9749 | 34283.6876 | 33182.1658 | 32300.2501 | 29833.0463 | 28345.0115 | 27055.4763 | 26113.1672 | 23755.1299 | 24906.9564 | 23143.9634 | 22401.2503
NMVOC | 16852.7898 | 16084.0758 | 15386.1386 | 14780.826 | 13710.4951 | 13087.5452 | 12937.9788 | 12551.5618 | 12071.1109 | 11427.7102 | 10667.5556 | 10196.5709 | 9713.939 | 9370.1434 | 9095.9584 | 8800.4433 | 8566.7852 | 8182.6082 | 7803.0211 | 7179.5929 | 7215.523 | 6904.2455 | 6707.4224
NH3 | 5102.972 | 4842.6071 | 4598.1219 | 4380.8316 | 4302.0347 | 4170.9011 | 4178.0649 | 4193.357 | 4161.5365 | 4170.2692 | 4102.1256 | 4041.7519 | 3986.1553 | 3984.257 | 3936.6252 | 3881.3795 | 3885.865 | 3896.8068 | 3811.4113 | 3775.669 | 3712.2873 | 3723.9092 | 3667.5806
PM10 | 3194.4565 | 3171.4626 | 3079.4055 | 3036.2232 | 2901.7061 | 2698.5717 | 2662.2211 | 2529.1065 | 2379.4138 | 2334.5054 | 2260.144 | 2253.1411 | 2160.3263 | 2144.6349 | 2128.343 | 2075.8356 | 2034.9002 | 2001.3298 | 1942.7522 | 1851.5165 | 1923.452 | 1850.2351 | 1834.5134
PM2.5 | 1911.1546 | 1928.7256 | 1879.7051 | 1833.9645 | 1770.8153 | 1730.9641 | 1732.1362 | 1676.6764 | 1624.5908 | 1582.5158 | 1542.3111 | 1542.6734 | 1488.3288 | 1482.0557 | 1461.1732 | 1417.1151 | 1378.3464 | 1345.083 | 1321.0277 | 1267.6482 | 1311.7001 | 1246.1307 | 1242.3135

## Slide 42: Air quality in Europe
Mean annual PM10 concentration
Mean annual NO2 concentration
Mean annual SO2 concentration
Highest daily running 8h running maximums O3
Year 2011
Source: EEA, 2013

## Slide 43: Emission factors. Diesel and gasoline
Chart: NOx PC Gasoline and Diesel
Chart: PM- PC Gasoline and Diesel
The Mayor of Paris has announced radical plans to ban diesel cars from the French capital by 2020 due to concerns about how much pollution the cars cause (France has the highest number of diesel cars in Europe). And the Mayor of London is also considering similar solutions.
She also said that the city would have more semi-pedestrianised areas with special zones introduced at weekends.

## Slide 44: Improvements for the road transport emissions
EF NOx - Euro 5 diesel PC
AB (2010)
Kouridis et al. (2013)
Remote Sensign Device
Portable Emission Measurement System

## Slide 45: Air quality and climate change. Emissions
GHG: CO2eq
Atmospheric pollutants: NO2, etc.
Global impact: Climate Change
Local-regional impact: air quality
Measures to reduce emissions

## Slide 46: Air quality and climate change. Measures to reduce emissions
Beneficial for AQ
Beneficial
for CC
Negative for AQ
Negative
for CC
Fuel gas desulphurisation
Three-way catalyst (petrol)
Particulate filters (diesel)
Air quality (AQ) and climate change (CC) synergies and trade-offs
Energy demand for coal and oil fossil fuels in stationary and mobile sources
Energy renewables
Nuclear
Demand management
Hybrids…
Some conventional biofuels
Biomass
Combined heat and power
Buying carbon credits
(Source: adapted form Drefra, 2010)
Beneficial for
AQ and CC
Negative for
AQ and CC

## Slide 47: Areas of study: Barcelona and Madrid
Combined-cycle
Meteorological
station
Meteorological
station
Chart: Vehicular fleet Madrid
| Gasoline PC < 1.4 L | Gasoline PC - EURO I < 1.4 L | Gasoline PC - EURO II < 1.4 L | Gasoline PC - EURO III < 1.4 L | Gasoline PC - EURO IV < 1.4 L | Gasoline PC - ECE 15-04 1.4-2.0 L | Gasoline PC - EURO I 1.4-2.0 L | Gasoline PC - EURO II 1.4-2.0 L | Gasoline PC - EURO III 1.4-2.0 L | Gasoline PC - EURO IV 1.4-2.0 L | Gasoline PC - EURO III > 2.0 L | Gasoline PC - EURO IV > 2.0 L | Diesel PC - EURO I < 2.0 L | Diesel PC - EURO II < 2.0 L | Diesel PC - EURO III < 2.0 L | Diesel PC - EURO IV < 2.0 L | Diesel PC - EURO III > 2.0 L | Electric mode PC | Hybrid mode PC | GasolineLDV - EURO IV < 3.5 t | Diesel LDV- Conventional < 3.5 t | Diesel LDV- EURO I < 3.5 t | Diesel LDV- EURO II < 3.5 t | Diesel LDV- EURO III< 3.5 t | Diesel LDV- EURO IV < 3.5 t | Electric mode LDV | Hybrid mode LDV | Diesel HDV- Conventional rígid <= 7.5 t | Diesel HDV- EURO I rigid <= 7.5 t | Diesel HDV- EURO II rigid <= 7.5 t | Diesel HDV- EURO III rigid <= 7.5 t | Diesel HDV- EURO IVrigid <= 7.5 t | Diesel HDV- EURO Vrigid <= 7.5 t | Diesel HDV- EURO III rigid 12-14 t | Diesel HDV- EURO II rigid 14-20 t | Diesel HDV- EURO III rigid 14-20 t | Diesel HDV- EURO IVrigid 14-20 t | Diesel HDV- EURO Vrigid 14-20 t | Buses - EURO II urban 15-18 t | Buses- EURO III urban 15-18 t | Buses - EURO IV urban 15-18 t | Buses - EURO V urban 15-18 t | Natural gas buses - EURO III | Natural gas buses - EEV | Biodiesel buses | Electric mode buses | Hybrid mode buses | Motorcycle 4T - Conventional < 250 cc | Motorcycle 4T EURO I < 250 cc | Motorcycle 4T EURO II < 250 cc | Motorcycle 4T EURO III < 250 cc | Motorcycle 4T EURO II 250-750 cc | Motorcycle 4T EURO III 250-750 cc | Mopeds - Conventional < 50 cc | Mopeds -EURO II < 50 cc | Mopeds -EURO III < 50 cc | Electric Mopeds < 50 cc | Electric Motorcycle
Base Case | 0.011218 | 0.01888 | 0.057786 | 0.091653 | 0.091446 | 0.0014523 | 0.0025471 | 0.0045133 | 0.0090938 | 0.0056722 | 0.0030768 | 0.0045838 | 0.0038728 | 0.040728 | 0.15147 | 0.30956 | 0.0013544 | 0 | 0.00026765 | 0.0012833 | 0.0022704 | 0.0036277 | 0.0039649 | 0.018253 | 0.031283 | 0 | 0 | 0.002362 | 0.0020138 | 0.0057883 | 0.012427 | 0.010265 | 0.004552 | 0.0018047 | 0.0032671 | 0.010919 | 0.0072674 | 0.0018878 | 0.0049399 | 0.0050781 | 0.0041454 | 0.00051817 | 0.0011271 | 0.0012941 | 0.0051762 | 0 | 0 | 0.0033544 | 0.0023127 | 0.0048962 | 0.0092034 | 0.0010681 | 0.0020077 | 0.0012808 | 0.0018695 | 0.003514 | 0 | 0
Chart: Vehicular fleet Barcelona
| Gasoline PC - ECE 15-04 < 1.4 L | Gasoline PC - EURO I < 1.4 L | Gasoline PC - EURO II < 1.4 L | Gasoline PC - EURO III < 1.4 L | Gasoline PC - EURO IV < 1.4 L | Gasoline PC - EURO I 1.4-2.0 L | Gasoline PC - EURO II 1.4-2.0 L | Gasoline PC - EURO III 1.4-2.0 L | Gasoline PC - EURO IV 1.4-2.0 L | Gasoline PC - EURO III > 2.0 L | Gasoline PC - EURO IV > 2.0 L | Diesel PC - EURO I < 2.0 L | Diesel PC - EURO II < 2.0 L | Diesel PC - EURO III < 2.0 L | Diesel PC - EURO IV < 2.0 L | Diesel PC - EURO III > 2.0 L | Electric mode PC | Hybrid mode PC | Gasoline LDV - Conventional < 3.5 t | Gasoline LDV - EURO I < 3.5 t | Gasoline LDV - EURO III< 3.5 t | Gasoline LDV - EURO IV < 3.5 t | Diesel LDV - Conventional < 3.5 t | Diesel LDV - EURO I < 3.5 t | Diesel LDV - EURO II < 3.5 t | Diesel LDV - EURO III< 3.5 t | Diesel LDV - EURO IV < 3.5 t | Electric mode LDV | Hybrid mode LDV | Gasoline HDV > 3.5 t | Diesel HDV - EURO II rigid <= 7.5 t | Diesel HDV - EURO III rigid <= 7.5 t | Diesel HDV - EURO IVrigid <= 7.5 t | Diesel HDV - EURO Vrigid <= 7.5 t | Diesel HDV - EURO II rigid 14-20 t | Diesel HDV - EURO III rigid 14-20 t | Diesel HDV - EURO IVrigid 14-20 t | Buses - EURO II urban 15-18 t | Buses- EURO III urban 15-18 t | Buses - EURO IV urban 15-18 t | Natural gas buses - EURO III | Natural gas buses - EEV | Biodiesel buses | Electric mode buses | Hybrid mode buses | Motorcycle 4T - Conventional < 250 cc | Motorcycle 4T EURO I < 250 cc | Motorcycle 4T EURO II < 250 cc | Motorcycle 4T EURO III < 250 cc | Motorcycle 4T - Conventional 250-750 cc | Motorcycle 4T EURO I 250-750 cc | Motorcycle 4T EURO II 250-750 cc | Motorcycle 4T EURO III 250-750 cc | Motorcycle 4T EURO II > 750 cc | Motorcycle 4T EURO III > 750 cc | Mopeds - Conventional < 50 cc | Mopeds -EURO I < 50 cc | Mopeds -EURO II < 50 cc | Mopeds -EURO III < 50 cc | Electric Mopeds < 50 cc | Electric Motorcycle
Base Case | 0.0075996 | 0.01265 | 0.039136 | 0.061744 | 0.067113 | 0.0017067 | 0.0030241 | 0.0061766 | 0.0038006 | 0.0020616 | 0.0030713 | 0.0026783 | 0.028541 | 0.11801 | 0.25097 | 0.0010744 | 0 | 0.00042965 | 0.0019651 | 0.0014292 | 0.0020644 | 0.0030966 | 0.0054785 | 0.0087537 | 0.0095676 | 0.044047 | 0.075488 | 0 | 0 | 0.0023168 | 0.0049737 | 0.0041084 | 0.0018219 | 0.0013076 | 0.0043701 | 0.0029088 | 0.0060038 | 0.0061717 | 0.0050382 | 0.0013698 | 0.0015728 | 0.006291 | 0 | 0 | 0.016082 | 0.011088 | 0.023474 | 0.044124 | 0.0035083 | 0.0024188 | 0.0051208 | 0.0096255 | 0.0014292 | 0.0026865 | 0.0098341 | 0.0067802 | 0.014354 | 0.026982 | 0 | 0
PC
LDV
HDV
Motos
PC
LDV
HDV
Motos