## Slide 1
City of México , 10 November 2015
CALIOPE Mobile
European Air Quality Forecast at hand
Miguel Castrillo
miguel.castrillo@bsc.es

## Slide 2: CALIOPE Air Quality Forecast System

## Slide 3: Barcelona Supercomputing Center
Created in 2005; more than 400 employees.
Research, develop and manage information technology.
Facilitate scientific progress and its application in society.
Earth Science Department
Atmospheric composition modelling
Climate prediction modelling
Computational Earth Sciences
Earth Sciences Services

## Slide 4: CALIOPE Air Quality Forecast System
Operational Air Quality Forecast System.
6 nested domains, from 12 to 1km spatial resolution.
Meteorological, emission and air quality forecast.
Run daily on Marenostrum III Supercomputer.
Scientific support: 19 PhD thesis, > 50 papers
International projects and companies.
- 3,056 compute nodes, 48,896 processor cores
- 16 CPU cores per node (2x Intel SandyBridge-EP @ 2.6 GHz)
- 32GM main memory per node (8 x 4GB DDR3-1600 DIMMS)
- Infiniband FDR10

## Slide 5: CALIOPE system overview
AIR QUALITY PRODUCTS
METEOROLOGICAL FORECAST
NCEP GLOBAL SIMULATIONS
WRF-ARW
12 km x 12 km
IC/BC
nesting
WRF-ARW
4 km x 4 km
EMISSION FORECAST
HERMES-DIS
12 km x 12 km
HERMES-BOUP
4 km x 4 km
Meteo. fields
EMEP inventory
AIR QUALITY FORECAST
CMAQ
4 km x 4 km
CMAQ
12 km x 12 km
NCAR MOZART4
1.9 º x 2.5º
Meteo. fields
IC/BC
nesting
Emis. fields
DESERT DUST FORECAST
BSC-DREAM8b
0.5º x 0.5º
WEB SITE
MOBILE SITE AND APP
POPULATION UNDER AQI
NO2 COLUMN
AQI
TIME SERIES PLOTS

## Slide 6: CALIOPE System products
CALIOPE website (www.bsc.es/caliope)
Air Quality Levels for Europe
What’s on CALIOPE website:
  Air Quality, Weather, Emissions, AQI Forecast.
  Satellite images.
  Forecast evaluation.
  Publications.

## Slide 7: CALIOPE EU mobile application

## Slide 8: CALIOPE EU mobile application
V1.0, Nov 2013  IP domain (4x4 km resolution, 431 stations).
v1.6, Dec 2014  Canary Islands domain (2x2 km resolution, 483 stations).
Over 12,000 downloads (Android + iOS).
EU v1.0, Sep 2015  Europe domain version (12x12 km resolution, 563 stations) financed by MYGEOSS
v1.0
Oct 2013
v1.2
Nov 2013
v1.3
Dec 2013
v1.6
Dec 2014
EU v1.0
Sep 2015

## Slide 9: CALIOPE EU mobile application
48-hour Air Quality forecast.
Geolocation: Provides information for near stations by using the user device’s GPS.
Search: Stations can be found by country.
Map visualization: Stations positioned on map.

## Slide 10: CALIOPE EU mobile application
48-hour five pollutant overlays.

## Slide 11
For further information please contact
caliope@bsc.es
Thank you!

## Slide 12: Temporal scales
Today
Hours
Days
Weeks
Months
Seasons
Years
Decades
Past
Century
FORECAST
PREDICTION
PROJECTION
DIAGNOSTIC
Mineral Dust
Air quality
Meteorology
Climate predictions
Climate projections
Climate projections
Climate predictions
Notes: També podem treballar a totes les escales temporals. L’anàlisi diagnòstic d’esdeveniments passats, els pronòstics per als propers dies, les projeccions a molts anys vista i el terme mitg, les prediccions que van des de setmanes i mesos fins a dècades.
On som forts i el que ens fa destacar son dos casos concrets que molt pocs altres centres treballen i que estan fortament lligats tant a l’energia solar com a l’energia eòlica.
D’una banda som líders en temes de modelització de la pols a l’atmòsfera que és un tema crític per a zones àrides, semiàrides i zones adjacents (Àfrica, Sud d’Espanya i Orient Mitjà) i cabdal per a la gestió de l’energia solar.
D’altra banda les prediccions climàtiques (seasonal to decadal) són un tema molt nou que tot just es comença a treballar a nivell mundial i en el que només el nostre centre i la Met Office de Regne Unit estem fent coses i en molts casos col·laborant i en contacte constant amb el sector de l’energia eòlica.
A continuació us explicaré aquest dos punts amb una mica més de detall.

## Slide 13: CALIOPE System open data sources
External open data sources, used into the models (yellow):
EMEP emission database (CEIP, 2015)
CORINE Land Cover v16 04/2012 (EEA, 2012)
SRTM DEM v4.1 90m (CGIAR-CSI, 2008)
Open data sources used in operational mode, downloaded daily (green):
GFS Meteorological initial conditions (UCAR/NCEP, 2015)
Mozart4 /GEOS-5 Chemical boundary and initial conditions (UCAR/NCAR, 2015)
The AIRBASE AQ e-Reporting (EEA, 2015).