## Slide 1: BSC UPDATE
Carlos Pérez García-Pando
Oriol Jorba, Enza di Tomaso, Sara Basart, Marc Guevara, María Gonçalves, Vincenzo Obiso, María Teresa Pay, Carles Tena
Atmospheric Composition Group
Earth Sciences Department
Barcelona Supercomputing Center
26/06/2017
9th ICAP Meeting, Lille France

## Slide 2: Development of MONARCH Multiscale Online Non-hydrostatic AtmospheRe CHemistry model
Multiscale: global to regional scales allowed (nesting capabilities)
Non-hydrostatic dynamical core: single digit kilometre resolution allowed
On-line coupling: weather-chemistry feedback processes allowed
Ensemble-based data assimilation system for aerosols
MONARCH
NCEP/NMMB
BSC-CTM
AEROSOLS
GAS-PHASE CHEMISTRY
VOLCANIC ASH
→ Janjic and Gall (NCAR/TN 2012)
→ Janjic and Vasic (EGU2012)
→ Janjic et al. (MWR 2011)
→ (...)
→ Pérez et al. (ACP 2011)
→ Haustein et al. (ACP 2012)
→ Spada et al. (ACP 2013)
→ Spada et al. (AE 2014)
→ Spada et al. (in prep)
→ DiTomaso et al. (GMD 2016)
→ Martí et al. (ACP 2016)
→ Jorba et al. (JGR 2012)
→ Badia and Jorba (AE 2014)
→ Badia et al. (GMD 2016)
Multiscale Model from Global to Local Scales

## Slide 3
Non-hydrostatic Multiscale Model NMMB (Janjic et al., 2004)
Arakawa B grid (Arakawa and Lamb, 1977)
Vertical hybrid σ-pressure coordinate system (Simmons and Burridge, 1981)
A rotated longitude-latitude coordinated system is used for regional simulations
Radiation: RRTMG
Convection: Betts-Miller-Janjic (BMJ) (Betts, 1986)
Clouds and microphysics: Ferrier (Ferrier et al., 2002)
Turbulence: Mellor-Yamada-Janjic (MYJ) (Janjic, 2001)
Land model: NCEP NOAH (Eck et al., 2003) and LISS
Model features
Physics schemes
NMMB

## Slide 4
4
DOMAIN | GLOBAL (ICAP) | REGIONAL North Africa, Middle East and Europe (SDS-WAS) | REGIONAL Europe/Iberian Peninsula/Urban Areas (CALIOPE)
Model | MONARCH | MONARCH | CMAQ (DREAM for dust) MONARCH
Status | QO | O | O
Meteorology | Inline: NMMB | Inline: NMMB | Offline: WRF-ARW Inline: NMMB nesting
Resolution | 1.4x1 deg 0.7x0.5 deg | 0.1x0.1 deg 0.03x0.03 deg | 0.1x0.1 / 0.04x0.04 / 0.01 x0.01
levels | 24 48 | 40 60-70 | 30 60-70
DA | LETKF | LETKF | NA LETKF
Assimilated Obs | MODIS DT+DB (DU) MODIS DT+DB (ALL) | MODIS DT+DB (DU) | NA MODIS DT+DB (ALL)
Aerosol Species | DU, SS, BC, POA, SOA bio, SOA anthro, SU, NI | DU | CMAQ (AERO5) MONARCH aerosols
Gas phase chemistry | CBM-IV CB05 ONLINE and CLIMATOLOGY |  | CB05 CB05
Emissions | HERMES 3.0 (HTAP v2) MEGAN ONLINE |  | EMEP, MEGAN / HERMES, MEGAN/ HERMES MEGAN
Bio. Burn. Emissions | GFAS NRT |  | NA NRT
CURRENT FORECASTING – DEVELOPED/AVAILABLE – UNDER DEVELOPMENT - PLANNED
BSC Current forecasts and plans

## Slide 5
Sectional
dust (DU)
sea-salt (SS)
Organic Aerosols (OA)
Primary Organic Aerosols (POA)
Secondary organic aerosols (SOA)
4 gaseous tracers (OH, O3, TERP, ISOP). Online emission (MEGAN)
4 aerosol-phase hydrophilic tracers
2-product scheme of Tsigaridis and Kanakidou (2007)
Oxidation by OH and O3 and gas-particle partitioning
Anthropogenic SOA from Toluene and Xylene under development
Sulfate (SU):
4 additional prognostic tracers (SO2, DMS, H2O2, H2SO4)
3 online or climatological oxidants (OH, O3, HO2)
gas-phase oxidation of SO2, DMS and H202 by OH
aqueous-phase oxidation by H202 and O3
Bulk
Black Carbon (BC)
MONARCH: Aerosols

## Slide 6: HERMESv2.0: An emission model for Europe and Spain

## Slide 7: HERMESv3.0: A multiscale emission modeling framework
* Vertical profiles:
- Point sources, biomass burning, air traffic
* Temporal profiles: Monthly, weekly and daily factors per sector
* VOC and PM2.5 speciation: CB05, SAPRC99, AERO5, AERO6
A stand-alone tool for simulating emissions on a user-defined grid for global, regional and urban air quality models.
Users can select, combine and scale multiple inventories through a flexible configuration file to obtain hourly gridded emissions.
Multiple global and regional emission inventories
Online emissions:
Biogenic (MEGAN), lightning, ocean
Spanish bottom- up emission inventory (street level emissions)
User-defined grid:
- Regular lat-lon
- Rotated lat-lon
- LCC
Masking and scaling factors to combine and update emission inventories
Vertical profiles:
- Point sources, biomass burning, air traffic
Temporal profiles:
- Monthly, weekly and daily factors per sector
VOC and PM2.5 speciation:
- CB05, SAPRC99, AERO5, AERO6
(···)
Emission data library
Conservative regridding
Vertical, temporal, speciation

## Slide 8: HERMESv3.0 Configuration for ICAP
EI | Sector | Year | Pollutants | Vertical | Temporal
GFASv1.2 Kaiser et al. (2012) | Biomass burning | 2015 | oc, bc(*), so2, pm25,c2h6s | Plume top = Sofiev et al. (2012) Distribution=50 % top 50% uniform below | Daily
HTAPv2.2 Janssens-Maenhout et al. (2015) | energy | 2010 | oc,bc,so2, pm25,pm10 | 218-724 m (Bieser et al., 2011) | Monthly
 | industry |  |  | 72-292 m (Bieser et al., 2011) | 
 | residential |  |  | First layer | 
 | transport |  |  | First layer | 
 | air_lto |  |  | 0 – 1 km | Yearly (monthly flat profile)
 | air_cds |  |  | 1 – 9 km | 
 | air_crs |  |  | 9 – 12 km | 
 | ships |  |  | First layer | 
Wiedinmyer el al. (2014) | Residential trash burning |  |  | First layer | 
MOZART Horowitz et al. (2013) | Ocean | 2000 | c2h6s | First layer | Monthly
(*) Scaling factors applied: bc  6.1 and oc  3.1 (Rémy et al., 2017) |  |  |  |  | 

## Slide 9: Residential waste burning
Wiedinmyer et al. (2014)
For this sector, PM2.5-BC-OC accounts for 42.7% of total PM2.5.
All PM2.5-BC-OC is considered PMFINE
Residential waste burning emissions have a significant contribution to global OC. These emissions are mainly occurring in developing and poor countries

## Slide 10: Natural aerosol emissions
Sea-salt: Jaeglé et al. (2011) wind and sst
Dust: source location based on MODIS DB, vertical flux scaled with the topographic source of Ginoux - 2001

## Slide 11: Natural aerosol emissions
z0 based on satellite static roughness +
monthly vegetation (LAI) from MODIS
3 emission schemes with drag partition:
NMMB original (~Maticorena based scheme)
GOCART scheme
New Kok scheme (Kok et al., 2014)

## Slide 12
AOD Evaluation 2015
DJF
MAM
MODIS C6 Level 3
MONARCH All Sky
MONARCH Clear Sky

## Slide 13
JJA
SON
MODIS C6 Level 3
MONARCH All Sky
MONARCH Clear Sky
AOD Evaluation 2015

## Slide 14
Dust
SS
SU
SOA
OM
BC
Fine (unspec.)
Coarse (unspec.)
AOD components

## Slide 15
AOD AERONET
A
O
D
M
O
N
A
R
C
H
AOD Evaluation 2015

## Slide 16
Dust Atlantic Transport

## Slide 17
Europe

## Slide 18
Biomass Burning

## Slide 19
China

## Slide 20
Intensive Optical Properties in MONARCH
Preliminary results of evaluation against AERONET of aerosol single scattering albedo simulated by the MONARCH:
i) AERONET level 1.5 data with all screening 2.0 filters applied except AOD > 0,4
ii) Monthly data collected over 5 years (2002-2006): # measures > 30 for each month

## Slide 21: Data assimilation updates at BSC
Testing new observational datasets (MODIS coarse DB, IASI dust AOD)
Vertical observational constraint (assimilation of extinction profiles)
Multi-scale capability (coping with a limited area domain and rotated coordinate system, e.g. used by the BDFC)
Adapting the DA scheme to model developments (MONARCH v2.0)
Notes: Paul Ginoux’s coarse AOD dataset with error estimation; IASI dust dataset from the aerosol_cci project
Lidar profile case studies under the ACTRIS-2 project
The data assimilation scheme, initially built for a global regular grid, has been adapted to the NMMB-MONARCH regional rotated coordinate system. The rotated frame is used in order to reduce the variation of the grid size.
MONARCH v2.0 has new emission schemes for dust and the most important aerosol species

## Slide 22
MODIS Deep Blue coarse DoD
Assimilation of 0.1x0.1 deg MODIS Deep Blue coarse DOD based on Ginoux et al., 2012
Error estimates: collocated comparison of DOD over N Africa (5 to 35N,-20 to 60E) with AERONET data between 2003 and 2015
First assimilation tests with MONARCH at 0.3x0.3 deg resolution
Notes: Error estimates based on collocated comparison of DOD over N Africa (5 to 35N,-20 to 60E) with sunphotometer data (AERONET) between 2003 and 2015

## Slide 23: Assimilation of MODIS coarse Deep Blue
Feedback from assimilation increments
Notes: Feedback on model bias
some of these known biases have been corrected, we are now preparing DA tests for MONARCH v2.0
Though observations were assigned at 12 UTC, the 4D extension used for the LETKF propagates the observational impact through the whole assimilation window.
Notes on the 4D LETKF in general:
We use a 24-hour assimilation window and observations are considered for assimilation at four time slots within the window, at 0, 6, 12 and 18 UTC. The system uses as first guess a 1-day forecast with output every 6 hours. Simulated observation and background departures are calculated at each time slot. We are using the LETKF implementation with a four-dimensional extension as described in Hunt et al. (2007). The state vector comprises of the mixing ratio at all the time slots considered. Background observation means and perturbation matrices are formed at the various time slots when the observations are available. They are then vertically concatenated to form a combined background observation mean and perturbation matrix which are used for the standard LETKF calculations, i.e. the analysis increments are based on all innovations throughout the day.

## Slide 24: ACTRIS-2 project Joint Research Activity on DA
24
Evaluating the potential of ACTRIS‐2 data for assimilation through pilot dust case studies
Multi-wavelength Mie-Raman lidar profile observations provided by the University of Lille for the M'bour site outside Dakar
Notes: Top row: dust AOD analysis at 550 nm at three time steps of the assimilation window.
Bottom row: The corresponding analysis increments
For this particular event the assimilated profile corrects an underestimation in total column extinction in the model.
Though observations were available only at 18 UTC, the 4D extension used for the LETKF propagates the observational impact through the whole assimilation window.
Observation operator: model equivalent of extinction profiles at 532 nm. The observation vertical information is interpolated at the mid altitude of the model layers using a third-order polynomial interpolation function. Model tracers are then interpolated at the observation location at each model level. The extinction efficiency factors for 532 nm have been calculated using the Mie scattering theory assuming dust spherical, non soluble particles for the 8 model size bins, and, within a bin, a lognormal distribution, and using information on refractive indices at different wavelength from the OPAC database. The imaginary part of the refractive index has been interpolated from the available values at 500 and 550 nm. We plan to revise our choice of optical properties since the OPAC database is known to provide a too absorptive dust aerosol.
Vertical and horizontal localization are performed through R-localization, i.e. the localization is performed in the observation error covariance matrix, making the influence of an observation on the analysis decay gradually toward zero as the distance from the analysis location increases. We apply both horizontal and vertical localization, and use a horizontal localization factor equal to 2. This means that observation's influence in the horizontal plane will become negligible at distances greater than 3 to 4 grid points (i.e. 1.3° circa, the actual distance is resolution dependent). Vertical localization factor set to the value 1: it means that after two grid points the influence of an observation is negligible.
Observations: All the extinction profiles are computed by averaging 2-hour lidar signals except when some of the measurements are not available. All the nightime extinction profiles are derived from the Raman method, while the daytime extinction profiles are calculated from the Klett method. The assumed lidar ratio that is required for the Klett method is taken from the nearest nighttime Raman retrieval. Due the overlap range of the lidar system, only signal above 700 m (in height) is considered valid. We have assimilated observations from model level 7 to 17, i.e. above 700 m and up to 4000 m circa.
Obs uncertainty: described by the diagonal observation error covariance matrix with elements set to 0.0001+0.01*ext532 in this first test (too low! But otherwise no impact)

## Slide 25: ACTRIS-2 project Joint Research Activity on DA
Evaluating the potential of ACTRIS‐2 data for assimilation through pilot dust case studies
Increasing the vertical localization factor
Higher observation uncertainty
Observational impact through the whole assimilation window
Notes: Top:
a: As a sanity check we can note that the analysis is closer to the assimilated observations (available at 18UTC) than the first guess
Bottom:
a: When a higher observation uncertainty is used (0.0001+0.1* ext532), there are only minor analysis corrections. This might be due to an under-representation of the background uncertainty which translated into giving a lower weight to the observations with respect to the background. Background error statistics in our system should be investigated further in order to assess how well our ensemble configuration represents model uncertainty.
b: Increasing the vertical localization factor to the value 2 produces an overestimation of profile peak in the analysis. Further work should go into identifying a better function for the vertical localization than the one we have used. While in the horizontal grid of reference distances between grid points can be used, with some approximation, as a proxy for real distances, in the vertical grid of reference this approximation is less correct. we plan to test the calculation of vertical distances in physical space rather than in grid space.

## Slide 26: Case Study ESA Climate Change Initiative
26
IASI dust reanalyses (MetOp-A IASI in the thermal IR)
4 different retrieval algorithms
ULB v7, Universite Libre de Bruxelles
MAPIR v3.5, BIRA-IASB
LMD v2.1
IMARS v5.2, DLR
Level 3 mineral dust AOD datasets
retrieved from MetOp-A IASI in the thermal IR
uncertainty estimation
converted to 550nm
sub-daily set mineral dust retrievals (6h)
spatially aggregated (1x1)
screened for AOD (>0.15)
Notes: 4 different retrieval algorithms
ULB v7, Universite Libre de Bruxelles
MAPIR v3.5, BIRA-IASB
LMD v2.1, Laboratoire de Meteorologie Dynamique
IMARS v5.2, DLR
The aerosol_cci Phase 2 project is one of the fourteen parallel projects of the European Space Agency (ESA) Climate Change Initiative (CCI) programme. The objective of the CCI programme is to realise the full potential of long-term global Earth Observation archives that ESA together with its Member States have established over the last 30 years. Different Essential Climate Variables (ECVs) are under investigation, each of them in a dedicated project. With regard to the aerosol variables, the Aerosol_cci project brings together the major European aerosol retrieval experts and user communities, with the aim at producing a set of global aerosol ECV products from European Earth Observation sensors.
Assimilation of IASI aerosol_CCI mineral dust observations with the aim to:
showcase their potential to improve prediction and monitoring of mineral dust;
provide guidelines for the future development of dedicated dust observation products tailored for data assimilation.
Level 3 mineral dust AOD datasets
retrieved from MetOp-A IASI in the thermal IR
uncertainty estimation
converted to 550nm
sub-daily set mineral dust retrievals (6h)
spatially aggregated (1x1)
screened for AOD (>0.15)

## Slide 27
Case Study ESA Climate Change Initiative
Notes: Timeseries show differences in particular closer to source regions.
First feedback on the 4 products:
- ULB analysis performs best
- MLD analysis is comparable, but noisier
MAPIR analysis overestimates
IMARS analysis less good, experiments from 2007 performed much better

## Slide 28
IMARS_QC
+
DT
Case Study ESA Climate Change Initiative
Notes: - IMARS_QC: a quality control was applied based on thresholds on effective emission temperature of dust layer and on AOD
DT: NRL MODIS dark target with dust filter
DB: NASA MODIS deep blue with dust filter
- in Tamanrasset some evidence of a positive impact of the IASI IMARS dust product. IASI tends to overestimate AOD in Algeria/Morocco compared to MODIS (because thermal IR sensitive to bigger particles?)

## Slide 29: WMO Dust Regional Centers
ASIAN
PAN AMERICAN
Extracted from Ginoux et al. (2012, Rev. Geophys.)
NA-ME-E
Barbados, CMHI
Beijing, CMA
Barcelona,
BSC-AEMET
RSMC-ASDF
RSMC-ASDF
Notes: Regional Specialized Meteorological Center with activity specialization on Atmospheric Sand and Dust Forecast (RSMC-ASDF)
Panamerican working, web page
Beijing will have an operational (approved, not publicicez)

## Slide 30
SDS-WAS. North Africa, Middle East and Europe
Regional Center - Research
Started in 2010
http://sds-was.aemet.es
Barcelona Dust Forecast Center - Operations
First specialized WMO Center for mineral dust prediction. Started in 2014
http://dust.aemet.es @Dust_Barcelona
WMO Dust Centers in BCN

## Slide 31
http://sds-was.aemet.es/
SDS-WAS NAMEE: Dust observations
Archive
Notes: MSG second generation centrado a 42 grados este. Meteosat 8
EUMETSAT
We maintain an archive, started this year
Debra

## Slide 32
OBSERVATIONS
http://sds-was.aemet.es/projects-research/evaluation-of-model-derived-dust-vertical-profiles
SDS-WAS NAMEE: Towards NRT Evaluation profiles
3 ceilometers
1 lidar
  BSC-DREAM8b
  NMMB/BSC-Dust
  CAMS
  DREAM8-NMME
  ….
Data format
Exchange operational protocol includes 72 hours forecasts
SDS-WAS MODELS
Extinction profiles at 12UTC available in a window of 24 hours

## Slide 33
SDS-WAS NAMEE: NRT Evaluation profiles
Atlantic dust event: 9 - 12 December 2016

## Slide 34
Dust prediction models provide 72 hours (at 3-hourly basis) of dust forecast (AOD at 550nm and surface concentration) covering NAMEE
http://sds-was.aemet.es/
SDS-WAS NAMEE: Daily Dust Forecasts
MODEL | RUN TIME | DOMAIN | DATA ASSIMILATION
BSC-DREAM8b | 12 | Regional | No
CAMS ECMWF | 00 | Global | MODIS AOD
DREAM8-NMME | 00 | Regional | CAMS analysis
NMMB/BSC-Dust | 00 | Regional | No
MetUM | 12 | Global | MODIS AOD
GEOS-5 | 00 | Global | MODIS reflectances
NGAC | 00 | Global | No
RegCM4 EMA | 00 | Global | No
DREAMABOL | 12 | Regional | No
WRF-CHEM NOA | 12 | Regional | No
SILAM | 12 | Regional | No
LOTOS-EUROS | 12 | Regional | No

## Slide 35: ICAP-MME vs SDS-WAS: Results 2016
ICAP-MME Mean
SDS-WAS Mean
SDS-WAS Median
DJF
MAM
JJA
SON
Notes: Comparison based on 6-hourly basis DOD values
For the SDS-WAS Mean, only those values between 0 and 8 are considered.

## Slide 36: ICAP-MME vs SDS-WAS: Results 2016
Notes: Comparison based on 6-hourly basis DOD values
For the SDS-WAS Mean, only those values between 0 and 8 are considered.
Dust filter to the observations
Dust: AE > 0.75 DOD = AOD
No-dust: AE > 1.2 DOD = 0
Mixed (not considered in the statistical evaluation): 0.75 < AE < 1.2 DOD = NA

## Slide 37
37
DOMAIN | GLOBAL (ICAP)
Model | MONARCH
Status | QO
Meteorology | Inline: NMMB
Resolution | 1.4x1 deg 0.7x0.5 deg
levels | 24 48
DA | LETKF
Assimilated Obs | MODIS DT+DB (DU) MODIS DT+DB (ALL)
Aerosol Species | DU, SS, BC, POA, SOA bio, SOA anthro, SU, NI
Gas phase chemistry | CBM-IV CB05 ONLINE and CLIMATOLOGY
Emissions | HERMES 3.0 (HTAP v2) MEGAN ONLINE
Bio. Burn. Emissions | GFAS NRT
CURRENT FORECASTING – DEVELOPED/AVAILABLE – UNDER DEVELOPMENT - PLANNED
2017: New Marenostrum up in July
Full model into ICAP ensemble
Scalability tests and setting final resolution
Further tuning of
- emissions by region,
- wet scavenging
- optical properties
2018 Q2: Data assimilation with full aerosol model
Autosubmit workflow
Regional forecasts for Europe and Spain
Near future Operational Updates