## Slide 1: HERMESv3: A stand-alone multiscale atmospheric emission model Marc Guevara, Carles Tena, Manuel Porquet, Oriol Jorba, Carlos Pérez-García Pando
24/10/2018
17th Annual CMAS Conference
Friday Center, UNC-Chapel Hill, NC, USA

## Slide 2: Motivation
EMISSIONS: DIFFERENT NEEDS FOR DIFFERENT SCALES

## Slide 3: HERMESv3
A python-based, open source, parallel and stand-alone multiscale atmospheric emission model that processes and estimates gas and aerosol emissions for use in chemistry transport models
global-regional module
(HERMESv3_GR)
bottom-up module
(HERMESv3_BU)
A processing system to calculate emissions through an automatic combination of existing inventories and user defined vertical, temporal and speciation profiles
An emission model to estimate emissions at the source level (e.g. road link) combining state-of-the-art bottom-up methods with local activity and emission factors
Notes: Take existing emission inventories and adapt them to the CTM requirements in a flexible and transparent way

## Slide 4: General structure of the HERMESv3_GR
Emission inventory configuration file
General configuration file
Temporal
Vertical
Speciation
Emission data library
Profiles
Pre-processing
Emission core
Spatial regridding
Vertical distribution
Temporal distribution
Speciation treatment
Writing
Input data
Configuration files
Initialization
Auxiliary files
Original emission inventories
Output
emission file
Dataset/file
Function
Conf file
Shows input or output
Notes: interpolation weight matrix, timezones for temporal distribution

## Slide 5: Emission inventory pre-proccesing
HERMESv3 emission data library
Existing emission inventories
Homogenization of the original emission inventories
Unique file format (NetCDF)
CF 1.6 conventions (cell centroid and boundary coordinates, cell area)
All emissions are reported in the same units (fluxes, kg·m-2·s-1)
All pollutants follow the same naming convention
Notes: Different formats (NetcDF, CSV), units and naming conventions.
Individual pre-processing functions to homogeniese all these datasets to a common format

## Slide 6: Emission data library
Name | Sources | Spatial res/cov | Temporal res/cov | Reference
EDGARv4.3.2 | Anthropogenic | Global (0.1x0.1) | Annual (1970 – 2012) Monthly (2010) | Cripa et al. (2018) Huang et al. (2017)
CEDS | Anthropogenic | Global (0.5x0.5) | Monthly (1851 – 2014) | Hoesly et al. (2018)
ECLIPSEv5.a | Anthropogenic | Global (0.5x0.5) | Monthly (1990 - 2050) | Klimont et al. (2017)
HTAPv2.2 | Anthropogenic | Global (0.1x0.1) | Monthly (2008 and 2010) | Janssens-Maenhout et al. (2015)
GFASv1.2 | Biomass burning | Global (0.1x0.1) | Daily (2012-present) | Kaiser et al. (2012)
Carn | Volcanoes (degassing) | Point sources | Annual (2005 – 2015) | Carn et al. (2017)
Wiedinmyer | Open air trash burning | Global (0.1x0.1) | Annual (2010) | Wiedinmyer et al. (2014)
TNO_MACC-iii | Anthropogenic | Regional (0.0625*0.125) | Annual (2000 – 2011) | Kuenen et al. (2014)
EMEP | Anthropogenic | Regional (0.1x0.1) | Annual (2000 – 2016) | Mareckova et al. (2017)
Multiple up-to-date gridded emission inventories available to the user

## Slide 7: Spatial regridding
User defined destination working domain:
Conservative regridding (ESMF)
Multiple spatial resolutions
Multiple projections: regular lat-lon, rotated lat-lon, mercator, lambert conformal conic
Regular lat-lon
(0.7*0.5 deg)
Rotated lat-lon
(0.1*0.1 deg)
Lambert conformal conic
(4kmx4km)
Mercator
(50kmx50km)

## Slide 8: Spatial regridding
Designing and adjusting the emission modelling experiment:
Combination of multiple emission inventories
Country-specific scaling factors
Country-specific masks
HTAPv2.2
HTAPv2.2 + GFASv1.2
HTAPv2.2
(China x5, India x0.5)
HTAPv2.2
(China and India masked out)
ECLIPSEv5.a (China and India)
HTAPv2.2 (other countries)
Notes: We know that for a certain región an emission inventory performs better than another HERMESv3 allows to combine and tune different emission inventories through the applicaton of user defined country specific scaling factors and masks
Combinations are endless Functionality useful not only for adjusting emissions but also for perturbing them in a transparent way for data assimilation exercises

## Slide 9: Temporal distribution
From anual to hourly emissions:
Specific monthly, weekly and diurnal profiles per sector and pollutant
World time zones and daylight saving time

## Slide 10: Temporal distribution
From anual to hourly emissions:
Gridded temporal profiles (variation not uniform across the space, e.g. agricultural emissions)
Default gridded monthly profile
Janssens-Maenhout et al. (2016)
Improved gridded monthly profile
Paulot et al. (2014) and Zhang et al. (2018)
Rate of change of NH3 volume mixing ratio (AIRS, 2002 – 2016) (Warner et al., 2017)

## Slide 11: Speciation and writing
Mapping of the original pollutants to the species needed by the chemical mechanism of interest:
Gas-phase: CB05, CB05e51, RADM2
Aerosols: AERO5, AERO6, MADE/SORGAM
Writing of the output files following the conventions of the selected CTM:
NMMB-MONARCH
CMAQ
WRF-Chem
CB05 specie | mapping
NO | 0.72*nox_no
NO2 | 0.18*nox_no
HONO | 0.1*nox_no
CO | co
SO2 | so2
NH3 | nh3
ALD2 | c2h4o
CB05 specie | mapping
OLE | c8h16+c5h10+c3h6+c4h8+c6h12+0.5*hialkanes
PAR | 4*c4h10+6*c6h14+5*hialkanes+6*c8h16+3*c5h10+c3h6+3*c3h6o+2*c4h8+7*c7h16+4*c6h12+hialkenes+5*c5h12+1.5*c3h8
SESQ | 0
TERP | terpenes
(···) | (···)
Carter et al. (2015)
Reff et al. (2009)
(···)

## Slide 12: Technical Implementation
1cpu: 1h20min
32cpu: 15min
Initialization
Regrid
Vertical
Temporal
Speciation
Write
No
More sectors?
Yes
P_0
P_1
P_2
P_3
t0
t1
tn
t2
…
P_0
P_2
P_3
v0
v1
v2
v3
vn
…
Test case:
European-North Africa-Middle East domain (0.1x0.1deg, 48 layer)
TNO_MACC-iii (EU)
HTAPv2.2 (rest of countries)
All sectors/pollutants
24-h simulation
Notes: Emission core module parallelized using a map partitioning strategy
the destination working domain is divided into vertical sections, which are equal to the number of processors to be used defined by the user
Writing function does not scale properly
netCDF4 Python library writes the results in row-major order (C-style), while during the spatial regridding ESMF divides the domain in vertical sections (column-major order, FORTRAN-style)

## Slide 13: Applications
ICAP multi-model ensemble (MONARCH) www.nrlmry.navy.mil/aerosol/icap.1135.php
CALIOPE-EU forecast system (WRF/CMAQ)
http://www.bsc.es/caliope/
AIRE – Mexico forecast system (WRF/CMAQ)
http://www.aire.cdmx.gob.mx/pronostico-aire/
HERMESv3_GR is used as the emission core in several air quality forecasting systems

## Slide 14: HERMESv3_BU: Road transport
Traffic flow data
Vehicle fleet composition
Speed profiles
Emission factors
Barcelona NO2 concentration (10 m × 10 m)
Benavides et al. (2018)
00h UTC
07h UTC
12h UTC
18h UTC
R-LINE input
Meteo parameters
(temp, prec)

## Slide 15: Code Availability
HERMESv3_GR code package, test case and user guide available at a gitlab repository
Access restricted for now…but
Soon (few weeks) changed to an open source Project!

## Slide 16: marc.guevara@bsc.es

## Slide 17: Spatial regridding
Widely applicable framework for designing and adjusting the emission modelling experiment:
Combination of multiple emission inventories
Country-specific scaling factors
Country-specific masks
Manufacturing industrial NOx emissions:
North Africa
(HTAPv2.2 0.1x0.1deg)
Portugal
  (ECLIPSEv5.a, 0.5x0.5deg),
France
(TNO_MACC-iii, 0.0625x0.125deg)
Spain
(bottom-up inventory, Guevara et al. 2013)

## Slide 18: Vertical distribution
0%
10%
90%
100m
200m
1000m
ID;layers;weights
V001;100,200,1000;0,0.1,0.9
0%
4%
5%
34.75%
22.5%
33.75%
75m
140m
190m
700m
500m
1200m
Ilayer;height_magl
1;75
2;140
3;190
4;500
5;700
6;1200