## Slide 1
Seasonal climate prediction: forecast quality and multi-model combination
Francisco J. Doblas-Reyes
Thanks to Rodrigo Manzanas, José Manuel Gutiérrez (IFCA-CSIC/Univ Cantabria, Spain), Stephan Hemri, Jonas Bhend (Meteoswiss), Nube González-Reviriego, Isadora Jiménez, Llorenç Lledó, Raúl Marcos, Albert Soret, Marta Terrado, Verónica Torralba (BSC)
Milan, 17 January 2019

## Slide 2: Earth Sciences Department
Computational Earth Sciences
Climate Prediction
Atmospheric Composition
Earth System Services
Environmental modelling and forecasting, with a particular focus on weather, climate and air quality
~95 people
Funding from H2020, COPERNICUS, private contracts, ESA, Spanish and regional government and AXA Chair

## Slide 3: Climate and renewable energy
Renewable energy is growing fast to decarbonize the energy system.
Both energy supply and demand are strongly influenced by atmospheric conditions and its evolution over time in terms of climate variability and change.

## Slide 4: Predictability sources
Different components of the climate system act as predictability sources depending on the time scale.
However, converting predictability into actual forecast ability (skill) is not a trivial task.

## Slide 5: And the chain goes well beyond climate
Even when there is skill in the climate variables, converting it into proven usefulness for a specific application involves a complex chain.

## Slide 6: Monitoring is key: what we want to predict

## Slide 7: Products and their quality
The prediction process follows a series of steps:
Formulate a prediction from a forecast system. The exact definition of the prediction is very important.
Select the verification metrics of the prediction that allow us to adequately represent the attributes of interest and an observational reference.
Choose a comparison standard that provides a reference level (persistence, climatology or a previous forecast system).
A prediction is of high quality if it predicts the conditions observed according to some objective criterion better than a reference prediction.
The prediction has value if it helps the user to obtain some kind of benefit from the decisions he has to make.
Note that the forecast quality is valid for a specific forecast product. Different products from the same forecast system will show different forecast quality.

## Slide 8: Observational uncertainty is a big issue
Coherence of the 10-metre wind speed trends in three reanalyses (ERA-Interim, JRA-55 and MERRA) over 1981-2015 during boreal winter.
Torralba et al. (2017, ERL)

## Slide 9: What does a prediction look like

## Slide 10: What does a prediction look like
 | Start Date |  | 
 | Oct | Nov | Dec
RPSS | 0.35 | 0.39 | 0.35
CRPSS | 0.14 | 0.11 | 0.14
Corr | 0.55 | 0.54 | 0.51
DJF wind speed predictions starting on the first of October, November and December for the first trimester of 2015, ECMWF SEAS5, reanalysis: ERA-Interim, hindcasts over 1993-2015.

## Slide 11: Forecast quality, calibration, multi-model
Forecast quality assessment:
  Verification procedure of existing forecast systems based on scoring rules (e.g. RPS for multi-category probabilities, CRPS for ensembles)
  Products, and not data, are verified; forecast products are scrutinised
Calibration (or bias adjustment)
  All bias correction and recalibration methods effectively remove bias
  Added value of sophisticated methods (e.g. EMOS) small to inexistent due to limited hindcast length (and low skill)
Multi-model combination
  No forecast system consistently outperforms others
  Multi-model combination is beneficial
  Avoid the temptation of identifying inadequate data sources to e.g. discard “bad” forecast systems.

## Slide 12: Bias adjustment and forecast quality
Skill of JJA temperature from ECMWF SEAS5 + recalibration: CRPSs of JJA near-surface temperature from, ECMWF SEAS 5 initialized in May, calibrated with the climate-conserving recalibration (CCR) and verified against ERA Interim for 1993-2014.
Better
than constant climatological forecast
Worse

## Slide 13: Bias adjustment and forecast quality
CRPS of DJF temperature from several systems with different bias adjustment methods, bias adjusted and verified against ERA Interim for 1993-2014.
Manzanas et al. (2019, Climate Dynamics)

## Slide 14: Bias adjustment and forecast quality
RPS of DJF temperature from several systems with different bias adjustment methods, bias adjusted and verified against ERA Interim for 1993-2014.
Manzanas et al. (2019, Climate Dynamics)

## Slide 15: Multi-model predictions: how to

## Slide 16: Multi-model and forecast quality
CRPSS of JJA temperature from ECMWF SEAS 5, Météo-France System 5, MetOffice GloSea5, initialized in May, all systems recalibrated with CCR and weighted (RMSE) averaging of forecast PDF and verified against ERA Interim for 1993-2014.
Better
than constant climatological forecast
Worse

## Slide 17: Bias adjustment and forecast quality
Skill of JJA temperature from ECMWF SEAS5 + recalibration: CRPSs of JJA near-surface temperature from, ECMWF SEAS 5 initialized in May, calibrated with the climate-conserving recalibration (CCR) and verified against ERA Interim for 1993-2014.
Better
than constant climatological forecast
Worse

## Slide 18: Multi-model and forecast quality
CRPSS of DJF temperature from ECMWF SEAS 5, Météo-France System 5, MetOffice GloSea5, initialized in November and verified against ERA Interim for 1993-2014.
Hemri et al. (2019)

## Slide 19: Illustrating prediction value
Gamification is useful to illustrate the challenges of using and the value of seasonal climate predictions:
Play against a reference taken from climatological frequencies.
The bets are proportional to the predicted probabilities.
The amount invested in the observed category is multiplied by three.
play.google.com/store/apps

## Slide 20: Illustrating prediction value
Examples of return ratio for 33 betting runs for different points where wind power plants are installed:
Top row cases with RPSS=0, but ignorance skill score negative or zero.
Bottom row cases with RPSS>0.
Line for the geometric average of return ratios (interest rate).
Terrado et al. (2019, BAMS)

## Slide 21: Elements involved in the prototype development
co-design & co-development
Sci-tech. development
Market development
Real-time forecasts improvement
Model skill improvement
Development of real-time forecasts
Case studies modelling
1st DST pilot
2nd DST pilot
3rd DST pilot
Map user needs
Evaluation of forecasts operational performance
Business model development
DST services dissemination
Economic impact assessment
Build case studies

## Slide 22: Operational prototype: the DST
www.bsc.es/ESS/resilience

## Slide 23: BSC, from research to services
Scientific
user-driven
research
User
engagement
Users
Industrial partners
Administrations
International
organisations
Research centres
Meteorological
Centers
Participatory approaches
Case studies for specific needs
and more…

## Slide 24: A twist to the idea: event attribution
During the first quarter of 2015 the United States experienced a widespread and extended episode of low surface wind speeds. This episode had a strong impact on wind power generation. Some wind farms did not generate enough cash for their steady payments, and the value of wind farm assets decreased.
Wind speed anomalies reflecting the wind drought over the United States for the first trimester of 2015, where the USA wind-farm fleet is also shown (Lledó et al., JGR 2018)

## Slide 25: Summary
Forecast quality assessment:
  No prediction should be considered without its corresponding verification.
  Products, and not data, are verified. Always define a product.
Bias adjustment:
  All bias adjustment methods effectively remove bias.
  Simpler methods tend to work best, and the chosen method should be carefully assessed.
  Correlation of the direct model output is not a good measure of the actual skill of a product.
Multi-model combination
  Multi-model combination is beneficial, although weighting the best systems is not a trivial exercise.