## Slide 1: European air quality with the online multiscale MONARCH v2.0 Model
Oriol Jorba, Sara Basart, Jaime A. Benavides, Francesco Benincasa, Dene Bowdalo, Matthew L. Dawson, Enza Di Tomaso, Jerónimo Escribano, María Gonçalves, Marc Guevara, Martina Klose, Francesca Macchia, Gilbert Montané, Vincenzo Obiso, Miriam Olid, María Teresa Pay, Herve Petetin, Manuel Porquet, Kim Serradell, Carles Tena, Carlos Pérez García-Pando
3/4/2019
27th GLOREAM Workshop, 1-3 April 2019, Norrköping, Sweden
Atmospheric Composition Group
Earth Sciences Department of BSC
Notes: In this talk, I will present an update of the work done with the in-house MONARCH air quality model to predict the air quality at the European scale.
MONARCH is a group project with around 20 people involved with different profiles.

## Slide 2
Notes: Where MONARCH was born? The Earth Sciences Department @BSC
BSC-ES objective: has as main objective doing research on climate and atmospheric composition.
Tools: We maintain air quality forecasts and climate prediction systems both for research and services deployment.
Indeed, there is a third group in the Department doing the transition of our research outcomes to other economic sectors like in energy or urban development, the Earth System Services group.

## Slide 3
CALIdad del aire Operacional Para España (CALIOPE)
Multiscale models from regional to local scales
In the media
Web / App
12km
4km
1km
Benavides et al. (2019 GMDD)
Pay et al. (2014 GMD)
Baldasano et al. (2012 AE)
Pay et al. (2011; 2012 AE)
Notes: When: The Department runs an air quality forecast system, named CALIOPE, since 2006 (around 13 years). It’s based on the WRF meteo model, the CMAQ, and HERMES.
Objective: The CALIOPE’s objective is to provide air quality forecast in: (1) Spain and hot spots areas at 1km with nesting of the mesoscale models and (2) urban areas with CALIOPE urban model.
Free products: Since the begging CALIOPE products has been disseminated without restriction through the website.
Main users so far: national and regional administration, citizen, and the media.
3

## Slide 4
Mineral dust services
WMO Dust Centers
Barcelona Dust Forecast Center.
Unique specialized WMO Center for
mineral dust prediction in Europe
http://dust.aemet.es
started in 2014 - Operations
MONARCH is the reference model
SDS-WAS. North Africa, Middle East and Europe
Regional Center.
http://sds-was.aemet.es
started in 2010 – Research
MONARCH is contributing to the model ensemble
Notes: An important area of work in our department is the deployment of mineral dust services.
Our department is managing this task in collaboration with the Spanish metoffice under the mandate of the WMO.
Two main centers have been established
1) the Barcelona Dust forecast center, is a unique WMO center specialized in providing operational mineral dust forecast for the Northern Africa, Middle East and Europe domain since 2014. The main objective of the center is to provide operational mineral dust forecasts with the MONARCH model, previously known as NMMB/BSC-Dust.
2) The second center, mainly focused in research activities, is the Sand and Dust Storm Warning Advisory and Assessment System. It maintains a research ensemble forecast based on 11 models.
MONARCH is the reference model in the operational centre and contribute to the ensemble in the warning alert system.

## Slide 5: CAMS_50.II: Regional production*
Products
NRT Individual & Ensemble 4-Day Forecasts
NRT Individual & Ensemble Analyses (DD-1)
NRT Validation & Statistics products
Reanalyses (2014-2017)
Inputs
Global products
Regional emissions
In situ observations
New operational AQ models
New candidates AQ models
7 operational AQ models
*CAMS_50.II: Augustin Colette’s presentation yesterday
Notes: Another important project in which we are involved is the air quality regional production for the Copernicus Atmosphere Monitoring Service, in this second phase of CAMS50 that started last October.
Involvement: Our group is involved with the participation of the MONARCH model as a new candidate model to be part of the multi-model ensemble of regional CAMS (set by 9 models) in three years.
Objective: Our efforts are focused to adapt our system to the CAMS50 requirements and make the ensemble more robust (in terms of uncertainty and reliability). We are not committed to be operational, but be ready to it at the end of the project.

## Slide 6
MONARCH: online weather-chemistry model
Fully on-line coupling: weather-chemistry feedback processes
In-house developed.
Multiscale: global to regional (up to 1km) scales (nesting capabilities)
Enhancement with a data assimilation system
The AEROSOL module includes a dust module known as NMMB/BSC-Dust
Multiscale Model from Global to Local Scales
Notes: MONARCH is a fully on-line coupled meteorology – chemistry model with the option to solve feedback processes.
The meteorological driver is the NCEP NMMB
The chemistry and aerosol schemes are in-house implemented and developed.
Motivation:
  (1) further development of mineral dust model dream (since 2006) towards to fully couple online meteo-chem system (since 2008),
  (2) extend the area of application from regional to global scales.
It runs from global to regional domain up to 1km with telescoping nesting capability.
Data assimilation system for aerosols based on the EnKF approach.
6

## Slide 7: *HERMESv3: emission model
An open source, parallel and stand-alone multiscale atmospheric emission model that processes and estimates gas and aerosol emissions for use in chemistry transport models
global-regional module
(HERMESv3_GR)
bottom-up module
(HERMESv3_BU)
A highly customizable processing system that calculates emissions through an automatic combination of existing inventories and user defined vertical, temporal, speciation scaling and masking factors
A Spanish emission model to estimate emissions at the source level (e.g. road link, industrial facility, crop type) combining state-of-the-art bottom-up methods with local activity and emission factors
*HERMESv3: Marc Guevara’s presentation yesterday
Notes: The emissions used in MONARCH are based on the last version of HERMESv3 (presented yesterday by Marc Guevara).
MONARCH uses HERMES for anthropogenic and some natural emissions. Meanwhile for biogenic emissions it uses MEGAN.
At global/regional scale, HERMES estimate emissions fluxes from a combination of existing inventories.
At the Spanish level, it estimates emissions based on a bottom-up approach.

## Slide 8
MONARCH forecasts
MONARCH contributes to the ICAP global forecast aerosol multi-model ensemble http://icap.atmos.und.edu
Global
Regional
CALIOPE (www.bsc.es/caliope)
AQ Forecast System for EU and Spain
BDFC and SDS-WAS dust forecast
Candidate model CAMS_50.II
It will be implemented in
20100715 at 12UTC
And more products in: http://www.bsc.es/ess/
Notes: This diagram summaries the ongoing forecast activities conducted by our group with MONARCH.
At the global scale, MONARCH is providing aerosol forecast for the ICAP (International Consensus on Aerosol Prediction) initiative, an international forum for global aerosol forecast.
At regional scale, MONARCH is a consolidated system providing mineral dust services as mentioned before.
For regional air quality services, it is as a candidate of the CAMS_50.II ensemble and the replacement of the meteo and chem modules in the CALIOPE system for Spain. In this presentation we show the assessment of MONARCH for both purposes.

## Slide 9: MONARCH Experiment Configurations
 | New model CALIOPE (European domain) | New candidate model CAMS_50.II (Europe)
Year | 2015 | 2016
Domain | 0.1º x 0.1º 48 layers (50hPa) | 0.2º x 0.2º 48 layers (50hPa)
Gas chemistry | CB05 (extended with TU and CL chemistry) | 
Aerosols | Primary (dust, sea salt, BC, POM, PSO4, PNO3, PNH4), SIA (EQSAM), SOA (2-product scheme) | 
Emissions | HERMESv2: EMEP2014 GFASv1.2 MEGANv2.04 | 1HERMESv3 (gr): CAMS-REG-AP_v2.1.1-2015 + CAMS-GLOB-2015 (ANTv2.1, SHIPv1.1, OCENv1.1, SOILv1.1) + GFASv1.2 MEGANv2.04
IC-BC | GFS/NCEP (met) - C-IFS (gas) | GFS/NCEP (met) - C-IFS (gas+aero)
Evaluation method | EIONET validated | EBAS with quality control flags2 CAMS ens. + individ. models3.
2Quality control flags: Dene Bowdalo’s presentation
1HERMESv3: Marc Guevara’s presentation yesterday
3CAMS_50.I
Notes: This table shows the different configuration of MONARCH experiments to forecast air quality for the project CALIPOE and CAMS. (in the future efforts will converge to the same configuration)
The MONARCH configuration in the CALIOPE project tried to follow the configuration of the current system and started 1 year ago and set 2015 as a reference year.
The MONARCH configuration for CAMS are defined by the project and it focused on the year 2016.
Domain
Gas phase and aerosols
Emissions.
IC-BC: Copernicus global forecasting system C-IFS. Global forecast of the National Centers of Environmental Prediction (GFS/NCEP). The coupling of MONARCH with the IFS/ECMWF is still under development, and here we presents only results using GFS data.
Evaluation method: quality control of the measurements that take into account the measurement technique, redundancy, detection limit by technique, calibration problems.

## Slide 10: MONARCH vs CALIOPE Period: full year 2015

## Slide 11: MONARCH vs CALIOPE: annual cycle Period: full year 2015
MONARCH
MONARCH
CALIOPE (WRF-CMAQ)
EIONET 2015 validated (rural, suburban, urban)
958 stations (O3)
774 stations (NO2)
Notes: Time series of the distribution of the O3 (first row) and NO2 (second row) concentrations by monthly chunks for observation in grey and models in red (MONARCH on the left and CALIOPE on the right).
Note that both models used C-IFS, same emission and BC.
Validated EIONET measurements for all stations type.
For O3, MONARCH shows lower bias than CALIOPE. Both agree in showing lowest bias in warmer months, when O3 chemistry is enhanced, and higher bias in cold months when long-range transport control O3 concentration.
  Note the better skills of MONARCH reproducing the annual cycle.
For NO2, both models show positive bias, higher in winter than in summer.

## Slide 12: MONARCH vs CALIOPE: station category Period: full year 2015
O3 (958 EIONET stations)
MONARCH
CALIOPE (WRF-CMAQ)
NO2 (774 EIONET stations)
PM2.5 (374 EIONET stations)
Correlation
MB
Obs mean
Mod mean
RMSE
Notes: The evaluation of the models according the station type provide more insight in the model behavior.
Plot shows by category (all, rural, suburban and urban), the different statistics (correlation-star, MB-diamond, Mod mean-filled dot, Obs mean-empty dot, color box RMSE), read color indicates MONARCH, blue color is for CALIOPE.
For O3:
  Correlation doesn’t change to much between models neither station category (0.6-0.7), although it is slightly higher for MONARCH than for CMAQ.
  Main different pattern between models are shown in MB. They are higher in CMAQ than in MONARCH, more positive and higher absolute value.
  MONARCH shows lower RMSE than CMAQ with a very well balanced MB.
For NO2:
  Correlation does not change between station category. Higher correlation for CMAQ than for MONARCH.
  MB increases when moving from rural to urban in both models. MONARCH tends to slightly overestimate NO2 in rural stations compared with CMAQ, while for suburban and urban both models underestimate.
  RMSE does not change too much between models.
For PM2.5:
  Both models underestimates in all the categories
  RMSE is very similar for both models, being slightly larger in MONARCH for rural stations.
  The correlation is significantly lower in MONARCH than in CMAQ.
  This results show that there’s still improvements to do in MONARCH with particles, specially in secondary organic aerosols.

## Slide 13: MONARCH vs CAMS_50 Period: July-August 2016

## Slide 14: MONARCH vs CAMS: O3 Period: 20160801-20160901
MONARCH
(113 EBAS stations)
MB (ppb)
PCC
MB (ppb)
PCC
CAMS_ENS
(113 EBAS stations)
Notes: EBAS stations: rural background
For O3 MB:
  MONARCH shows lower MB than CAMS_ens: median ~2ppb vs. 5ppb, especially shown in the northern countries.
  Both systems agree on having highest MB in high altitude stations near big mountains.
For O3 PCC:
  Still CAMS_ens shows higher PCC than MONARCH: median ~0.7 vs. 0.6, but spatial distribution is very similar in both systems.

## Slide 15: MONARCH vs CAMS: O3 daily cycles Period: 20160801-20160901
Mo : conc observations (ppb), Mm : conc model (ppb), MB : mean bias (ppb), NMB : normalized mean bias (%), NRMSE : normalized RMSE (%), PCC: correlation coefficient.
113 EBAS stations
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
Notes: MONARCH in read, ensemble in green, individual CAMS ens in blue colours. Individual models’ names are hidden
Errors (absolute and relative): MONARCH shows errors which are in the range of the individual models and the ens.
Bias (absolute and relative):
  MONARCH shows less overestimation than the individual models and the ensemble.
  Main problem in the early morning (~6 am)
PCC close to the ensemble, but slightly lower, within other models.
Overall, MONARCH shows very good results for O3 for this two month period.

## Slide 16: MONARCH vs CAMS: NO2 daily cycles Period: 20160801-20160901
6 EBAS stations
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
Mo : conc observations (ppb), Mm : conc model (ppb), MB : mean bias (ppb), NMB : normalized mean bias (%), NRMSE : normalized RMSE (%), PCC: correlation coefficient.
Notes: MONARCH in read, ensemble in green, individual CAMS ens in blue colours.
Errors (absolute and relative): upper range of the individual models. Although the shape of that daily cycle error is similar to the other models
  MONARCH is in the.
  As seen in 2015 results, MONARCH tends to overestimate NO2 in rural stations but this performance is changed in suburban and urban, where the model understimates NO2.
Bias (absolute and relative):
  MONARCH shows general overestimation, in the whole cycle, and higher bias than the individual models and the ensemble.
  MONARCH highest overestimations in the early morning (~3-6 am) collocated with the O3 understimation.
  Our current hypothesis for this behaviour are: too strong nocturnal stable conditions (low winds, low PBL), impact of new emissions like soil NO, or diffusion of the model under stable conditions.
PCC close to the ensemble at night, but slightly lower during the rest of the day.
NOTE: Rural background stations, low concentrations (high NMB and NRMSE). Need for further analysis on urban -suburban stations.

## Slide 17: Conclusions
We have assessed the performance of the online multiscale MONARCH v2.0 Model to forecast the air quality in Europe in the context of CALIOPE and CAMS_50.II
MONARCH performance for O3
  Better skills than CALIOPE (WRF-CMAQ)
  In the range of other CAMS_50 models.
MONARCH performance for NO2
  General overestimation in rural stations.
  Underestimation near urban stations.
MONARCH performance for PM
  General underestimation, more important in PM10 than in PM2.5
  Ongoing work in SOA formation may reduce the bias.
The replacement inside CALIOPE system foreseen during 2019.
Next tasks within CAMS_50.II:
  Coupling with IFS forecast initial and boundary conditions.
  Rerun 2016
  Expand the evaluation analysis with EIONET stations with quality control flags.
Notes: General overestimation in rural stations (not a limitations or critical issue).

## Slide 18
Acknowledgments
The research leading to these results has received funding from
the Ministerio de Economía y Competitividad (MINECO) as part of the PAISA project CGL2016-75725-R.
the Copernicus Atmosphere Monitoring Service (CAMS50 Phase II), a programme being implemented by the European Centre for Medium-Range Weather Forecasts (ECMWF) on behalf of the European Commission.
We acknowledge PRACE for awarding access to MareNostrum 4 based in Spain at the Barcelona Supercomputing Center through the eFRAGMENT project.
Thank you!