## Slide 1: Models de pronòstic d’ozó troposfèric
María Teresa Pay, Oriol Jorba, Marc Guevara, Miriam Olid, Kim Serradell, Carles Tena, Carlos Pérez García-Pando
Earth Sciences Department – Atmospheric Composition Group
Colaboradores externos:
X. Querol (CSIC), S. Napelenok (U.S. EPA), G. Gangoiti (Uni. Vasc Country)
Barcelona
13 mayo 2018

## Slide 2: Outline
The Earth Sciences Department
Air quality forecast system: CALIOPE
Improvements in the O3 modelling
Tools for the diagnosis of O3
Conclusions
O3 modelling

## Slide 4: Air quality forecast system: CALIOPE

## Slide 5
CALIdad del aire Operacional Para España (CALIOPE)
Multiscale models from regional to local scales
In the media
Web / App
12km
4km
1km
Benavides et al. (2019 GMDD)
Pay et al. (2014 GMD)
Baldasano et al. (2012 AE)
Pay et al. (2011; 2012 AE)
Notes: 5

## Slide 6: CALIOPE: main elements
METEOROLOGICAL FORECAST
NCEP GLOBAL SIMULATIONS
WRF-ARWv3.5.2
12 km x 12 km
IC/BC
nesting
WRF-ARWv3.5.2
4 km x 4 km
EMISSION FORECAST
HERMESv2.0-DIS
12 km x 12 km
HERMESv2.0-BOUP
4 km x 4 km
Meteo. fields
EMEP inventory
AIR QUALITY FORECAST
CMAQv5.0.2
4 km x 4 km
CMAQ v5.0.2
12 km x 12 km
NCAR MOZART4
1.9 º x 2.5º
Meteo. fields
nesting
Emis. fields
DESERT DUST FORECAST
BSC-DREAM8b
50 km x 50 km
AIR QUALITY PRODUCTS

## Slide 7: The CALIOPE project
2006-2010: Start-up of the air quality forecast system for Spain at 4 km.
Funding:
2010-2014: Dedicated domains over Andalucia, Catalunya and Madrid at 1-km resolution.
Funding:
Since 2015 (without funding):
  The 1-km resolution domains only on demand.
  Generation of adapted products on demand.
  Interaction with users to learn from their experience and create specific products adapted to their needs.
2006-2010
2010-2014
2015

## Slide 8: Air quality forecast for Catalonia (www.bsc.es/caliope)
Servei de Vigilància i Control de l’Aire
Daily monitoring and detection of pollution episodes in all parts of the territory.
Activation of warning protocols for pollution episodes (e.g. reports).
Complementary tool to other air quality forecast systems.

## Slide 9: Air quality forecast for Catalonia (www.bsc.es/caliope)

## Slide 10: Air quality forecast for Catalonia (www.bsc.es/caliope)
1-6
Max 24h -2/08
Max: 180-190 µg/m3
Max 24h -17/08
Max: 120-130 µg/m3

## Slide 11: Air quality forecast for Catalonia (www.bsc.es/caliope)

## Slide 12: On going works to improve the O3 modelling

## Slide 13: HERMESv3
A python-based, open source, parallel and multiscale emission modelling framework that processes and estimates gas and aerosol emissions for use in atmospheric chemistry models.
Guevara et al. (2019, GMDD)

## Slide 14: HERMESv3_BU: Bottom-up module
An emission model to estimate emissions at the source level (e.g. road link) combining state-of-the-art bottom-up methods with local activity and emission factors

## Slide 15: MONARCH: online weather-chemistry model
Fully on-line coupling: weather-chemistry feedback processes
In-house developed.
Multiscale: global to regional (up to 1km) scales (nesting capabilities)
Data assimilation system
CGL2006-11879/CLI, CGL2008-02818/CLI, CGL2010-19652, CGL2013-46736-R1, CSD2007-0050, SEV-2011-00067, now with ERC-FRAGMENT
Funding:
Notes: 15

## Slide 16
Mineral dust services
WMO Dust Centers
Barcelona Dust Forecast Center.
Unique specialized WMO Center for
mineral dust prediction in Europe
http://dust.aemet.es
started in 2014 - Operations
MONARCH is the reference model
SDS-WAS. North Africa, Middle East and Europe
Regional Center.
http://sds-was.aemet.es
started in 2010 – Research
MONARCH is contributing to the model ensemble

## Slide 17: Copernicus Atmosphere Monitoring Service Regional air quality (CAMS_50.II)
Products
NRT Individual & Ensemble 4-Day Forecasts
NRT Individual & Ensemble Analyses (DD-1)
NRT Validation & Statistics products
Reanalyses (2014-2017)
Inputs
Global products
Regional emissions
In situ observations
New operational AQ models
New candidates AQ models
7 operational AQ models

## Slide 18: MONARCH vs CALIOPE: annual cycle Period: full year 2015
MONARCH
CALIOPE (WRF-CMAQ)
EIONET 2015 validated (rural, suburban, urban)
958 stations (O3)
774 stations (NO2)

## Slide 19: MONARCH vs CAMS: O3 Period: 20160801-20160901
113 EBAS stations

## Slide 20: Tools for the diagnosis of O3

## Slide 21: Who is responsible of the O3 exceedances?
Source apportionment
Which are the economic activities (sectors) responsible for high O3?
Where do the precursors responsible for O3 exceedances come from (regions)?
1

## Slide 22: O3 source apportionment in the Iberian Peninsula Pay et al., 2019. Atmos. Chem. Phys. 19, 5467–5494
Imported O3
Contributions: anthropogenic emissions + imported O3
Sectors accounting 92% of the total NOx
This presentation
#exceedances
O3 episode: 21-31 July 2012

## Slide 23: Unravelling total O3
p90 O3 for 31 Jul 2012
Others
Imported
On-road
Non-road
Power Plants
Industry
p90 O3 contributions for 31 Jul 2012
µg/m3
Total
µg/m3

## Slide 24: Unravelling total O3: Catalonia region
Daily mean contribution in exceedances (MDA8 > 120 µ/m3)
Episode (21-31 July 2012)
MDA8 = maximum daily 8-hour averaged

## Slide 25: Unravelling total O3: Palau Reial
Receptor: urban station (3)

## Slide 26: Unravelling total O3: Montseny
Receptor: rural station (4) - Montseny
High model performance at rural background stations (bias = 4.5µg/m3 and r= 0.7)

## Slide 27: Vertical distribution of O3
Main contributor to concentration overall (background levels).
Processes: advection + vertical mixing.
E
W
E
W

## Slide 28: Conclusions
1. Models together with observations provide complementary and necessary information for the diagnosis and prediction of O3 episodes.
2. The improvement of models is necessary to improve the diagnosis of O3:
  2.1 Emissions | Regular update of the emissions inventories and estimation methodologies: speciation of VOCs from industry and solvents, biogenic VOCs, and soil NOx.
  2.2. Meteorology | Improvement of the stratification in stagnant conditions and mesoscale phenomena (sea breezes and thermal circulation).
  2.3. Chemistry | Coupling with the meteorological model and improvement of the chemical mechanisms.
3. The new sources contribution techniques allow:
  3.1 Estimate the dominant regional/local contribution in episodes of O3. Next: Identify key emission sectors.
  3.2. Estimate imported O3 to the Iberian Peninsula, which, on average, contributes significantly to O3 levels in summer (background). Next: Quantify the relative importance of imported vs. regional/local O3.

## Slide 29
Acknowledgments
Spanish Ministry of Economy and Competitiveness (PAISA , CGL2016-75725-R).
“Red Española de Supercomputación” (AECT-2017-1-0008).
PRACE for awarding access to MareNostrum 4 through the eFRAGMENT project.
The Copernicus Atmosphere Monitoring Service (CAMS50, CAMS81) on behalf of the European Commission.
AXA Research Fund.
References:
Pay, M.T., Gangoiti, G., Guevara, M., Napelenok, S., Querol, X., Jorba, O., Pérez García-Pando, C. A source apportionment assessment of ozone concentrations in peak summer events over the Iberian Peninsula. Atmos. Chem. Phys., 19, 5467 -5494, 2019
Guevara, M., Tena, C., Porquet, M., Jorba, O., and Pérez García-Pando, C.: HERMESv3, a stand-alone multiscale atmospheric emission modelling framework – Part 1: global and regional module, Geosci. Model Dev. Discuss., in review, 2019
Thank you!