## Slide 1: Perspectives on modeling dust mineralogical composition and its effects upon climate
24.09.2019
18th AEROCOM Workshop, Barcelona
Carlos Pérez García-Pando
Acknowledgements:
EMIT and FRAGMENT TEAMS

## Slide 2: Dust mineralogy and climate
RADIATION
CHEMISTRY
CLOUDS
hematite
BIOAVAILABLE IRON

## Slide 3: Shortwave forcing
Moosmüller et al. (2012)
Iron oxides
Hematite

## Slide 4: Longwave forcing
Di Biagio et al. (2017)
Calcite
Quartz

## Slide 5: Heterogeneous chemistry
Krueger et al. (2004)
dolomite
Nitrate salt

## Slide 6: Ice nucleation and mixed-phase clouds
Atkinson et al. (2017)
K-Feldspar

## Slide 7: Iron mineralogy and solubility
Shi et al. (2011)
FeA: amorphous and/or poorly crystalline and nanoparticulate Fe (ascorbate Fe)
FeD: crystalline Fe(III) oxides, mainly goethite and hematite (dithionite Fe)
FeT: Total Fe including Structural Fe (FeSt)

## Slide 8: Motivation
IPCC Key
Uncertainty
Earth System Models neglect
dust mineralogical composition variations
Constrain the global dust mineralogical composition
Understand and calculate its effects upon climate
SOIL MINERAL CONTENT?
EMISSION?
CLIMATE EFFECTS?
RADIATION
CHEMISTRY
CLOUDS
hematite
BIOAVAILABLE IRON

## Slide 9: Mapping of soil-surface mineralogy
Claquin et al., 1999; Journet et al., 2014
Currently 12 key minerals estimated
700 soil descriptions sampling 55 % of FAO soil units
Many regions including prolific sources not sampled
Massive extrapolation based on soil unit/type
A number of assumptions to overcome the lack of data: for example on hematite and goethite size
Soil analysis based on wet sedimentation (“wet sieving”), which breaks the aggregates found in undispersed soils subject to wind erosion.
FAO soil types or units
Sieves for mechanical analysis
Soil Hydrometer apparatus

## Slide 10: Space borne hyperspectral imaging spectroscopy
Hyperion: satellite hyperspectral sensor 0.4 to 2.5 μm, 242 spectral bands, 10nm spectral resolution, 30 m spatial with a SNR of ~50:1
VSWIR Spectra of Dust Source Minerals
AVIRIS airborne scenes
0.4–2.5 μm, 224 bands, 10 nm spectral resolution, SNR of ~500:1
Coming soon (2021)!!!
NASA FUNDED
EMIT
Earth Surface Mineral Dust Source Investigation
90.000 scenes

## Slide 11: EMIT
ISS Coverage
52° S
52° N

## Slide 12: EMIT

## Slide 13: Mineral Mapping Test in the Salton Sea, CA Dust Source Region
AVIRIS imaging spectroscopy measurements of the Salton Sea region in Southern California acquired as part of the 2014 NASA HyspIRI airborne campaign.
Hematite
Goethtite
Carbonates
Clay Minerals
Illite

## Slide 14: Existing FAO Mineralogy versus Imaging Spectroscopy
FAO Based Minerals
VSWIR Spectroscopy
Comparison

## Slide 15: EMIT Target Areas are focused in the Arid Land Regions
These occur under the orbit of the ISS.

## Slide 16: Emission of dust minerals
Emitted PSD of dust minerals is key to quantifying their climate effect
Dust emission mechanisms (Shao et al. 2008)
Without consideration of mineralogy:
Incomplete understanding of the physics
Paucity and incompleteness of measurements
Lack of (realiable) input data at global scale (e.g. soil PSDs)

## Slide 17: Emission of dust minerals
Emitted PSD of dust minerals is key to quantifying their climate effect
Incomplete understanding of the physics
Paucity and incompleteness of measurements
Lack of (realiable) input data at global scale (e.g. soil PSDs)
Complete lack of experimental studies tackling the relationship of the emitted PSD and soil-surface mineralogy
Internal and external mixtures of different minerals important for climate impacts
Dust emission mechanisms (Shao et al. 2008)
With consideration of mineralogy:

## Slide 18: Emitted PSD and mineralogy in models
Kok (2011)
Brittle Fragmentation Theory auspicious for mineralogy as it is based on the soil dispersed PSD
Scanza et al. (2015)
Perlwitz et al., 2015 (a,b)
Pérez García-Pando et al., (2016)
Pérez García-Pando et al., in prep

## Slide 19
Realistic dust size
Distribution
No aggregate
reconstruction
Estimating mineral size
Distributions
Aggregate reconstruction
and fragmentation
Observations

## Slide 20: FRAGMENT: FRontiers in dust minerAloGical coMposition and its Effects upoN climaTe
Role of mineralogy
Global soil mineral content
Mixed-phase
warm
Radiation, Chemistry and Clouds
wind
FRAGMENTation of aggregates
Emission of minerals
Theory
+
field campaigns
+
Laboratory analyses
Field and Lab
+
Airborne spectroscopy
+
Space-borne spectroscopy
EMIT
Modelling
+
State-of-the-art
+
New methodologies
EMIT

## Slide 21: Emitted PSD of minerals
Understand emitted PSD of minerals and relationship with parent soil
Extend theoretical framework(s) and produce global model scheme
FRAGMENT Carlos Pérez García-Pando
QUARTZ
FELDSPAR
CALCITE
IRON OXIDES
GYPSUM
PHYLLOSILICATES
c
D(m)
dV/dlnD
Field campaigns
Laboratory
Theory
Atmospheric Forcing
Size-segregated and composition resolved dust fluxes
Size-segregated and composition resolved dry and wet soil

## Slide 22: Global soil-surface mineralogy
Point and field spectrometers
Lab spectroscopy of soil and aeolian samples
Tetracorder Spectral Identification and Mapping
Linking to size and composition resolved measurements relevant to theories of dust PSD
Constrain global soil-surface mineralogy
Link spectroscopy of soil-surface to dust emission
Field and lab
spectroscopy
Airborne
Spectroscopy
Space-borne
Spectroscopy
AVIRIS (US)
EMIT
SUPPORT and TIMELY
IMPACT EMIT

## Slide 23: Field Campaigns: Where, Why and When?
Testing in Aragón, Spain 2019
Salton Sea and surroundings, US 2020
Icelandic sources (HiLDA!) 2020
M´Hamid, Zagora, Morocco 2019 (ONGOING)
……Erfoud, Morocco in 2021

## Slide 24: Field Campaigns: What?
Atmospheric forcing
2D wind and temp profiles, 3D wind, turbulence, pressure
Radiative fluxes
Soil-surface humidity
RH close to the ground
Precipitation
Soil sampling, surface spectroscopy and lab analyses
Soil-surface sampling
Surface composition (based on reflectance spectra + tetracorder)
Dry soil aggregate stability, crust strength
PSD in wet and dry dispersion of soil and saltation samples
Size-resolved mineralogy, chemistry, morphology and mixing state of soil, saltation and dust samples (XRD, TEM, BSED,..)
Composition of soil and aeolian samples and sub samples based on spectroscopy
Sand and Dust
Time- and size-resolved vertical number and mass fluxes
Size-segregated samples of suspended dust (compositional fluxes)
Saltation flux (time/size resolved and bulk) – active and passive
Absorption and scattering

## Slide 25
Results of ultrasound sieving in Zaragoza
Chart: microns
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10
 | 42.4742 | 13.9002 | 11.3972 | 11.5712 | 12.6955 | 1.6691 | 3.0377 | 1.5826 | 1.5469 | 0.1254
 | 46.7467 | 13.2357 | 10.1321 | 8.9324 | 10.9005 | 2.7585 | 3.62 | 1.6556 | 1.9583 | 0.060048
Chart: microns
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10
 | 2.1931 | 1.3565 | 1.3452 | 2.0687 | 14.6507 | 7.0314 | 8.1393 | 10.8524 | 8.4332 | 43.9295
 | 2.1931 | 1.3565 | 1.3452 | 2.0687 | 14.6507 | 7.0314 | 8.1393 | 10.8524 | 8.4332 | 43.9295
 | 1.0038 | 0.62735 | 0.47679 | 1.5056 | 9.2095 | 3.8896 | 7.2773 | 11.5433 | 10.941 | 53.5257
 | 2.4836 | 1.5805 | 1.0386 | 2.5062 | 14.089 | 5.7349 | 9.9571 | 10.7473 | 7.7218 | 44.1409

## Slide 26
Chart: µm
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10 | <1000
Illite-Musc | 5.1 | 5 | 5.8 | 7.7 | 5.1 | 7 | 3.7 | 4.7 | 10.2 | 4.8385 | 4.3
Kaol-Clin | 3.7 | 3.4 | 3.8 | 1.9 | 3.2 | 3.2 | 5.1 | 4.1 | 6.6 | 2.9641 | 3.1
Quartz | 27.8 | 27.1 | 26.3 | 27.4 | 27 | 29.5 | 33.2 | 33 | 19.8 | 20.5061 | 29.2
Calcite | 59.6 | 60.8 | 59.3 | 58.7 | 61.3 | 56.5 | 53.5 | 54.8 | 58.8 | 64.831 | 58.9
Dolomite | 1.2 | 1.6 | 2.2 | 1.6 | 1.3 | 1.6 | 1.7 | 1.3 | 1.6 | 2.4909 | 1.6
Halite | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.1 | 0.10379 | 0
Gypsum | 0.1 | 0.1 | 0.1 | 0 | 0 | 0 | 0.1 | 0.1 | 0.2 | 0 | 0.4
Microcline | 0.7 | 0.3 | 0.8 | 0.6 | 0.5 | 0.6 | 0.5 | 0.9 | 0.9 | 1.4945 | 0.6
Ab-An | 1.7 | 1.5 | 1.6 | 1.8 | 1.5 | 1.3 | 1.4 | 0.8 | 1.5 | 1.5257 | 1.5
Hematite | 0 | 0 | 0 | 0 | 0 | 0.3 | 0.4 | 0.2 | 0.3 | 0.62272 | 0.4
Goethite | 0.1 | 0.2 | 0.1 | 0.4 | 0.1 | 0.2 | 0.3 | 0.1 | 0.2 | 0.62272 | 0
Chart: µm
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10 | <1000
Illite-Musc | 5.1 | 5 | 5.8 | 7.7 | 5.1 | 7 | 3.7 | 4.7 | 10.2 | 4.8385 | 4.3
Kaol-Clin | 3.7 | 3.4 | 3.8 | 1.9 | 3.2 | 3.2 | 5.1 | 4.1 | 6.6 | 2.9641 | 3.1
Quartz | 27.8 | 27.1 | 26.3 | 27.4 | 27 | 29.5 | 33.2 | 33 | 19.8 | 20.5061 | 29.2
Calcite | 59.6 | 60.8 | 59.3 | 58.7 | 61.3 | 56.5 | 53.5 | 54.8 | 58.8 | 64.831 | 58.9
Dolomite | 1.2 | 1.6 | 2.2 | 1.6 | 1.3 | 1.6 | 1.7 | 1.3 | 1.6 | 2.4909 | 1.6
Halite | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.1 | 0.10379 | 0
Gypsum | 0.1 | 0.1 | 0.1 | 0 | 0 | 0 | 0.1 | 0.1 | 0.2 | 0 | 0.4
Microcline | 0.7 | 0.3 | 0.8 | 0.6 | 0.5 | 0.6 | 0.5 | 0.9 | 0.9 | 1.4945 | 0.6
Ab-An | 1.7 | 1.5 | 1.6 | 1.8 | 1.5 | 1.3 | 1.4 | 0.8 | 1.5 | 1.5257 | 1.5
Hematite | 0 | 0 | 0 | 0 | 0 | 0.3 | 0.4 | 0.2 | 0.3 | 0.62272 | 0.4
Goethite | 0.1 | 0.2 | 0.1 | 0.4 | 0.1 | 0.2 | 0.3 | 0.1 | 0.2 | 0.62272 | 0
Mineralogy of dry size fractions
Mineralogy of wet size fractions
Chart: µm
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10
Illite-Musc | 0.48149 | 1.3217 | 0.87051 | 2.2218 | 2.0569 | 1.2618 | 1.769 | 5.0382 | 13.8845 | 14.9294
Kaol-Clin | 0.42799 | 0.24922 | 0.47482 | 0.93359 | 4.1751 | 2.607 | 2.5731 | 3.1631 | 4.9379 | 5.1311
Quartz | 3.8554 | 4.3097 | 14.7907 | 39.7171 | 32.6832 | 29.0239 | 43.4476 | 32.6958 | 27.1766 | 14.2353
Calcite | 95.169 | 93.5987 | 82.7244 | 54.5611 | 55.181 | 58.9499 | 47.8862 | 53.2872 | 49.1158 | 61.6188
Dolomite | 0.011672 | 0.15487 | 0.32446 | 0.3501 | 1.0148 | 2.2556 | 1.2791 | 1.4469 | 1.3482 | 1.8005
Halite | 0 | 0 | 0.092326 | 0.071815 | 0.011163 | 0.015642 | 0.01496 | 0.039147 | 0.055482 | 0
Gypsum | 0.054471 | 0.049843 | 0.083094 | 0.10682 | 0.046887 | 0.080296 | 0.068067 | 0.082209 | 0.024274 | 0
Microcline | 0 | 0.093456 | 0.25719 | 0.72712 | 1.4652 | 3.0267 | 1.3464 | 2.1727 | 1.7581 | 0.56694
Ab-An | 0 | 0.22251 | 0.38249 | 0.96052 | 3.2151 | 2.6227 | 1.1444 | 1.605 | 1.283 | 0.82464
Hematite | 0 | 0 | 0 | 0.13465 | 0.083726 | 0.15642 | 0.33659 | 0.46977 | 0.20806 | 0.6872
Goethite | 0 | 0 | 0 | 0.21544 | 0.066981 | 0 | 0.13464 | 0 | 0.20806 | 0.20616
Chart: µm
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10
Illite-Musc | 0.48149 | 1.3217 | 0.87051 | 2.2218 | 2.0569 | 1.2618 | 1.769 | 5.0382 | 13.8845 | 14.9294
Kaol-Clin | 0.42799 | 0.24922 | 0.47482 | 0.93359 | 4.1751 | 2.607 | 2.5731 | 3.1631 | 4.9379 | 5.1311
Quartz | 3.8554 | 4.3097 | 14.7907 | 39.7171 | 32.6832 | 29.0239 | 43.4476 | 32.6958 | 27.1766 | 14.2353
Calcite | 95.169 | 93.5987 | 82.7244 | 54.5611 | 55.181 | 58.9499 | 47.8862 | 53.2872 | 49.1158 | 61.6188
Dolomite | 0.011672 | 0.15487 | 0.32446 | 0.3501 | 1.0148 | 2.2556 | 1.2791 | 1.4469 | 1.3482 | 1.8005
Halite | 0 | 0 | 0.092326 | 0.071815 | 0.011163 | 0.015642 | 0.01496 | 0.039147 | 0.055482 | 0
Gypsum | 0.054471 | 0.049843 | 0.083094 | 0.10682 | 0.046887 | 0.080296 | 0.068067 | 0.082209 | 0.024274 | 0
Microcline | 0 | 0.093456 | 0.25719 | 0.72712 | 1.4652 | 3.0267 | 1.3464 | 2.1727 | 1.7581 | 0.56694
Ab-An | 0 | 0.22251 | 0.38249 | 0.96052 | 3.2151 | 2.6227 | 1.1444 | 1.605 | 1.283 | 0.82464
Hematite | 0 | 0 | 0 | 0.13465 | 0.083726 | 0.15642 | 0.33659 | 0.46977 | 0.20806 | 0.6872
Goethite | 0 | 0 | 0 | 0.21544 | 0.066981 | 0 | 0.13464 | 0 | 0.20806 | 0.20616

## Slide 27
Chart: microns
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10 | <1000
Kaol-Clin | 3.7 | 3.4 | 3.8 | 1.9 | 3.2 | 3.2 | 5.1 | 4.1 | 6.6 | 2.9641 | 3.1
Illite-Musc | 5.1 | 5 | 5.8 | 7.7 | 5.1 | 7 | 3.7 | 4.7 | 10.2 | 4.8385 | 4.3
Chart: microns
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10
Kaol-Clin | 0.42799 | 0.24922 | 0.47482 | 0.93359 | 4.1751 | 2.607 | 2.5731 | 3.1631 | 4.9379 | 5.1311
Illite-Musc | 0.48149 | 1.3217 | 0.87051 | 2.2218 | 2.0569 | 1.2618 | 1.769 | 5.0382 | 13.8845 | 14.9294
Chart: microns
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10 | <1000
Goethite | 0.1 | 0.2 | 0.1 | 0.4 | 0.1 | 0.2 | 0.3 | 0.1 | 0.2 | 0.62272 | 0
Hematite | 0 | 0 | 0 | 0 | 0 | 0.3 | 0.4 | 0.2 | 0.3 | 0.62272 | 0.4
Chart: microns
| >2000 | 1000-2000 | 500-1000 | 250-500 | 80-250 | 63-80 | 40-63 | 20-40 | 10-20 | <10
Goethite | 0 | 0 | 0 | 0.21544 | 0.066981 | 0 | 0.13464 | 0 | 0.20806 | 0.20616
Hematite | 0 | 0 | 0 | 0.13465 | 0.083726 | 0.15642 | 0.33659 | 0.46977 | 0.20806 | 0.6872

## Slide 28: Field setup
Dominant wind direction
90°
Fetch length > 50m
10m tower: 5 2D sonic anemometers, 4 temp sensors with aspirated shield, 1 RH/T sensor, P sensor, 2 3D sonic anemometers, 1 Wellas optical counter
2 FIDAS Optical counters at 2 m and 4 m 2 MOUDI Multistage Cascade impactors Polar nephelometer and aethalometer
3 SANTRIS Saltation sensors, 3 heights each
5 MWAC masts (4 heights: 0.1, 0.2, 0.5, 1)
Radiometer and pluviometer
Soil-surface moisture sensors
PM2.5/PM10 low volume samplers
3 Free wing impactors

## Slide 29: M´Hamid (24 Aug – 6 Oct)
L´Bour

## Slide 37: EMIT Science team
Science Team The EMIT investigation, led by Robert O. Green (JPL), brings together leaders in mineral measurements, soil science, surface property retrievals, Earth System modeling, and imaging spectroscopy.
Deputy-PI Natalie M. Mahowald (Cornell)
Roger Clark (PSI)
Bethany Ehlmann (Caltech) Paul Ginoux (NOAA)
Olga Kalashnikova (JPL)
Ron Miller (GISS)
Greg Okin (UCLA) Thomas Painter (JPL)
Carlos Perez (BSC)
Vincent Realmuto (JPL)
Gregg Swayze (USGS)
David R. Thompson (JPL)
Science Collaborators:
Luis Gaunter (GFZ)
Eyal Ben Dor (UTA)
Elizabeth Middleton (GSFC)

## Slide 38: FRAGMENT Team
Research Team:
FRAGMENT, led by Carlos Pérez García-Pando* from the Barcelona Supercomputing Center, involves world-class experts on modelling, aerosol campaigns and analyses, mineralogy, and spectroscopy.
Martina Klose (BSC)
Cristina González (BSC)
Adolfo González (BSC-CSIC)
Oriol Jorba (BSC)
Maria Gonçalves (BSC)
+ other members of BSC
Xavier Querol (IDAEA-CSIC)
Andrés Alastuey (IDAEA-CSIC)
+ other members of IDAEA-CSIC
Konrad Kandler (TUDA)
Agnesh Panta (TUDA)
Ron Miller (NASA GISS)*
Robert Green (JPL)**
Bethany Ehlmann (Caltech)*
Roger Clark (PSI)*
** PI of EMIT
* Part of EMIT´s Science Team

## Slide 39: Thank you
carlos.perez@bsc.es