## Slide 1: Deploying the MONARCH atmospheric model in the Cloud
Miguel Castrillo, Francesca Macchia, Gilbert Montané, Kim Serradell
Computational Earth Sciences
09/02/2021
Weather and climate in the cloud

## Slide 2: Outline
Mineral dust services at BSC
First experience (AWS)
PoC with ORACLE
Main takeaways
Conclusions

## Slide 3: Earth Sciences

## Slide 4: Mineral dust services at BSC
4
BSC dust operational forecast:
Contribution to the SDS-WAS (regional) and ICAP (global) multi-model ensembles
WMO Dust Regional Centres:
Barcelona Dust Forecast Centre. First specialized WMO Centre for mineral dust prediction. Started in 2014 - Operational
  http://dust.aemet.es
  @Dust_Barcelona
Sand and Dust Storms Warning Advisory and Assessment System (SDS-WAS). North Africa, Middle East and Europe Regional Center. Started in 2010 – Research
  http://sds-was.aemet.es
Both WMO Regional Centres are jointly managed by BSC and AEMET

## Slide 5: Operational services with some constraints
BSC is a research center not an operational one. That means:
  No 24/7 helpdesk for HPC services
  No 24/7 forecast managers
  [Annual] power maintenances
  No HPC redundancy
But…
  we need to deliver our products.
  Customers are always expecting the daily output (even if they know our constraints)
Two solutions
  Duplication of processes
    BDFC simulation is executed in Mare Nostrum4 and Nimbus (AEMET)
  Cloud

## Slide 6: Why moving to the cloud?
oper
VM
Inidata
HPC
post VM
Web
FTP
…
Cloud

## Slide 7: Amazon Web Services
In 2019, we contacted AWS for a test
We got some free credits
Work done as final graduate work
  Evaluation of AWS for running BSC-EC models, Adrià Quesada, 2019
We deployed NMMB/MONARCH model (previous version)
We did a MANUAL deployment
  Starting from scratch from a AWS Ubuntu ISO
  Install packages and/or compile dependencies
  Build a small SLURM cluster
  Compile model (Fortran+MPI)
  Run model
  Analyse results

## Slide 8: Amazon Web Services (II)
Results
  The experience was successful
  We validated the idea of running a forecast in the cloud
  But everything was manual

## Slide 9: Amazon Web Services (III)
Bonus track: extract traces using EXTRAE + PARAVER

## Slide 10: Parallel tasks
In the meantime, many efforts in parallel
  Refactor of the code (from NMMB/MONARCH to MONARCH)
  Development of Auto-MONARCH (code supported by Autosubmit, our workflow manager)
  Gitlab + Jenkins integration
  Output checker
  Hiring of two Research Engineers

## Slide 11: ORACLE
BSC-ES has a partnership with HPCNow!
  Spanish consultancy providing advanced supercomputing services for science and engineering.
  They become partners with ORACLE Cloud.
  Agreement between the three parts for a PoC.
Three roles
  Cloud provider (ORACLE Cloud)
  HPC consultants (HPCNow!)
  Research Engineers (Earth Sciences)

## Slide 12: Workflow
Management VM
bscesoper
VM
GFS
HPC
(MN4)
post VM
Web
FTP
…
HPC cloud resources
Cloud
GFS
Cloud

## Slide 13: Configuring HPC resources
Between HPCNow! and ORACLE
  Provision HPC resources. Configure the resources needed that will be available on request
    Deploy a management node (login)
    Using SLURM Cloud Scheduling capabilities
    Sending a batch job will deploy automatically the resources
    Efficient control of these resources
 | Resource for the PoC
Management Node | 1 x VM.Standard.E2.4
Storage | 1 x VM.Standard.E2.4 + 10 VPU (Total: 6TB)
Compute 1 - AMD | 2 x BM.Standard.E2.64
Compute 2 - Intel | 2 x BM.HPC2.36

## Slide 14: Software deployment
Between BSC-ES and HPCNow!
  Deploy the software stack
    Using EasyBuild to automate the installation
    Reproducibility and performance
    Replicate your usual software stack
  Compile and optimize your model to get the best performance
    You don’t know the hardware

## Slide 15: Auto-MONARCH - Configuration
MONARCH NAME-E Regional
  Res: 0.1º x 0.1º
  Grid: 1021 x 701 x 40
  24h Forecast
  Scaling exercise: 68, 144, 288 and 576 cores.

## Slide 16: Auto-MONARCH - Results

## Slide 17: Results (II)

## Slide 18: Main Takeaways
The cloud is a feasible solution to replace usual HPC premises as a backup solution
Collaboration with vendors is mandatory
Automate your processes as much as possible
Replicate the software stack is key
Verify your results
Invest on human resources
And Price?

## Slide 19: Future work
Deploy operationally this solution
Develop “smart” capabilities for Autosubmit
Extend this approach to other BSC forecasts
Notes: Including the financial agreement to get those resources

## Slide 20: Acknowledgements
ORACLE
HPCNow!
Computational Earth Sciences research engineers and scientists from Atmospheric Composition group and Earth System Services group.

## Slide 21: Thank you
kim.serradell@bsc.es

## Slide 22: Extending the PoC
At the beggining, we defined a second use case to test the Cloud approach.
  From the S2S4E project, we ported the workflow used to compute an ensemble of sub-seasonal climate predictions from the ECMWF monthly system with data from the ERA5 reanalysis.
Serial computing with high I/O needs (volume and performance).