## Slide 1: Assessment of modelled dust mineralogy with multiple Earth System Models
María Gonçalves Ageitos, Vincenzo Obiso, Ron Miller, Longlei Li, Natalie Mahowald, Paul Ginoux, Samuel Remy, Jan Perlwitz, Philip G. Brodrick, Robert O. Green, David R. Thompson, Oriol Jorba, Carlos Pérez García Pando.
21th AeroCom /10th AeroSAT meeting
Oslo, 10/10/2022
Climate, Aerosol, and Pollution Research

## Slide 2: … these impacts are modulated by mineralogy.
Dust
Radiation interaction
Cloud formation
Biogeochemical cycles
Atmospheric chemistry
Image credits: NASA, NOAA, Krueger et al. (2004)
Kandler et al. (2007)
Gypsum
Calcite
Silicates
Iron grains
Notes: Mineral dust plays a key role in multiple processes of the Earth System.
Dust interacts with short and long wave radiation
and influences cloud formation, hence having an impact on the Earth’s radiative balance
It also acts as a carrier of nutrients to ocean and land ecosystems, which can potentially influence the global carbon cycle.
Dust particles can also get coated with different atmospheric species and intervene in atmospheric chemistry.

## Slide 3: Goal
More and more, Earth System Models (ESMs) are including dust mineralogy in their frameworks, with different levels of complexity.
Overview of the variability in modelled dust mineralogy produced by different state of the art atmospheric and ESMs: CESM-CAM6, GFDL-AM4, IFS-AER, GISS-ModelE and MONARCH.
Provide an evaluation of the modelled mineral mass fractions against observations.

## Slide 4: Modelling dust mineralogy
Soil mineralogy
Emitted size-resolved mineral fractions
Minerals’ atmospheric cycle

## Slide 5: Global soil mineralogy atlases
Journet et al. 2014
HWSD
FAO soil classification
Mean mineralogy
Mineralogical composition for
clay (ϕ < 2 µm) and silt (ϕ 2-63 µm) size classes
Claquin et al. 1999, Nickovic 2012: 8 minerals.
Illite, smectite, kaolinite, quartz, feldspars, calcite, gypsum and hematite (iron oxides).
Journet et al. 2014: 12 minerals.
Illite, smectite, kaolinite, vermiculite, chlorite, mica, quartz, feldspars, calcite, gypsum, hematite and goethite.
Notes: Currently 2 SMAs implemented:
  Claquin – 8 minerals, including hematite as iron oxides
  Journet – same minerals, plus other 4, particularly distinguishes between goethite and hematite
They use a common methodology
  FAO soil classification
  Assign to each soil type or unit a mean mineralogy composition based on available literature – information is provided in two size classes (clay/silt).
  Large uncertainty, due to the scarcity of observations and the number of assumptions or empirical approaches used to fill in missing information
  Example of iron oxides: Claquin on top hematite distribution over arid soils in arid and semi-arid regions // Journet goethite + hematite. – Huge differences over dust sources
  Best information we have (so far)

## Slide 6: Ongoing EMIT NASA mission
Green et al. (2020)
Map of the mineralogy of dust sources at high resolution
Abundance of 10 minerals
(to be complemented with additional methods for quartz and feldspars)
Input for ESMs

## Slide 7: Model characteristics
Model | CESM-CAM6 | MONARCH | GFDL-AM4 | GISS-ModelE | IFS-Aer
Soil mineralogy | C1999 | C1999 J2014 | C1999 | C1999 | J2014
PSD | Modal model 3 modes | Sectional model 8 bins | Sectional model 5 bins | Sectional model 5 bins | Sectional model 3 bins
Size range (diameter) | 10 µm | 20 µm | 20 µm | 32 µm | 40 µm
Emission method | BFT | BFT | BFT | Modified BFT | Projected
Mixing state | Internally mixed | Externally mixed Fraction of iron oxides mixed with other minerals | Externally mixed Fraction of iron oxides mixed with other minerals | Externally mixed Fraction of iron oxides mixed with other minerals | Externally mixed
References | Scanza et al. (2015), Hamilton et al. (2019), Li et al. (2021) | Gonçalves Ageitos et al. (in. prep), Klose et al. (2021) | Horowitz et al. (2020) | Obiso et al. (in prep), Perlwitz et al. (2015a,b) | Remy et al. (2022)

## Slide 8: Variability across models: same soil map. Mineral mass fractions at surface PM10 concentration.
Quartz (%w)
Feldspars (%w)
Iron oxides (%w)
CESM-CAM6 MONARCH GFDL-AM4 GISS-ModelE

## Slide 9: Observations of mineral mass fractions
Obs. from the late 60’s to date.
Sampling time vs. model average: Temporal collocation – monthly basis
Reported minerals vs. modelled minerals: Mineral fractions estimated over those minerals observed AND modelled
Size range of observations vs. modelled size range: Size collocation
    Statistics in the plots use data in the modelled size ranges.
    Normalized Mean Bias (nMB)
    Normalized Root Mean Square Error (nRMSE)
    Correlation (r)
    Number of measurements in the samples used for the comparison (n)
Perlwitz et al. (2015)
Notes: Perlwitz et al. (2015) observations and evaluation methodology
  Observed minerals in specific sites and from ship campaigns since the late 60’s to present (2015).
  Method to derive uncertainty of the measurement comparable to modelled monthly mean.
  Collocation in space (nearest neighbour to the lat-lon location of the obs. Site or average over the ship’s trajectory) and time (model value corresponding to the month(s) of the measurement).
  Collocated size ranges considering fractions below 2, 10, 20 µm, between 2 and 20 µm and bulk (i.e. measures reported as bulk or below ranges larger than 20 µm).
  Evaluation of mineral fractions over minerals present in the observation and the model.

## Slide 10: Quartz mass fraction evaluation
CESM-CAM6 MONARCH GFDL-AM4 GISS-ModelE
IFS-AER MONARCH
Overestimation of the mass fraction above 2 µm of diameter across models.
Some models also show an underestimation in clay sized fractions (below 2 µm of diameter).

## Slide 11: Feldspar mass fraction evaluation
CESM-CAM6 MONARCH GFDL-AM4 GISS-ModelE
IFS-AER MONARCH
Better correlation between models and observations for the feldspars mass fraction than for quartz (less observations).
Underestimation of the mass fraction above 2 µm of diameter across models.

## Slide 12: Iron oxides mass fraction evaluation
CESM-CAM6 MONARCH GFDL-AM4 GISS-ModelE
IFS-AER MONARCH
Improved spatio-temporal distribution of iron oxides in models that use the Journet et al. (2014) soil map.
Underestimation in models using Claquin et al. (1999) and overestimation in models using Journet et al. (2014).

## Slide 13: Conclusions
Dust mineralogy is increasingly present in Earth System Models with the aim of improving the representation of dust climate interactions.
Despite the large variability across models, the evaluation metrics are overall similar when compared to our reference observational dataset.
Our current knowledge of the composition of dust sources is limited, and ultimately determines the models’ ability to reproduce the minerals’ atmospheric cycle.
Additional adjustments to define the size-distributed mineralogy at emission may be key to solve the overestimation of quartz in silt sizes, and in turn improve the feldspars representation.
Including goethite within the modelled iron oxides results in a slightly better comparison with observations. The reason for this improvement has to be further explored (increased mass, speciation, spatial distribution).
Our results support the need for further observational constraints, both to better characterize the soils and to assess the airborne dust composition.
Ongoing projects, such as EMIT or FRAGMENT, will provide key new information for the modelling community.
Notes: (e.g. mapping of soil units to the model grid, normalization of soil mineral fractions, projection of the size-distributed soil composition on the emitted size distribution),

## Slide 14: Acknowledgments
This work was supported by the ERC Consolidator Grant FRAGMENT (grant agreement No. 773051), and the AXA Chair on Sand and Dust Storms at BSC funded by the AXA Research Fund both led by Dr. Carlos Pérez García Pando.
The research leading to these results has also received funding from the Spanish Ministerio de Economía y Competitividad as part of the NUTRIENT project (CGL2017-88911-R), the H2020 GA 821205 project FORCeS, and the ESA-DOMOS project.
We thankfully acknowledge the computer resources at Marenostrum4, granted through the PRACE project eFRAGMENT2 and the RES project AECT-2020-3-0020; the technical support provided by the BSC, and the work of all the members of the BSC Earth Science Department group who contribute to the MONARCH model and infrastructure developments.
Thanks to all the providers of the observational data used for the model evaluation.
Thank you !