## Slide 1
Okke van Eck
GPU Research Engineer Barcelona Supercomputing Center
The Wild West of Energy Profiling on EuroHPC Systems
23rd of June 2025, Vienna
okke.vaneck@bsc.es

## Slide 2: Supercomputers consume energy..

## Slide 3: Supercomputers consume energy.. But how much?

## Slide 4: Energy Consumption
Energy = Power × Time
Notes: References:
[1] https://ceec-coe.eu/wp-content/uploads/2024/08/ceec-bpg-measuring-energy.pdf

## Slide 5: Energy Consumption
Energy = Power × Time
Granularity of measurements
Notes: References:
[1] https://ceec-coe.eu/wp-content/uploads/2024/08/ceec-bpg-measuring-energy.pdf
Figure of sampling: https://en.wikipedia.org/wiki/Sampling_(signal_processing)

## Slide 6: Energy Consumption
Energy = Power × Time
Granularity of measurements
Overhead of a single measurement
Notes: References:
[1] https://ceec-coe.eu/wp-content/uploads/2024/08/ceec-bpg-measuring-energy.pdf
Figure of sampling: https://en.wikipedia.org/wiki/Sampling_(signal_processing)

## Slide 7: Energy Consumption
Energy = Power × Time
Granularity of measurements
Overhead of a single measurement
Computers are complex with many parts.
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
RAPL Power domains [1]
Notes: References:
[1] https://ceec-coe.eu/wp-content/uploads/2024/08/ceec-bpg-measuring-energy.pdf
Figure of sampling: https://en.wikipedia.org/wiki/Sampling_(signal_processing)

## Slide 8: Energy Consumption
Energy = Power × Time
Granularity of measurements
Overhead of a single measurement
Computers are complex with many parts.
What is included in a measurement?
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
RAPL Power domains [1]
Notes: References:
[1] https://ceec-coe.eu/wp-content/uploads/2024/08/ceec-bpg-measuring-energy.pdf
Figure of sampling: https://en.wikipedia.org/wiki/Sampling_(signal_processing)

## Slide 9: Cool! So how do we measure?

## Slide 10: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]

## Slide 11: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
PERF -

## Slide 12: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
PERF -
Notes: Out-of-band energy measurement refers to the process of monitoring power or energy consumption using a dedicated management subsystem that operates independently of the main CPU and operating system.
So for out-of-band we need don't need a CPU, while for in-band measurements it's done via the CPU.

## Slide 13: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
IMPI: Coarse measurements, 1-5s interval
High overhead
PERF -
[1]
Notes: Out-of-band energy measurement refers to the process of monitoring power or energy consumption using a dedicated management subsystem that operates independently of the main CPU and operating system.
So for out-of-band we need don't need a CPU, while for in-band measurements it's done via the CPU.

## Slide 14: Measuring Energy
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
It's not as straightforward as you might hope..
[1]
IMPI: Coarse measurements, 1-5s interval
High overhead
PM_Counters: Fine measurements, 1-10ms interval
Medium overhead
PERF -
[1]

## Slide 15: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
IMPI: Coarse measurements, 1-5s interval
High overhead
PM_Counters: Fine measurements, 1-10ms interval
Medium overhead
RAPL: Fine measurements, 1ms interval
Low overhead
PERF -
[1]

## Slide 16: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
IMPI: Coarse measurements, 1-5s interval
High overhead
PM_Counters: Fine measurements, 1-10ms interval
Medium overhead
RAPL: Fine measurements, 1ms interval
Low overhead
HWMON: Coarse measurements, on-demand interval
Sysfs for 100ms interval
PERF -
[1]

## Slide 17: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
NVML: Fine measurements, 20ms interval (Hopper)
Used by nvidia-smi
AMD GPA: Fine measurements, 50ms interval (MI250X)
Used by rocm-smi
PERF -

## Slide 18: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
PERF -
Notes: Out-of-band energy measurement refers to the process of monitoring power or energy consumption using a dedicated management subsystem that operates independently of the main CPU and operating system.
So for out-of-band we need don't need a CPU, while for in-band measurements it's done via the CPU.

## Slide 19: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
PERF -
[1]

## Slide 20: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
PERF -

## Slide 21: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ eacct -j $jobid
…
PERF -

## Slide 22: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ eacct -j $jobid
…
PERF -

## Slide 23: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ eacct -j $jobid
…
PERF -
Notes: The sampling interval depends on what backend is used!

## Slide 24: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ eacct -j $jobid
…
$ srun --ear=on ./a.out
PERF -
Notes: The sampling interval depends on what backend is used!

## Slide 25: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
source.c
include "meric.h"
MERIC_Init();
// computations..
MERIC_Close();
$ cat results.csv
PERF -
Notes: The sampling interval depends on what backend is used!

## Slide 26: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ scontrol show config
AcctGatherEnergyType = acct_gather_energy/ipmi
AcctGatherNodeFreq = 60 sec
PERF -
Notes: The sampling interval depends on the sys admin's wish!

## Slide 27: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ scontrol show config
AcctGatherEnergyType = acct_gather_energy/ipmi
AcctGatherNodeFreq = 60 sec
$ sacct -j $jobid --format=ConsumedEnergy
ConsumedEnergy
------------------------
729.09K
251.09K
…
PERF -
Notes: The sampling interval depends on the sys admin's wish!

## Slide 28: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
PERF -

## Slide 29: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ perf list | grep energy
power/energy-pkg/
power/energy-psys/
power/energy-pram/
PERF -
[1]

## Slide 30: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ perf list | grep energy
power/energy-pkg/
power/energy-psys/
power/energy-pram/
$ perf stat -e <events> -- ./a.out
27567.82 Joules power/energy/pkg
0.00 Joules power/energy/psys
429.40 Joules power/energy/pram
183.371090953 seconds time elapsed
PERF -
[1]

## Slide 31: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ module load papi
source.c
#include <papi.h>
PAPI_library_init(..);
PAPI_start_counters(events, NUM_EVENTS);
// computations
PAPI_stop_counters(values, NUM_EVENTS);
printf(..);
PERF -
Notes: The sampling interval depends on what backend is used!

## Slide 32: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ module load papi
source.c
#include <papi.h>
PAPI_library_init(..);
PAPI_start_counters(events, NUM_EVENTS);
// computations
PAPI_stop_counters(values, NUM_EVENTS);
printf(..);
PERF -
Notes: The sampling interval depends on what backend is used!

## Slide 33: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ likwid-perfctr -g ENERGY ./a.out
…
PERF -
Notes: The sampling interval depends on what backend is used!

## Slide 34: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ likwid-perfctr -g ENERGY ./a.out
…

## Slide 35: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ likwid-perfctr -g ENERGY ./a.out
…
PERF -
Notes: The sampling interval depends on what backend is used!

## Slide 36: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ likwid-perfctr -g ENERGY ./a.out
…
$ likwid-powermeter -t 100ms ./a.out
...
PERF -
Notes: The sampling interval is provided by the user via -t.

## Slide 37: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
[1]
$ likwid-perfctr -g ENERGY ./a.out
…
$ likwid-powermeter -t 100ms ./a.out
...

## Slide 38: Measuring Energy
It's not as straightforward as you might hope..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable
PERF -
[1]

## Slide 39: Hmm, do I just pick one?

## Slide 40: Availability on EuroHPC
Portability is hard..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable

## Slide 41: Availability on EuroHPC
Portability is hard..
[1] Gedik et al. for the HORIZON-EUROHPC-JU-2021-COE-01 deliverable

## Slide 42: Availability on EuroHPC
Portability is hard..

## Slide 43: Availability on EuroHPC
Portability is hard..
(**) Only on partitions with GPUs.

## Slide 44: Availability on EuroHPC
Portability is hard..
(*) Can be lowered by setting a variable.

## Slide 45: Soo.. What is fully portable then?

## Slide 46: Energy Profiler
Wrapper tool for targeting different methods.

## Slide 47
Okke van Eck
GPU Research Engineer Barcelona Supercomputing Center
The Wild West of Energy Profiling on EuroHPC Systems
23rd of June 2025, Vienna
okke.vaneck@bsc.es
Notes: That was all from my side. I hope you learned something about climate modellen or performance engineering.
Here you have my contact information in case you want to contact me later, but please ask any questions you have now as well.
Thank you!