## Slide 1: Scalable kinetics treatment for gas–aerosol systems in atmospheric models
Matthew Dawson1, Matthew West2, Nicole Riemer3, and Oriol Jorba1
10/4/2019
EGU General Assembly 2019
1. Earth Sciences, Barcelona Supercomputing Center, Barcelona, Spain.
2. Mechanical Science & Engineering, University of Illinois at Urbana–Champaign, USA.
3. Atmospheric Sciences, University of Illinois at Urbana–Champaign, USA.
Notes: Development of scalable kinetics treatment for chemistry in gas-phase models

## Slide 2: Motivation—Chemistry in Atmospheric Models
Host Model
gas-phase chemistry
KINETIC
inorganics
chemistry and partitioning
EQUILIBRIUM
organics chemistry and partitioning
EQUILIBRIUM
cloud
chemistry
changes model state
Notes: Typical configuration of modules used to resolve chemistry in atmospheric models
Generally a mix of equilibrium (parameterized or iteratively solved) and kinetics systems
Importantly, each module typically updates the model state and often have been developed independently
Mapping between modules
Order of operations can affect results

## Slide 3: Motivation—Chemistry and Related Modules
Host Model
Aerosol Representation
activity
model
activity
model
vapor
pressure
model
deposition
photolysis
emissions
aerosol
microphysics
gas-phase chemistry
KINETIC
inorganics
chemistry and partitioning
EQUILIBRIUM
organics chemistry and partitioning
EQUILIBRIUM
cloud
chemistry
calculates rates
support module
changes model state
transport
Notes: Zooming out to chemistry-related modules adds to the complexity
Increase need for mapping between modules
Overlapping scope
Equilibrium & Kinetics approaches
Aerosol-related modules are tightly tied to aerosol representation used by the host model
Difficulty adding new reactions/species
What if you want to use your new scheme in a different model?

## Slide 4: Design Goals
Treat chemistry, partitioning and related processes kinetically as one system to solve
Make it flexible
  Usable by modelers and experimentalists
  Portable between models (chamber, plume, regional, global)
  Object oriented design
  JSON configuration files
Make it efficient
  Scalable chemical complexity
  Condensed data structure
  Porting to GPUs
Notes: Scary part is the kinetics solving of everything
Making a stiff chemical system even stiffer
Why we have hope
Start simple (don’t expect to handle complexity of advanced equilibrium models from the beginning)
Apply filters at the reaction type (rather than the specific reaction level)
Use knowledge of system
  Stiff chemical systems rapidly relax to equilibrium or steady state unlike physical systems with rapid oscillations
Make it easier for new processes to be tested in large-scale models
Adaptable framework for modelers to add new types of processes and parameterizations
Experimentalist-friendly interface for testing new findings in a variety of models
Scalability of chemical and aerosol mechanisms in real time
Approach
JSON configuration files
Object-Oriented design

## Slide 5: Approach—Integrated Chemistry Module
Host Model
Aerosol Representation
aerosol
microphysics
calculates rates
changes model state
chemistry API
emissions
deposition
photolysis
model state
provides aerosol
properties
Chemistry Module
chemistry core
integrated
chemical
mechanism
Solver
solver API
PartMC Science Library
transport
Notes: Include emissions, gas- and aerosol-phase chemistry, photolysis, deposition, partitioning, and aerosol-phase chemistry
Chemistry module developed as part of the PartMC science software library.
Will be employed in PartMC, but can also be directly employed in other host models, like MONARCH.
(discussion not specifically focused on single-particle simulations)
Employ external solvers (right now SUNDIALS CVODE solver with the SuiteSparse sparse matrix for Jacobian data)
Will explore other solvers in the future

## Slide 6: JSON Configuration Files
Readily applied to science models
Industry standard – lots of free tools available
{
"name" : "MONARCH mass-based",
"type" : "AERO_REP_MODAL_BINNED_MASS",
"modes/bins" : {
"dust" : {
"type" : "BINNED",
"phases" : [ "dust" ],
"bins" : 8,
"minimum diameter" : 1.0e-7,
"maximum diameter" : 1.0e-5,
"scale" : "LOG"
},
"organic matter" : {
"type" : "MODAL",
"phases" : [ "organic matter" ],
"shape" : "LOG_NORMAL",
"geometric mean diameter" : 2.12e-8,
"geometric standard deviation" : 2.24
}, …
{
"type" : "SIMPOL_PHASE_TRANSFER",
"gas-phase species" : "ISOP-P1",
"aerosol phase" : "organic matter",
"aerosol-phase species" : "ISOP-P1_aero",
"B" : [ 3.81e3, -2.13e1, 0.0, 0.0 ]
}
{
"name" : "n-butanol/water activity",
"type" : "SUB_MODEL_UNIFAC",
"phases" : [ "n-butanol/water mixture"],
"functional groups" : {
"CH2(-OH)" : {
"main group" : "CHn(-OH)",
"volume param" : 0.6744,
"surface param" : 0.540
},
"CH2(hydrophobic tail)" : {
"main group" : "CHn(hydrophobic tail)",
"volume param" : 0.6744,
"surface param" : 0.540
}, …
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
Notes: First step is a flexible means to configure the chemistry.
Must be able to describe complex chemical systems and be easy to work with.
JSON!

## Slide 7: JSON Configuration Files – Arrhenius Reaction
{
"reactants" : {
”NO3" : {},
"NO" : {}
},
"products" : {
"NO2" : { ”yield” : 2.0 }
},
"type" : "ARRHENIUS",
"A" : 1.5E-11,
"C" : 170.0
}
NO3 + NO 2 NO2
k
Notes: Simple reactions are easily described…

## Slide 8: JSON Configuration Files – UNIFAC Activity
{
"name" : "n-butanol/water activity",
"type" : "SUB_MODEL_UNIFAC",
"phases" : [ "n-butanol/water mixture"],
”main groups" : {
"CHn(-OH)" : {
"interactions with" : {
"OH" : 986.5,
”H2O" : 2314
}
},
"CHn(hydrophobic tail)" : {
"interactions with" : {
"OH" : 986.5,
”H2O" : 1325
}
}, …
Marcolli, C., & Peter, T. (2005). Atmos. Chem. Phys Discuss, 5(2), 1501–1527.
Notes: … and even relatively more complex submodels like the UNIFAC activity model are readily converted to JSON format.
It essentially is like putting the tables from the paper describing a model into an input file

## Slide 9: Object-Oriented Design
Chemistry Module
chemistry core
integrated
chemical
mechanism
SubModel
load()
initialize()
update()
…
AerosolRepresentation
load()
initialize()
effective_radius()
number_concentration()
…
Reaction
load()
initialize()
calc_derivative()
calc_Jacoobian()
…
Notes: The second tool used to increase flexibility is object oriented model design
Three types of abstract classes are employed: reactions, sub models and aerosol representations
The way the model interacts with any extending class is the same.
- Permits rapid development of new reaction types, addition of new sub models, and deployment to host models with unique aerosol representations

## Slide 10: Object-Oriented Design
Chemistry Module
chemistry core
integrated
chemical
mechanism
PDFiTE
load()
initialize()
update()
…
MassBasedBinsModes
load()
initialize()
effective_radius()
number_concentration()
…
SIMPOLPhaseTransfer
load()
initialize()
calc_derivative()
calc_Jacoobian()
…
Troe
load()
initialize()
calc_derivative()
calc_Jacoobian()
…
Arrhenius
load()
initialize()
calc_derivative()
calc_Jacoobian()
…
Arrhenius
load()
initialize()
calc_derivative()
calc_Jacoobian()
…
UNIFAC
load()
initialize()
update()
…
Notes: Reactions: Arrhenius, Troe, HL and SIMPOL VP-based phase transfer, emissions, photolysis, first-order loss (deposition), and more!
Sub-Models
PD-FiTE inorganic activity and UNIFAC organic activity
Aerosol Representations
Mixed binned modals mass-only scheme (MONARCH)
Single particle (PartMC)

## Slide 11: Aerosol Representations in Chemical Models – Challenges
Modal
Binned
Particle Resolved
Notes: Chemistry modules – particularly inorganic and organic partitioning and chemistry – are often tightly tied to the aerosol representation used in the host model
Chemistry doesn’t really care about the scheme as long as some basic questions can be answered: e.g., effective radius, number concentration

## Slide 12: Aerosol Representation Abstraction – Approach
Modal
INPUT
{
"name" : "Modal",
"type" : "AERO_REP_MODAL_BINNED_MASS",
"modes/bins" : {
"dust" : {
"type" : "BINNED",
"phases" : [ "dust" ],
"bins" : 8,
"minimum diameter" : 1.0e-7,
{
"name" : "inorganics",
"type" : "AERO_PHASE",
”species" : [
"PM_phob", "PM_phil", "ISOP-P1_aero",
"ISOP-P1_aero", "TERP-P1_aero", "TERP-P1_aero"
]
}
{
"name" : "black carbon",
"type" : "AERO_PHASE",
”species" : [
"PM_phob", "PM_phil", "ISOP-P1_aero",
"ISOP-P1_aero", "TERP-P1_aero", "TERP-P1_aero"
]
}
{
"name" : "organics",
"type" : "AERO_PHASE",
”species" : [
"PM_phob", "PM_phil", "ISOP-P1_aero",
"ISOP-P2_aero", "TERP-P1_aero", "TERP-P2_aero"
]
}
AerosolPhase
load()
initialize()
…
AerosolPhase
load()
initialize()
…
AerosolPhase
load()
initialize()
…
Modal
load()
initialize()
effective_radius()
number_concentration()
…
BC
O
I
mode 1 – black carbon
mode 2 – organics
mode 3 – inorganics
gas-phase species
INPUT
Model State

## Slide 13: Aerosol Representation Abstraction – Approach
INPUT
{
"name" : "Modal",
"type" : "AERO_REP_MODAL_BINNED_MASS",
"modes/bins" : {
"dust" : {
"type" : "BINNED",
"phases" : [ "dust" ],
"bins" : 8,
"minimum diameter" : 1.0e-7,
{
"name" : "inorganics",
"type" : "AERO_PHASE",
”species" : [
"PM_phob", "PM_phil", "ISOP-P1_aero",
"ISOP-P1_aero", "TERP-P1_aero", "TERP-P1_aero"
]
}
{
"name" : "black carbon",
"type" : "AERO_PHASE",
”species" : [
"PM_phob", "PM_phil", "ISOP-P1_aero",
"ISOP-P1_aero", "TERP-P1_aero", "TERP-P1_aero"
]
}
{
"name" : "organics",
"type" : "AERO_PHASE",
”species" : [
"PM_phob", "PM_phil", "ISOP-P1_aero",
"ISOP-P2_aero", "TERP-P1_aero", "TERP-P2_aero"
]
}
AerosolPhase
load()
initialize()
…
AerosolPhase
load()
initialize()
…
AerosolPhase
load()
initialize()
…
Binned
load()
initialize()
effective_radius()
number_concentration()
…
BC
O
I
bin 1 – black carbon
bin 1 – organics
bin 1 – inorganics
gas-phase species
INPUT
Binned
BC
O
I
bin 2 – black carbon
bin 2 – organics
bin 2 – inorganics
Model State
bin 3 – …
Notes: Chemistry modules – particularly inorganic and organic partitioning and chemistry – are often tightly tied to the aerosol representation used in the host model

## Slide 14: Aerosol Representation Abstraction – Approach
INPUT
{
"name" : "Modal",
"type" : "AERO_REP_MODAL_BINNED_MASS",
"modes/bins" : {
"dust" : {
"type" : "BINNED",
"phases" : [ "dust" ],
"bins" : 8,
"minimum diameter" : 1.0e-7,
{
"name" : "inorganics",
"type" : "AERO_PHASE",
”species" : [
"PM_phob", "PM_phil", "ISOP-P1_aero",
"ISOP-P1_aero", "TERP-P1_aero", "TERP-P1_aero"
]
}
{
"name" : "black carbon",
"type" : "AERO_PHASE",
”species" : [
"PM_phob", "PM_phil", "ISOP-P1_aero",
"ISOP-P1_aero", "TERP-P1_aero", "TERP-P1_aero"
]
}
{
"name" : "organics",
"type" : "AERO_PHASE",
”species" : [
"PM_phob", "PM_phil", "ISOP-P1_aero",
"ISOP-P2_aero", "TERP-P1_aero", "TERP-P2_aero"
]
}
AerosolPhase
load()
initialize()
…
AerosolPhase
load()
initialize()
…
AerosolPhase
load()
initialize()
…
ParticleResolved
load()
initialize()
effective_radius()
number_concentration()
…
BC
O
I
particle 1 – black carbon
particle 1 – organics
particle 1 – inorganics
gas-phase species
INPUT
BC
O
I
particle 2 – black carbon
particle 2 – organics
particle 2 – inorganics
Model State
particle 3 – …
Particle Resolved
Notes: Chemistry modules – particularly inorganic and organic partitioning and chemistry – are often tightly tied to the aerosol representation used in the host model

## Slide 15: Work Flow – Initialization
USER
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
INPUT
OPTIMIZE
SIMPOLPhaseTransfer
load()
initialize()
…
TroeReaction
load()
initialize()
…
ArrheniusReaction
load()
initialize()
…
UNIFAC
load()
initialize()
…
PDFITE
load()
initialize()
…
MassOnlyBinsModes
load()
initialize()
…
Condensed Data Structure
Single dense data block
  Species indices
  Fixed parameters
  Environment-dependent parameters
  etc.
Notes: Model initialization work flow
User builds set of JSON configuration files or extends existing mechanism
During initialization, input data is parsed, validated and converted to instances of classes extending the three main abstract classes
To maintain efficiency, each reaction, sub model and aerosol representation determines the size of a block of data just large enough to contain the indices, parameters, and working memory it will need during solving
  Then, a continuous block of memory is allocated to store all this data sequentially
  (Memory access is often a major bottleneck in model execution)
  During solving, model elements are asked to calculate required info (time derivatives, Jacobian contributions, etc.) in the order they exist in the data block

## Slide 16: Porting to GPUs
Solving chemical mechanisms involve repeated calculations of contributions from hundreds or thousands of individual reactions
Approach: simultaneously solve for multiple grid cells by spreading reaction calculations across GPUs
GPUs
State
species_state[]
advance
state
Solver
(CPU)
Condensed Data Structure
Notes: Describe porting to GPUs

## Slide 17: MONARCH: On-line Weather–Chemistry Model
Multiscale Model from Global to Local Scales
Notes: MONARCH is a fully on-line coupled meteorology – chemistry model
The meteorological driver is the NCEP NMMB
The chemistry and aerosol schemes have been developed in-house.
It operates at global and regional domains up to 1 km with telescoping nesting capabilities.

## Slide 18: Chemistry Module – Overall Workflow
Load input files into model objects
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
{
"reactants" : {
"O3" : {} ,
"NO" : {}
},
"products" : {
"NO2" : {}
},
"type" : "ARRHENIUS",
"A" : 3.0E-12,
"B" : 0.0E+00,
"C" : -1500.0
}
SIMPOLPhaseTransfer
load()
initialize()
…
TroeReaction
load()
initialize()
…
ArrheniusReaction
load()
initialize()
…
UNIFAC
load()
initialize()
…
PDFITE
load()
initialize()
…
MassOnlyBinsModes
load()
initialize()
…
Your favorite model
PartMC
Change the chemical mechanism without recompiling
  Vary mechanism complexity based on conditions/location
  Compare mechanisms in real time
Use same mechanisms across models (MONARCH, PartMC, etc.) changing only Aerosol Representation JSON
State
species_state[]
Solver
advance
state
MONARCH
Condensed Data Structure
The PartMC library is available at: https://github.com/compdyn/partmc
Notes: Summarize by example –
Experimentalist finds new chemical process
gas-phase reactions
Partitioning to aqueous aerosols
Acid dissociation
Aqueous reaction with dissolved species
Re-evaporation
Further reactions
Condensation to organic aerosols
Now they can do all this by modifying or creating a couple JSON files and run the same chemistry in a particle-resolved chamber model, a PartMC Lagrangian urban plume simulation and a global MONARCH simulations with a mixed binned/model aerosol scheme
No modifying source code
No recompiling the model
Just sit back and enjoy

## Slide 19
matthew.dawson@bsc.es
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under the Marie Sklodowska-Curie grant agreement No 747048.

## Slide 20: Check out our on-going development!
> git clone https://github.com/compdyn/partmc.git
> cd partmc
> git checkout chem_mod
> docker build -t try-out-chemistry .
> docker run -it try-out-chemistry bash
> cd build
> make test
With Docker© installed:
Start 13: test_rxn_first_order_loss
13/85 Test #13: test_rxn_first_order_loss .............. Passed 0.06 sec
Start 14: test_rxn_HL_phase_transfer
14/85 Test #14: test_rxn_HL_phase_transfer ............. Passed 0.07 sec
Start 15: test_rxn_PDFiTE_activity
15/85 Test #15: test_rxn_PDFiTE_activity ............... Passed 0.04 sec
Start 16: test_rxn_photolysis
16/85 Test #16: test_rxn_photolysis .................... Passed 0.06 sec
...
Start 21: test_sub_model_UNIFAC
21/85 Test #21: test_sub_model_UNIFAC .................. Passed 0.03 sec
...
Start 23: test_chemistry_cb05cl_ae5
23/85 Test #23: test_chemistry_cb05cl_ae5 .............. Passed 5.78 sec
Start 25: test_MONARCH_1
25/85 Test #25: test_MONARCH_1 ......................... Passed 0.37 sec
Start 26: test_MONARCH_2
26/85 Test #26: test_MONARCH_2 ......................... Passed 7.00 sec
Notes: Still a work in progress! But if you want to see the design and how to interact with it, try it out!
(describe unit testing)