## Slide 1: Coupling between traffic and emission models for the evaluation of mobility plans
08/10/2019
Fairmode – Madrid
Daniel Rodriguez Rey1, Marc Guevara1, Mari Paz Linares2, Juan Salmeron2, Josep Casanovas1,2, Jaime Benavides1, Oriol Jorba1, Albert Soret1.
Barcelona Supercomputing Centre – Centro Nacional de Supercomputación (BSC-CNS) Earth Sciences division
inLab FIB, Universitat Politècnica de Catalunya, Facultat d’Informàtica de Barcelona

## Slide 2: Need to integrate mobility and emission models
Historic NO2 measured levels in Barcelona (ASPB, 2018)
Urban air quality problems mostly related to traffic. They can be tackled:
  Technological policies: Euro classification program: Inefficient for NOx reduction in Diesel (Carslaw and Rhys-Tyler, 2013).
  Reduction of VKT (vehicles kilometres travelled) by mobility plans:
Which tools or methodologies should we use to evaluate urban mobility plans?
https://urbanaccessregulations.eu/userhome/map

## Slide 3: CALIOPE / CALIOPE – Urban workflow
HERMESv3
(emissions)
WRF-CMAQ
(mesoscale)
R-Line
(urban scale)
VISUM
CALIOPE-Urban NO2 high-resolution (10m × 10m) concentration map. Benavides et al. (2019, Geosci. Model Dev.)
CALIOPE
CALIOPE - Urban
Available at: www.bsc.es/caliope
Observed
CALIOPE
CALIOPE-Urban
445 Valencia St.
(Baldasano et al., 2008; Guevara et al., 2013)
(Snyder et al., 2013)
(Benavides et al. 2019)
(Baldasano et al., 2008)

## Slide 4: The traffic simulator
Zone A
Zone B
Origin Destination matrixes OD
Each path with difference impedance
Traffic assigment by an iterative process achieving user optimum.
Traffic lights
Vehicle flow
Road capacity
Network construction:
Network: Open Street Map data.
Private Tr. OD matrix data: GPS phone.
Public Tr. OD matrix data: GPS phone + public administration counting.
Calibration: 138 traffic flow data.

## Slide 5: Visum network

## Slide 6: Visum - HERMESv3
High resolution emission modelling system
  Emissions estimated at the source level combining state-of-the-art methodologies with local data and meteorology (Energy and manufacturing industries, residential and commercial combustion, agriculture, road transport, other mobile sources)
Road transport emissions
  Street-level and vehicle-specific emissions
  COPERT 5 + resuspension (Pay et al., 2011)
  AADT (Annual Average Daily Traffic) 
  Traffic Network 
  Volume profile 
  Speed profile 
  Vehicle fleet
    RSD study (RACC-AMB, 2017)
VISUM
VISUM
VISUM
VISUM

## Slide 7: Superblocs idea
Street type to simulate
Aj. de Barcelona – “Pla d’Acció de l’àmbit de Superilles de St. Antoni.” December 2017

## Slide 8: Superblocks scenario
Creation of a new road type: “Superblock”.
  Max speed: 20 km/h
  Link capacity: 5,250 vehicles/day
    Estimated AADT: 3,000 to 8,000 vehicles. (action plan superilles: St. Antoni)
Vehicle demand (nº of trips) kept constant
Modification of the streets according to the reports of the city hall for each Superblock.
Aj. de Barcelona – “Pla d’Acció de l’àmbit de Superilles de St. Antoni.” December 2017
Screenshot from Visum network

## Slide 9: Superblocs scenario results
Superblock

## Slide 10: Superblocs scenario results
Total Base (24h) | 22.454 mol Nox
Total Superblocks (24h) | 22.743 mol NOx
Chart: Superblocks Scenario: Hourly flow and NOx for principal roads
| València | C. Cent | Viladomat | GV (pl. españa) | Pere IV
AADT Base | 1884.1266 | 868.5898 | 374.9989 | 3254.8011 | 1110.7553
AADT Superblocks | 2082.5465 | 363.6314 | 517.22 | 3501.5008 | 647.8182
NOx base | 1.6 | 0.7 | 0.14 | 4 | 1.2
NOx Superblocks | 2 | 0.08 | 0.4 | 4.6 | 0.9
NOx [mol.h-1]

## Slide 11: Diagonal Tram plan
Current disposition
Proposed disposition
New Tram line
Current Tram line

## Slide 12: Diagonal Tram scenario results
Total Base (24h) | 11743 mol NOx
Total Tram (24h) | 11180 mol NOx
Chart: Tram Scenario: Hourly flow and NOx for principal roads
| Diagonal Central | Diagonal Lateral out | Diagonal Lateral in | GV (Tetuan) | Ronda de dalt
AADT Base | 2554.4882 | 627.9571 | 429.0901 | 3542.9474 | 7926.7683
AADT Tram | 0 | 1466.0208 | 1037.8247 | 3701.9642 | 7982.2646
Nox base | 2.7 | 0.8 | 0.1 | 3.2 | 10
NOx TRAM | 0 | 1.75 | 0.6 | 3.4 | 10
NOx [mol.h-1]

## Slide 13: Tram+Superblocks scenario results
Total Base (24h) | 63274 mol NOx
Total Tram+SB (24h) | 64058 mol NOx
Chart: Tram+Superblocks Scenario: Hourly flow and NOx for principal roads
| Diagonal Central | Diagonal Lateral out | GV (pl. españa) | C. Cent | València
AADT Base | 2554.4882 | 627.9571 | 3254.8011 | 868.5898 | 1884.1266
AADT Tram + superblocks | 0 | 1470.1718 | 3495.9448 | 370.9755 | 2125.3341
NOx Base | 3 | 0.8 | 4 | 0.9 | 1.6
NOx Tram + Superblocks | 0 | 1.6 | 4.5 | 0.5 | 2
NOx [mol.h-1]

## Slide 14: Future work
Coupling the public transport network
Design and implementation of other mobility policies (congestion charge)
Air quality evaluation:
  Mesoscale CALIOPE
  Urban scale (CALIOPE – Urban)
Comparison between mesoscale (COPERT 5) and instantaneous (PHEMLight) emission models for hot spots

## Slide 15
08/10/2019
Daniel Rodríguez Rey
Barcelona Supercomputing Center
Earth Sciences department
daniel.rodriguez@bsc.es
Thank you for your attention
Acknowledgements:
Daniel R. Rey work is funded with the grant BES-2016-078116 from the FPI program by the Spanish Ministry of Economy and Competitiveness.
Daniel developed part of this work at the inLab-Fib UPC research center and acknowledges the staff in there.

## Slide 16: Future work
Instantaneous emission models for hot spots
Chart: Crossroad section, NOx, 24h
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
NOx_PHEMLight | 2572.5589 | 1748.5142 | 1388.4826 | 1019.8656 | 1181.3609 | 1742.4933 | 2549.2751 | 11008.0133 | 14942.5041 | 14868.5229 | 13897.4473 | 14232.346 | 13838.2067 | 13872.0047 | 13472.7227 | 12597.4397 | 14249.6035 | 14721.2891 | 15834.7916 | 14338.7287 | 12988.9375 | 8376.4446 | 5263.6767 | 4592.1939
NOx_hermes | 2481.6978 | 1574.1606 | 1054.7877 | 826.121 | 962.0676 | 1539.6783 | 2772.8436 | 8487.3824 | 12588.6886 | 12332.4456 | 11407.0231 | 11568.6988 | 11377.2471 | 10680.2168 | 9601.2304 | 9787.0214 | 11173.1834 | 12471.2263 | 13296.902 | 12409.856 | 9914.31 | 6737.1719 | 4159.8709 | 3481.3455
Flow Hermes | 1478.5386 | 937.8488 | 628.4183 | 492.184 | 571.9309 | 911.9173 | 1620.4936 | 4489.9794 | 6059.5693 | 5960.1939 | 5473.2854 | 5550.8742 | 5596.7767 | 5677.7911 | 5308.4818 | 5252.1657 | 5645.7621 | 5888.771 | 6128.1832 | 5935.7697 | 5263.8469 | 3903.7297 | 2478.3557 | 2074.1059
Flow PHEMLight | 1398 | 984 | 644 | 484 | 553 | 902 | 1516 | 4448 | 5823 | 5889 | 5379 | 5542 | 5487 | 5493 | 5184 | 5142 | 5503 | 5749 | 6064 | 5750 | 5112 | 3883 | 2447 | 888
AIMSUN
PHEMLight
Chart: NOx Emissions per second (PC Diesel Euro 3)
| 22.5 | 24 | 25.5 | 27 | 28.5 | 30 | 31.5 | 33 | 34.5 | 36 | 37.5 | 39 | 40.5 | 42 | 43.5 | 45 | 64.5 | 66 | 67.5 | 69 | 70.5 | 72 | 73.5 | 75 | 76.5 | 78 | 79.5 | 81 | 82.5 | 84 | 85.5 | 87 | 88.5 | 90 | 91.5 | 93 | 94.5 | 96 | 97.5 | 99 | 100.5 | 102 | 103.5 | 105 | 106.5 | 108 | 109.5 | 111 | 112.5 | 114 | 115.5 | 117 | 118.5 | 120 | 121.5
speed | 33.2076 | 30 | 8.9826 | 0 | 0 | 10.3164 | 29.8223 | 25.6964 | 27.5941 | 30 | 47.3472 | 50 | 50 | 50 | 50 | 50 | 24.4534 | 11.227 | 2.8106 | 0.1871 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10.3164 | 34.7952 | 54.0472 | 54.5825 | 51.8267 | 34.9089 | 19.7302 | 7.8099 | 1.4041 | 0.046852 | 8.5945 | 30.1677 | 42.0887 | 54.5825 | 54.5825 | 41.7028 | 22.4437 | 14.6192 | 40.4705 | 48.569 | 48.7408 | 50.0425 | 50.7766 | 51.3724 | 51.8116 | 52.1446
Av. Speed | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615 | 26.615
Panis '06 | 4.0745 | 4.6671 | 5.2638 | 8.676 | 8.676 | 120.3416 | 3.4867 | 21.0711 | 26.6146 | 201.727 | 62.4469 | 34.8622 | 34.8622 | 34.8622 | 34.8622 | 12.6117 | 2.8171 | 4.6622 | 12.8076 | 8.9817 | 8.676 | 8.676 | 8.676 | 8.676 | 8.676 | 8.676 | 8.676 | 8.676 | 8.676 | 120.3416 | 261.6068 | 48.0854 | 6.3539 | -2.6894 | 0.756 | 3.6068 | 4.9782 | 10.8704 | 10.5767 | 108.731 | 126.3353 | 186.2349 | 41.938 | -1.9265 | -0.097329 | 2.8145 | 163.7861 | 114.4543 | 34.7865 | 48.4655 | 43.7656 | 43.2816 | 42.3161 | 41.7081 | 41.2156
PHEMlight | 0 | 0 | 0 | 4.3696 | 4.3696 | 127.1339 | 0 | 23.7575 | 28.1269 | 340.493 | 50.1839 | 17.2261 | 17.2261 | 17.2261 | 17.2261 | 0 | 0 | 0 | 0 | 4.3696 | 4.3696 | 4.3696 | 4.3696 | 4.3696 | 4.3696 | 4.3696 | 4.3696 | 4.3696 | 4.3696 | 127.1339 | 491.1172 | 23.6623 | 0 | 0 | 0 | 0 | 0 | 4.3696 | 4.3696 | 94.1697 | 225.3226 | 312.1734 | 18.2954 | 0 | 0 | 0 | 236.0567 | 174.9037 | 18.3285 | 29.793 | 24.2028 | 22.971 | 21.4363 | 20.5429 | 19.9193
COPERT IV & V | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214 | 21.214
NOx (g/h)

## Slide 17: Future work
Congestion charge scenario
     Total travel time
    = 400 seconds
+400 seconds