## Slide 1: Impact Assessment of Sand and Dust Storms on key socio-economic sectors: Aviation
Developed by: Konstantina Chouta
Directed by: María Gonçalves Ageitos (UPC)
Co-directed by: Sara Basart (BSC), Isadora Christel Jiménez (BSC)
Universitat Politècnica de Catalunya · BarcelonaTECH (UPC)
School of Civil Engineering
October 2020

## Slide 2: List of contents
Research problem
Methodology and tools
Visibility diagnostics and evaluation results
Impact Assessment
Dust-visibility forecast product
Conclusions

## Slide 3: Research problem

## Slide 4
Haze
Drifting sand/dust
Blowing sand/dust
Dust whirls
Sand and Dust storms
Visibility
Reduction
GEOS-5 Aerosol Optical Depth (AOD) Source: NASA (2014)
Definitions by WMO
Orange: Mineral dust

## Slide 5
23 March 2018 Heraklion Airport closed for 8.5h
26 flights affected
308,000 EUR
Source: InDust project
Source: NASA Terra

## Slide 6: Available dust information
Dust monitoring (observations)
 satellite
 remote sensing
ground-based monitoring networks
 experimental campaigns
 indirect observations (visibility)
Dust forecasting (modelling)
atmospheric numerical models

## Slide 7
Develop a dust-related forecast product for the aviation sector, that predicts the visibility reduction due to sand and dust storms (SDS) in North Africa, the Middle East and Europe.
Implement a visibility diagnostic from the atmospheric composition NMMB-MONARCH model output, after testing different parametrisations.
Develop a methodology for the evaluation of the NMMB-MONARCH model on surface level using visibility observations.
Assess the impact of desert dust events on the aviation sector in dust-prone areas based on visibility reduction estimations.
Project aim

## Slide 8: Methodology and tools

## Slide 9
NMMB-MONARCH
Meteorological core NMMB by NCEP
Chemistry module
MONARCH by BSC
Aerosols
Gas-phase
Data
Assimilation
Volcanic Ash
Sea-salt
Sulphates
POA
OC/BC
Mineral Dust
International Cooperation for Aerosol Prediction
Operational forecasts for:
Tools: The NMMB-MONARCH model
Pérez et al., 2011;Haustein et al., 2012
Janjic et al., 2005; 2007; 2011
DiTomaso et al., 2016
Jorba et al., 2012;Spada et al,, 2013
Badia and Jorba, 2016

## Slide 10
Aerosol ground networks
Weather stations in airports
Visibility as an indirect source
Tools: Observations
Integrated Surface Database (NOAA)
(Smith et al., 2011)

## Slide 11
NMMB-MONARCH output
Visibility parametrisations
Predicted visibility
Input
Process
Surface extinction coefficient
PM10
ISD Observations
Observed visibility
Decoding, Quality Control, Dust filtering
Output
101 stations
Methodology
Selected visibility
diagnostic

## Slide 12
Model Configuration
Period: 2018-2019
Domain: North Africa, Middle East, Europe
Horizontal resolution: 0.1°x 0.1° (~ 10km)
Vertical resolution: 40 σ-layers (up to 15km)
Temporal resolution: 3h
Initial conditions: NCEP/GFS
NMMB-MONARCH simulation
Source: Barcelona Dust Forecast Center oficial webpage, hhtp://dust.aemet.es/

## Slide 13
Type | Name | Equation | References
Physically-based | Koschmieder |  | Godish, 1997
Physically-based | Biral |  | Bennett, 2012
Empirical | IZO |  | Camino et al., 2015 (Tenerife, Spain)
Empirical | D´Almeida |  | D’Almeida, 1986 (Niger, Sahel)
Empirical | Dayan |  | Dayan et al., 2008 (Israel)
Type | Name | Equation | References
Physically-based | Koschmieder |  | Godish, 1997
Physically-based | Biral |  | Bennett, 2012
Empirical | IZO |  | Camino et al., 2015 (Tenerife, Spain)
Empirical | D´Almeida |  | D’Almeida, 1986 (Niger, Sahel)
Empirical | Dayan |  | Dayan et al., 2008 (Israel)
Visibility Parametrisations
Y: Extinction coefficient or
Y :PM10 mass concentration

## Slide 14
Category 3
Sand and dust storms
Category 1
Dust in suspension
Category 2 Moderate dust events
Category 0
clean atmosphere
8000
1000
5000
Boudghene Ben Ali Lotfi Airport (N31°39.16', W2°15.40') in Béchar, Algeria
Visibility (m)
From continuous to categorical values

## Slide 15
Misses
Contingency table for categorical evaluation -2018
Frequency of observed visibility categories (%)
Frequency of predicted visibility categories (%)
Koschmieder parametrisation
81.59 | 0.12 | 0.01 | 0.00 | Category 0
12.49 | 0.14 | 0.02 | 0.00 | Category 1
4.88 | 0.37 | 0.08 | 0.00 | Category 2
0.21 | 0.05 | 0.03 | 0.00 | Category 3
Category 0 | Category 1 | Category 2 | Category 3 | 
Hits
False Alarms
 81.72%
 12.65%
 5.33%
 0.30%
Sand and dust storms
Dust in suspension
Moderate dust events
Clean atmosphere

## Slide 16
Category 0 (V>8km) is overpredicted by all parametrisations.
Category 1 (8km<V<5km) is underpredicted by all parametrisations.
Category 2 (5km<V<1km) is underpredicted by all parametrisations.
Category 3 (V<1km) is strongly underpredicted by IZO, D’Almeida and Dayan parametrisations and not predicted at all by Koschmieder and Biral.
V= Visibility
Categorical evaluation results 2018-2019

## Slide 17
Categorical evaluation results 2018-2019
X
Model´s
grid cell(2D)
Observer´s point (1D)
10km
10km
Linear
measurement
Bi-linear interpolation
Visual reference
Predicted visibility
Observed visibility
Particle diameter up to 10μm
Particle diameter up to 60μm
Empirical parametrisations can compensate this difference.

## Slide 18
Category 0 (V>8km) is overpredicted by all parametrisations.
Category 1 (8km<V<5km) is underpredicted by all parametrisations.
Category 2 (5km<V<1km) is underpredicted by all parametrisations.
Category 3 (V<1km) is strongly underpredicted by IZO, D’Almeida and Dayan parametrisations and not predicted at all by Koschmieder and Biral.
The physically-based parametrisations present higher overall accuracy.
V= Visibility
Categorical evaluation results 2018-2019
Local events (Haboobs)

## Slide 19
Koschmieder-calibrated
Calibration of the Koschmieder diagnostic- 2018
Frequency of observed visibility categories (%)
Frequency of predicted visibility categories (%)
77.30 | 3.30 | 1.12 | 0.00 | Cat0
10.75 | 1.13 | 0.77 | 0.00 | Cat1
3.37 | 0.78 | 1.18 | 0.00 | Cat2
0.11 | 0.04 | 0.15 | 0.00 | Cat3
Cat0 | Cat1 | Cat2 | Cat3 | 
Frequency of observed visibility categories (%)
Frequency of predicted visibility categories (%)
81.59 | 0.12 | 0.01 | 0.00 | Cat0
12.49 | 0.14 | 0.02 | 0.00 | Cat1
4.88 | 0.37 | 0.08 | 0.00 | Cat2
0.21 | 0.05 | 0.03 | 0.00 | Cat3
Cat0 | Cat1 | Cat2 | Cat3 | 
Koschmieder- not calibrated
+ c
Y: Extinction coefficient
a = 1.50- 3.92 | b= -1 | c=0 (Li et al., 2016)

## Slide 20: Impact Assessment for aviation

## Slide 21
Source: Commission Regulation (EU) No 748/2012
Aviation thresholds and airport classification
 | Flight rules | Visibility (m)
Approach and landing | Visual references | >5000
 | Navigation instruments | >800
 | Low visibility protocols | <550
Flow reduction | - | <1000
Operations under low visibility (<800m)
Green, yellow: yes
magenta, red: no
Number or airports in the studied domain= 2248
Source: Votsis et al., 2020, DustClim Technical Report

## Slide 22
Number of days with exceedance of aviation-related thresholds - 2018
V>5000m
90
365
270
180
60
30
0
Number of days
V>1000m
90
365
270
180
60
30
0
Number of days
V>550m
90
365
270
180
60
30
0
Number of days
V>800m
90
365
270
180
60
30
0
Number of days
V= Visibility

## Slide 23: Dust-visibility forecast product

## Slide 24
Dust-visibility forecast
20,000
8,000
5,000
1,000
800
550
0
Visibility (m)
Estimated cost ̴ 34,000€/ year
Economic loss- closure of 1 Greek airport for 9h
308,000 EUR (InDust Project)

## Slide 25: Conclusions

## Slide 26
The process followed has served to establish a methodology for forecast verification in areas where observations from air quality networks are scarce.
    Weather stations in airports can be used as an alternative source of observations.
Five different methods have been tested to diagnose visibility from the NMMB-MONARCH model. These methods relied either on physically-based or empirical parametrisations. Their comparison revealed that the physically-based (Koschmieder) parametrisations are more suitable for operational purposes, due to their higher accuracy and their applicability to different geographical domains.
The Koschmieder parametrisation has been selected for the NMMB-MONARCH model to estimate visibility. Its performance has been improved with calibration, based on the evaluation results.
    Improved predictions for visibility values between 1-8km (dust in suspension and moderate dust events).
The categorical evaluation of the NMMB-MONARCH model with visibility observations obtained from meteorological reports has revealed that it is a useful tool to mitigate the environmental risks related to air operations.
    It also provided interesting information about the model´s performance and the nature of its weaknesses, which could be useful for future developments.
Conclusions

## Slide 27
Based on estimations of visibility reduction by the selected and calibrated Koschmieder diagnostic, the number of days with potential impacts in the flow of air operations have been estimated for airports located in North Africa, the Middle East and Europe.
    Due to the limitations of the diagnostics revealed in the evaluation, this impact analysis is considered low estimation of the reality.
The final forecast product that has been designed and especially the methodology established for its verification has great potential and it can be considered for implementation under the framework of the Barcelona Dust Forecast Center of the WMO.
Conclusions

## Slide 28: Thank you for your attention!
Acknoweldgements to Sara Basart, Isadora Jiménez, María Gonçalves, Oriol Jorba, Ernest Werner, as well as to the Earth Sciences Department of Barcelona Supercomputing Center – Centro Nacional de Supercomputación (BSC-CNS). The long-term dust research program at the of Barcelona Supercomputing Center – Centro Nacional de Supercomputación (BSC-CNS) is associated to the AXA Research Fund. Special thanks to the WMO SDS-WAS NAMEE Regional Center, the WMO Barcelona Dust Forecast Center, AEMET and the European projects InDust (COST Action CA16202 supported by COST Assocation) and DustClim (as a part of ERA4CS, an ERANet initiated by JPI Climate, and funded by FORMAS (SE), DLR (DE), BMWFW (AT), IFD (DK), MINECO (ES), ANR (FR) with co-funding by the European Union Grant 690462) projects.