## Slide 1: Atmospheric dust transport models and usage
Elina Karnezi (eleni.karnezi@bsc.es)
Earth Sciences Department, Barcelona Supercomputing Center (BSC)
16/05/2019
inDust COST Action: The Effect of Soiling on Solar Energy, Munich, Germany

## Slide 2
Organic Carbon + Elemental carbon
Dust
Sulfate
Sea salt
Dust cycle and its extension
NASA | GEOS-5 Aerosols
Notes: Dust transport is a global phenomenon and the surface winds are the main driver of it. This is a simulation from NASA using GEOS-5 and the GOCART (Goddard Chemistry Aerosol Radiation and Transport) Model. With orange it shows the dust transport and we see that it mostly transported in the Northern Hemisphere.

## Slide 3
Image from WMO website (http://www.wmo.int/pages/prog/arep/wwrp/new/hurricanes.html)
Ecosystems, meteorology and climate
Air Quality and Human Health
Aviation and Ground Transportation
Energy and industry
Agriculture and fishering
Astrophysics
Motivation – Dust impacts
Notes: Dust and dust transport has many impacts, most of them adverse. In climate it has in two way, in direct by scattering and absorbing solar radiation and indirectly by acting as a ccn so in having an effect in cloud formation. It can contribute to high levels of PM10 and cause health problems as asthma and more respiratory and cardiovascular diseases and for long time exposure, even premature death. It can cause also disruption through flight delays and closure on highways. Impacts on energy, as solar energy, with soiling effects as our workshop focus today and solar irradiance. In agriculture and fishering, where with the deposition of dust, the nutrients that are included can favor both. Finally on the observations of stars, in astrophysics.

## Slide 4
Dust models are a mathematical representation of atmospheric dust cycle.
Dust forecasting models
Notes: Modelers use dust models as a mathematical representation of atm. dust cycle. These models are 3D models, with horizontal grids, from latitude and longitude and vertical grids expressed as height or in pressure levels.
The atmospheric dust cycle involves a variety of processes:
Dust emission from dry unvegetable surfaces (dust sources)
Mid- and long-range transport
Sedimentation and wet and dry deposition

## Slide 5
NMMB-MONARCH:
Atmospheric Composition and Air Quality
· The main system is build on the meteorological driver NMMB
· Multiscale: global to regional scales allowed (nesting capabilities)
· Nonhydrostatic dynamical core: single digit kilometre resolution allowed
· Fully on-line coupling: weather-chemistry feedback processes allowed
· Enhancement with a data assimilation system
Known as NMMB/BSC-Dust
Notes: BSC has developed the NMMB-MONARCH model (multiscale online nonhydrostatic atmosphere chemistry model) that can be run either globally or regionally, thanks to its unified nonhydrostatic dynamical core. It is based on thee online coupling of the meteorological model with a full aerosol-chemistry model.
And NMMB/BSC-Dust model specifically contains the dust module embedded online with NMMB and provides weather and dust forecasts.

## Slide 6: Mineral Dust Services
BSC dust operational forecast (global and regional domains)
  Contribution to the SDS-WAS (regional) and ICAP (global) multi-model ensembles
WMO Dust Regional Centers
  Barcelona Dust Forecast Center. First specialized WMO Center for mineral dust prediction. Started in 2014 - Operational
    http://dust.aemet.es
    @Dust_Barcelona
  SDS-WAS Regional Center. Sand and Dust Storm Warning Advisory and Assessment System. Started in 2010 – Research
    http://sds-was.aemet.es
Notes: SDS-WAS sand and dust storm warning advisory and assessment system
At the global scale, the model contributes to the ICAP International Cooperative for Aerosol Prediction multi-model ensemble.
The NMMB-MONARCH dust regional daily forecasts contribute to the Regional Center of the WMO Sand and Dust Storm Warning Advisory and Assessment System (SDS-WAS) dust forecast model intercomparison (https://sds-was.aemet.es) and it is the reference model of the operational WMO Barcelona Dust Forecast Center (https://dust.aemet.es/).

## Slide 7: Barcelona Dust Forecasting Center
@Dust_Barcelona
http://dust.aemet.es/

## Slide 8
http://dust.aemet.es/
@Dust_Barcelona
72-hours forecasts of:
Dust Optical Depth at 550nm
Dust Dry and Wet Deposition
Dust Load
Dust Surface Concentration
Dust Surface Extinction at 550nm

## Slide 9
SDS-WAS and the NAMEE Regional Center
http://sds-was.aemet.es/
Notes: SDS-WAS sand and dust storm warning advisory and assessment system

## Slide 10
Model intercomparison
  Products: surface concentration and DOD maps, the SDS-WAS multi-model product.
SDS-WAS and the NAMEE Regional Center
Operational
SDS-WAS Ensemble
12 Global – Regional models from ~ 100 to 10 km
http://sds-was.aemet.es/
Notes: Contribution to the SDS-WAS (regional) multi-model ensembles with 11 more global and regional models with resolutions 10 to 100 km.

## Slide 11
Applications in Solar Energy
Solar irradiance
  The presence of dust reduce the incoming solar irradiance through direct radiative effect
  but also indirectly, through favouring cloud formation
(Soret et al., 2016 )
Year 2014
Notes: Dust intrusion from Africa favored the cloud formation.
All models, here BSC models with multiple resolutions and WRF with their forecasts overpredicted solar irradiance. Measurements showed more cloud cover that day than the models predicted.

## Slide 12
Applications in Solar Energy
Soiling
  panels efficiency and water management
Notes: Dust act like barriers and they decrease panels efficiency.
CSP plants are being implemented in dusty environments such as Middle East and North Africa where solar radiation is high. But usually in these areas, water is in scarcity or very expensive.
The minimization of soiling-induced losses together with the reduction of cleaning costs is a challenge for operators and project planners.

## Slide 13
The solutions will be implemented at two CSP operational sites:
La Africana, Site location: Posadas, Córdoba, Spain
SEDC plant, Site Location: Rotem, Israel
Provide near to market solutions for reducing the water consumption of CSP
H2020SOLWATT project targets a significant reduction in the water used by CSP plants (by 35% for wet cooled & by 90% for dry cooled). In this way more of 0.5 M€/year of operational cost for a 50 MW CSP plant will be saved in the future.
SOLWATT project
Notes: The project focuses on the efficiency of innovations on solar field cleaning, power-block cooling, water recycling system, and plant operation strategy. The social acceptance of CSP will be increased by detailed analysis of case studies and education of local population to the benefits of solar energy.

## Slide 14
 O&M optimizer supported by soiling forecasts assures that innovative water-saving technologies are used in the best way.
SOLWATT project
Notes: WP2 includes the development of an unique soiling forecast product that will be included in the O&M optimizer. This additional input information will assure that innovative water-saving technologies are used in the best way.
Soiling forecast model will be developed coupling the outputs of an atmospheric composition model with a soiling model.

## Slide 15
Soiling-Downscaling
Operational forecasts
Prediction over specific locations
Biggest solar plant in EU in Hungary is
300,000m2  This is 0,3km2 vs 100km2 from the model
Notes: 15

## Slide 16
Merge of dust-soiling model
The DLR Institute of Solar Research (SF) is the largest research entity in Germany investigating and developing concentrating solar technologies to provide heat, electricity and fuel.
DLR has developed a soiling model that has been validated for two sites during WASCOP –Water Saving for Concentrated Solar Power (H2020 project).
Next presentation: Soiling modelling with ground data (Fabian Wolfertstetter)
Notes: We couple the dust regional-global NMMB-MONARCH model developed and maintained by BSC and the WASCOP soiling model developed by DLR.
Both models will exchange several parameters like particle number concentration by size, and other measured weather parameters.
a) Annual average of modelled column-dust optical depth at 550 nm for 2015 based on BSC-DUST b) Soiling rate (SR) determined with the WASCOP empirical model from ground atmospheric measurement data and plotted against the measured soiling rate for PSA. Data in daily resolution from 2.5 years.

## Slide 17
Operational dust atmospheric forecast
BSC model is going to be run for the years selected from DLR in order to provide inputs for the soiling model.
Its evaluations until now for various AERONET stations are satisfactory.

## Slide 18
Model evaluation results
Notes: 24-hour forecasts (on 3-hourly basis) of dust aerosol optical depth (DOD) from NMMB-MONARCH daily operational forecasts (MONARCH-GLOB, MONARCH-REG-033 and MONARCH-REG-010) have been validated for the year of 2015 against AERONET SDA AODcoarse cloud-screened observations over the study region and compare with the SDS-WAS Multi-model Median DOD. The SDS-WAS Multi-model Median DOD is obtained from twelve dust prediction models participating in SDS-WAS Regional Center.

## Slide 19
Model evaluation results
Notes: 24-hour forecasts (on 3-hourly basis) of dust aerosol optical depth (DOD) from NMMB-MONARCH daily operational forecasts (MONARCH-GLOB, MONARCH-REG-033 and MONARCH-REG-010) have been validated for the year of 2015 against AERONET SDA AODcoarse cloud-screened observations over the study region and compare with the SDS-WAS Multi-model Median DOD. The SDS-WAS Multi-model Median DOD is obtained from twelve dust prediction models participating in SDS-WAS Regional Center.

## Slide 20
Summary
SOLWATT will provide:
  Operational soiling forecasts: up to 5-days soiling forecasts based on the daily operational dust NMMB-MONARCH system.
To achieve this objective, the dust atmospheric NMMB-MONARCH model will be coupled with a soiling model.
  The evaluation of NMMB-MONARCH (the inputs used by the soiling model) shows that the model can predict the desert dust cycle over North Africa, Middle East and Europe.
    Over the Mediterranean, the model is capturing the timing and the magnitude of the dust events. The model can not reproduce the haboobs (associated to convective events) in the current operational configurations.
    In middle east the model is overestimating the summer events.
  Ongoing improvements in the description of the desert sources in the Middle east and Africa. Next, evaluation of the deposition fields.
Notes: We will couple the dust regional-global NMMB-MONARCH model developed and maintained by BSC and the WASCOP soiling model developed by DLR.
Both models will exchange several parameters like particle number concentration by size, and other measured weather parameters.
The resulting soiling forecast rates will be evaluated for the various forecasting horizons over the two CSP operational sites considered in SOLWATT.
As a result, within SOLWATT we will provide:
  Operational soiling forecasts: up to 5-days soiling forecasts based on the daily operational dust MONARCH system.
  A soiling rate map: based on a dust NMMB-MONARCH reanalysis for Northern Africa, Middle East and Europe.

## Slide 21: Thank you
eleni.karnezi@bsc.es
Notes: InDust (COST Action CA16202, www.cost-indust.eu). Also thanks to AXA Research Fund for funding aerosol research at the Barcelona Supercomputing Center through the AXA Chair on Sand and Dust Storms.

## Slide 22: Backup slides

## Slide 23: Soiling Model

## Slide 24: Soiling Model performance

## Slide 25: Soiling Model and cleaning optimization

## Slide 26
MODIS true colour composite image for March 2005 depicting a dust storm initiated at the Bodélé Depression (Chad Basin)
MODIS True color Western Africa – Altantic Ocean
Dust cycle and associated processes