## Slide 1: Bringing the complexity of organic chemistry to climate models with machine learning techniques
Camille Mouchel-Vallon, Alma Hodzic, John Schreck, Charlie Becker, Keeley Lawrence, Siyuan Wang, Jinkyul Choi, Daven Henze, David John Gagne
PASC24, Zürich, 2024/06/05
#PlanDeRecuperación

## Slide 2: Context
1st objective: A high resolution spatial (up to 2.5x2.5 km) and temporal (hourly) emissions system to compute emissions of primary atmospheric pollutants for Spain to be used in the national air quality prediction system.
Gaseous primary atmospheric pollutants
NOx, CO, SOx, NH3, NMVOCs
Non-Methane Volatile Organic Compounds are emitted by human and natural activities and their chemical evolution in the atmosphere has an impact on air quality, health and climate

## Slide 3
Distribution of emitted organic compounds families for two different inventories in Europe, China and USA
(Huang et al., 2017)
Primary organic compounds: many sources, high diversity, high uncertainty

## Slide 4
Measured fire emissions composition
(Hatch et al., 2017)
Indonesian peat fire
Chinese rice straw
Primary organic compounds: many sources, high diversity, high uncertainty

## Slide 5
Primary organic compounds: many sources, high diversity, high uncertainty
Inventory of terpenoids emitted by plants
(Graedel, 1979)
isoprene

## Slide 6
Atmospheric Evolution of Organics : formation of oxidized compounds
Volatile Organic Compounds
Biogenic and anthropogenic emissions
Oxidized Volatile Organic Compounds
Gaseous oxidation
Secondary Organic Aerosol
Low volatility
Oxidized Volatile Organic Compounds
Dissolution
Dissolution
Activation
Aqueous oxidation
Wet and dry deposition

## Slide 7
Volatile Organic Compounds
Biogenic and anthropogenic emissions
Oxidized Volatile Organic Compounds
Gaseous oxidation
Secondary Organic Aerosol
Low volatility
Oxidized Volatile Organic Compounds
Dissolution
Dissolution
Activation
Aqueous oxidation
Wet and dry deposition
Measured PM1 composition
Jimenez et al. (2009)
Atmospheric Evolution of Organics : formation of oxidized compounds

## Slide 8
Volatile Organic Compounds
Biogenic and anthropogenic emissions
Oxidized Volatile Organic Compounds
Gaseous oxidation
Secondary Organic Aerosol
Low volatility
Oxidized Volatile Organic Compounds
Dissolution
Dissolution
Activation
Aqueous oxidation
Wet and dry deposition
Contributions to rain composition in the tropics
Bakayoko et al. (2021)
Atmospheric Evolution of Organics : formation of oxidized compounds

## Slide 9
OVOC
Dissolution
Dissolution
Activation
VOC
Biogenic and anthropogenic emissions
OVOC
Gaseous oxidation
SOA
Low volatility
Aqueous oxidation
Wet and dry deposition
hygroscopicity
optical properties
Climate impacts
ozone chemistry
particulate matter composition
Air quality and health impacts
rain composition
inputs to soils
Ecosystems impacts
Impacts

## Slide 10
Progressive and complex oxidation of organics
Parent
Hydrocarbon
1st Generation
Species
2nd Generation
Species
CO2
How to bring this complexity to air quality models?
Volatile Organic Compounds
Oxidized Volatile Organic Compounds
Gaseous oxidation

## Slide 11
How I Learned to Stop Worrying and Love the Complexity
Master Chemical Mechanism (Jenkin et al., 1997; 15yrs 2-3people ?)
143 precursors from C1 to C12
17000 reactions of 6700 species
Simplified!
CLEPS (Mouchel-Vallon et al., 2017; 2yrs 2people)
Cloud oxidation of C1-C4 products from isoprene oxidation
1315 reactions involving 717 chemical species
Simplified!
Handwritten detailed mechanisms: high potential for errors and time consuming (creation and maintenance)

## Slide 12
Master Chemical Mechanism (Jenkin et al., 1997; 15yrs 2-3people ?)
143 precursors from C1 to C12
17000 reactions of 6700 species
Simplified!
CLEPS (Mouchel-Vallon et al., 2017; 2yrs 2people)
Cloud oxidation of C1-C4 products from isoprene oxidation
1315 reactions involving 717 chemical species
Simplified!
Handwritten detailed mechanisms: high potential for errors and time consuming (creation and maintenance)
Potential number of distinct species in a full oxidation mechanism as a function of the size of the precursor
Aumont et al. (2005)
How I Learned to Stop Worrying and Love the Complexity

## Slide 13: We need to go faster
Writing the chemical mechanism
Solving the ODEs in a (3D) model

## Slide 14
Automating boring things
Systematic and repeated oxidation steps
Generator for Explicit Chemistry and Kinetics of Organics in the Atmosphere
(GECKO-A, Aumont et al., 2005)

## Slide 15
Aumont et al., 2005
Automating boring things

## Slide 16: Accelerating things
Writing the chemical mechanism
Solving the ODEs in a (3D) model
GECKO-A
Machine learning?
12 biogenic, 53 anthropogenic precursors
23 million reactions involving 4.4 million species
(Mouchel-Vallon et al., 2020)
Simulating 2 days in 2 grid cells
≈ 36 hours on 16 cores

## Slide 17: Emulating atmospheric chemistry
Use GECKO-A 0D explicit simulations as training dataset
Emulate the behavior of the detailed model with machine learning
Computationally expensive
Neural Networks (NN)
Random Forest (RF)

## Slide 18: NN approach for predicting time-series of concentrations
Schreck et al. JAMES 2022: Neural network emulation of the formation of OA based on the explicit GECKO-A chemistry model
1. Multi-layer perceptron MLP model
Outputs
Inputs
Pre-existing OA (ti)
OH (ti)
O3 (ti)
NOx (ti)
Precursor (ti)
SOG (ti)
SOA (ti)
T (ti)
SZA (ti)
1748 neurons
Hidden layer
…
Precursor (ti+1)
SOG (ti+1)
SOA (ti+1)

## Slide 19: NN approach for predicting time-series of concentrations
Schreck et al. JAMES 2022: Neural network emulation of the formation of OA based on the explicit GECKO-A chemistry model
1. Multi-layer perceptron MLP model
Outputs
Inputs
Pre-existing OA (ti)
OH (ti)
O3 (ti)
NOx (ti)
Precursor (ti)
SOG (ti)
SOA (ti)
T (ti)
SZA (ti)
1748 neurons
Hidden layer
…
Precursor (ti+1)
SOG (ti+1)
SOA (ti+1)
2. Gated-recurrent unit GRU model
Gated Recurrent Unit (GRU)
Hidden state h(ti-1)
Hidden state h(ti)

## Slide 20: Generate Neural Network training dataset with GECKO-A
2,000 random experiments for each precursor
5 days / 5 minutes output
2.9 × 106 samples (80% training, 20% validation)
3 precursors: toluene, dodecane, a-pinene
Random environmental conditions
No diurnal variations
Initial precursor amounts of 10 ppt, 0.1 and 1 ppb
Schreck et al., JAMES, 2022

## Slide 21: Neural Network training dataset
Effect of T on condensation
Targets
Predictors
OH ↑
Precursor ↓
Organic gas ↓
Organic aerosol ↑
Schreck et al., JAMES, 2022

## Slide 22: Multi-Layer Perceptron vs. Gated-Recurrent Unit network
30-ensemble member predictions for Toluene
GECKO-A true
NN mean, 30 members
GECKO-A true
NN mean, 30 members
Multi-layer perceptron
GRU performs better but is challenging to implement in a 3D model
Gated-recurrent unit
GECKO-A true
NN mean, 30 members
Precursor exponential decay well captured
Schreck et al., JAMES, 2022

## Slide 23: Application in a box model for diurnally varying conditions
GECKO-A vs. GECKO-MLP
Neural Networks trained on datasets built under constant conditions cannot reproduce realistic diurnal cycles
Raises the question of the representativeness of the training data sets

## Slide 24: Computational gain GECKO-A vs. GECKO-NN
For Toluene, GECKO-NN is 4×102 times faster than GECKO-A on CPU, and 104 times faster on GPU
Ratio of GECKO-A / GECKO-NN
Timing per 5min timestep

## Slide 25: Random Forest approach
P(ti)
G(ti)
A(ti)
E(ti)
G(ti+1)
A(ti+1)
Tree 1
Prediction 1
Tree 2
Prediction 2
Tree N
Prediction N
…
Averaging predictions
Inputs :
Precursor concentration
Gas organic concentration
Aerosol organic concentration
Temperature
Solar zenith angle
Pre-existing aerosol
O3
NOx
OH
Output :
Gas organic concentration
Aerosol organic concentration
Mouchel‐Vallon & Hodzic, JGR, 2023:
Toward emulating an explicit organic chemistry mechanism with random forest models.
E(ti)
A(ti)
G(ti)
P(ti)
G(ti+1)
A(ti+1)

## Slide 26: Random Forest: Realistic training dataset
2 precursors: toluene, dodecane
Random environmental conditions
With diurnal variations
Random initial precursor concentration
From 3D model tropospheric ranges
0 60 120 240
Only 2 targets
10 days / 5 min output
1×106 samples/precursor

## Slide 27: Random Forest results: examples
RF perform similarly to NN
The training set allows reproducing the diurnal cycles
organic gases
organic aerosol
GECKO-A
Random Forest
time /day

## Slide 28: Random Forest results: performance
Increasing the number of training samples improves performance
error accumulation
diminishing returns of increasing the size of the training sample

## Slide 29: Random Forest results: errors distribution
increasing error
Little sensitivity of errors to the aerosol quantity to predict (seed, yield, mass)
Errors sensitive to NOx regime and OH mixing ratios: underrepresented regimes in training set
RO2 + NO
RO2 + HO2

## Slide 30: Random Forest results: specializing random forests
Do performances improve if the range of chemical regimes to predict is reduced?
Specialization requires more or better constructed training data
toluene | dodecane
1×105 | 7×104
6×105 | 3×105
4×105 | 7×105
# training points

## Slide 31: Random Forest results: predictors relative importance
The importance of predictors (mean decrease impurity) is similar for both species
Distribution of importance and predictive ability among correlated variables

## Slide 32: Random Forest results: reducing the number of predictors
Do performances improve if the number of predictor is reduced?
Reducing the number of (correlated?) predictors is beneficial for the worst performing simulations
Importance of selecting predictors and dimensionality reduction

## Slide 33: First tests in a global model: VBS vs. GECKO-NN
GEOS-Chem Monthly average Toluene SOA (May 2016)
VBS Hodzic et al., 2016
GECKO-NN-MLP
ug/m3
ug/m3
GECKO-NN simulations are
stable over several months
within a factor of 2 of the VBS parametrization for Toluene-SOA.
Implementing GECKO-NN in Geos-Chem

## Slide 34: Conclusions and Outlook
It is possible to emulate the behavior of detailed atmospheric chemistry models with machine learning
Long term stability can be achieved for recurrent neural networks with GRU
The training dataset must be carefully constructed to cover all environmental conditions
Random forests can perform similarly to NN+GRU
Predictors selection is crucial
Current and future works at BSC
Bring the complexity of organic chemistry to air quality models, built on the development of detailed Spanish emissions
Explore ML use, with lessons learned from this work: start again from the basics and systematic exploration by (i) progressively increasing chemical complexity (from toy mechanisms to GECKO-A complexity) and (ii) testing multiple families of ML techniques (RF, NN, GraphNet …)
Implementation in the MONARCH air quality model

## Slide 35: Thank you for your attention
camille.mouchel@bsc.es