## Slide 1
From day ahead to decadal wind power forecasting
Consorcio Español
Support by
Francisco Doblas-Reyes, Albert Soret, Melanie Davis, Verónica Torralba Fernandez, Nube Gonzalez-Reviriego
Notes: Current site selection practices use the retrospective wind speed climatology, with an assumption that the past will also represent the future. Recent advances in climate predictions can provide a more informative view by modeling future wind over months to decades: they use both an analysis of the past climate system, as well as its current state at the specific time when the prediction is created to provide a probability of different future outcomes, with an indication as to which will be the most likely.
It has been demonstrated that climate predictions can improve upon using climatology at some spatial and temporal scales, so decision makers now have a new set of climate risk management tools that can strengthen their decision making, but are they ready to use them?

## Slide 2
EUPORIAS: EUropean Provision Of Regional Impact Assessment on a Seasonal-to-decadal timescale
SPECS: Seasonal-to-decadal climate Prediction for the improvement of European Climate Services
NEWA: New European Wind Atlas
Notes: Climate predictions come with a new set of challenges for end users: information is often un-tailored and hard to understand or apply in a decision-making context. A new generation of European projects, including NEWA, SPECS and EUPORIAS aim to address these challenges and support the development of a new realm of climate services and tools using climate predictions. Here we will present the state-of-the-art in wind speed and power prediction methodologies, to include: initialisation of ensemble simulations; post-processing using bias correction or calibration and validation to assess the prediction skill, as well as new climate prediction visualisation tools and interfaces tailored to the energy sector.
To assess these needs it is need to further tailor, validate, harmonise and improve the presentation and communication of climate information for all timescales in the past and in the future.

## Slide 3
  Initial-value problems (weather forecasting) to forced boundary condition problem (climate projections)
  Climate forecasts (sub-seasonal, seasonal and decadal) in the middle
Meehl et al. (2009)

## Slide 4
  Wind power variability at monthly to decadal time scales has not been traditionally taken into account in wind power facilities planning and management
  In other sectors as hydropower or electricity generation and demand balance, climate information on seasonal-to-interannuel time scales have already been illustrated for management decisions.
Hydroelectric power management
Electricity demand
Notes: Wind resource is one of the fastest growing and most volatile forms of electric power generation, improved forecast beyond the first tow weeks of renewable power generation can improve the strategic and operational management of renewable power during the pre- and post-construction phase.

## Slide 5
Wind farm planners: Site selection
Wind farm investors: Evaluate return on investments
Policy makers: Understand changes to energy mix
Pre-Constuction Decisions:
Annual to Decadal Timescales
Notes: - For the pre-construction phase, forecasts (from annual to decadal timescales) support strategic decisions for these end-users: investors, planners, policy makers.
Information to answer questions such as: where should I locate my farm, what is the risk to my investment, how will the national energy mix change over time?

## Slide 6
Energy producers: Resource management strategies
Energy traders: Resource effects on markets
Wind farm operators: Planning for maintenance works
Wind farm investors: Optimize return on investments
Post-Construction Decisions:
Monthly to Seasonal Timescales
Notes: - For the post-construction phase, forecasts from monthly to seasonal timescales support operational and maintenance (O&M) decisions for these end-users: producers, traders, operators, investors.
Information to answer questions such as: when is the optimal time to undertake works on my wind farm, what is the risk to the scheduling of boats to repair offshore wind farms?

## Slide 7
  Objective within the NEWA project
  To complement the probabilistic mesoscale model chain with climate predications to produce predictability information at different scales/horizons:
    hours
    days
    weeks
    seasons
    and decades

## Slide 8
Capacity Factor (%)
Differences with NAO + and NAO - conditions
Some examples:
Impact of NAO on Wind Speed and Capacity Factor
NAO Index
Wind Speed (m/s)
10m wind speed “observations”: ERA-Interim
Boreal winter season period 1981-2012

## Slide 9
Some examples:
Seasonal wind power predictions
9

## Slide 10
Some examples:
RESILIENCE Prototype (EUPORIAS project)
10

## Slide 11
Some examples:
RESILIENCE Prototype (EUPORIAS project)
11

## Slide 12
Some examples:
RESILIENCE Prototype (EUPORIAS project)
12

## Slide 13
Some examples:
RESILIENCE Prototype (EUPORIAS project)
113

## Slide 14
Thank you!
For further information:
albert.soret@bsc.es

## Slide 15
CHALLENGE : models don’t provide capacity factor forecasts.
The wind power can be estimated from predictions of wind speeds and temperatures at the surface.
Limitations:
The wind turbines are at 100m so 10m wind speed must be scaled up.
Seasonal/monthly means of wind speed and temperature masks sub-seasonal/daily variability.
Introduction Methods Results Summary Future work
Notes: Daily variability is not captured

## Slide 16
PREDICTIONS OF CAPACITY FACTOR
Forecasts
10m Wind Speed
2m Temperature
Past Observations
10m Wind Speed
2m Temperature
POTENTIAL SOLUTION: The wind power can be estimated from predictions of wind speeds and temperatures at the surface.
Introduction Methods Results Summary Future work
7

## Slide 17
PREDICTIONS OF CAPACITY FACTOR
Corrected forecasts
Post-processing
10m Wind Speed
2m Temperature
10m Wind Speed
2m Temperature
Past Observations
10m Wind Speed
2m Temperature
Introduction Methods Results Summary Future work
Forecasts
8

## Slide 18
10m Wind Speed
ECMWF S4 1 month lead and ERA Interim
in DJF (1981-2013)
Introduction Methods Results Summary Future work
Simple bias correction
Calibration
Raw data
RPSS
Cumulative probability
Cumulative probability
Rank i
Rank Histograms
Forecast quality assessment
Region of Canada
Cumulative probability
Rank i
Cumulative probability
Cumulative probability
Cumulative probability
Cumulative probability
Rank i
9

## Slide 19
PREDICTIONS OF CAPACITY FACTOR
Corrected forecasts
MacLeod’s methodology
Past Observations
10m Wind Speed
2m Temperature
Capacity factor
Post-processing
10m Wind Speed
2m Temperature
10m Wind Speed
2m Temperature
10m Wind Speed
2m Temperature
Past Observations
Introduction Methods Results Summary Future work
Forecasts
10

## Slide 20
PREDICTIONS OF CAPACITY FACTOR
Corrected forecasts
Past Observations
10m Wind Speed
2m Temperature
Capacity factor
Post-processing
10m Wind Speed
2m Temperature
10m Wind Speed
2m Temperature
10m Wind Speed
2m Temperature
Past Observations
Introduction Methods Results Summary Future work
Multivariate regression
MacLeod’s methodology
Forecasts
11

## Slide 21
How can we get a prediction of the capacity factor with a multivariate regression?
Past observations of CF , WS and T are fitted to a multivariate regression and the coefficients A, B and C are obtained.
CF (WS,T) = A WS + B T + C
Predictions of WS and T in the target period are introduced in the expression with the coefficients A, B, C and the output is the forecast of the capacity factor.
Introduction Methods Results Summary Future work
Multivariate regression
1
2
13

## Slide 22
Forecast of capacity factor for December 2012
Introduction Methods Results Summary Future work
Past observations of CF.
December (1981-2011)
Multivariate regression
Forecasts of WS
and T. Simple bias correction.
December (2012)
1
2
Central US
region
13

## Slide 23
Bias correction
Simple method
: forecast
: climatology of the ensemble mean
: standard deviation of the reference
: standard deviation of the ensemble mean
: climatology of the reference
Calibration
Inflation method
: ensemble mean of the forecast
:difference of the ensemble member with the ensemble mean
: correlation between the ensemble mean and the reference
: standard deviation of the reference
: standard deviation of the ensemble mean : standard deviation of the anomalies of all ensemble members calculated with respect to corresponding (i.e., same start date and lead time) the ensemble mean.
Both methods are applied in ‘One-year out cross-validated’ mode
Introduction Methods Results Summary Future work

## Slide 24
Power output curve from technical turbine specifications: Vestas 2.0 MW
CF (%)
Capacity Factor
p : surface pressure
R : ideal gas constant
T: temperature
v : wind speed
A : area of turbine perpendicular to wind direction
: wind speed at vertical height
: wind speed at a reference height
: empirically derived constant ( for dry air over land at neutral stability conditions)
Ideal gas law
Assumptions
Estimation of observational Capacity Factor
Introduction Methods Results Summary Future work

## Slide 25
Impact Surfaces
What is an impact surface?
They are a tool to visualise an impact variable in a discretized ‘climate space’ (Dave MacLeod, Oxford University).
How can we get a prediction of the capacity factor from them?
Past observations of CF , WS and T are discretized and represented in an impact surface.
Predictions in the target period of WS and T are discretized and represented in an impact surface.
Each box of the two impact surfaces are combined to provide the capacity factor prediction.
Introduction Methods Results Summary Future work
1
2
3

## Slide 26
Simple bias correction.
WS and T bias corrected forecasts.
December (2012)
Forecast of capacity factor for December 2012
N/A values !!!
Introduction Methods Results Summary Future work
Impact Surfaces
Past observations of CF.
December (1981-2011)
1
2
3
Central US
region